## Slide 1: Security, Roaming and Utilities Enhancements in Wi-Fi 5 VR2.0 Firmware
Product Introduction Session
Zoltan Fekete
15 February 2024, v02
2024 MTSC Product Session
Field Application Engineer

## Slide 2: Agenda
Moxa Wi-Fi Portfolio Including AWK Wi-Fi 5 Devices (Refresher)
VR2.0 Scope, Introduction and Features
VR2.0 Security Enhancements
VR2.0 Roaming Enhancements
VR2.0 Services and Utilities
VR2.0 Demo

## Slide 3: AWK Series Portfolio Update
 | Current IEEE 802.11n AWK Series | Next Generation IEEE 802.11ac AWK Series
3000/4000 Series Advanced AP/Bridge/Client |  | 
1000 Series Value AP Pure Client |  | 
AWK-3131A
2x2 11n single radio, indoor
AWK-4131A
2x2 11n single radio, outdoor
AWK-3252A
2x2 11ac dual radio, indoor
AWK-4252A
2x2 11ac dual radio, outdoor
AWK-1151C
2x2 11ac single radio, indoor
AWK-1131A
2x2 11n single radio, indoor
AWK-1137C
2x2 11n single radio, indoor
VR2.0
Notes: Classic 11n (Wi-Fi 4) portfolio
1000 series: value products: AP and client
3000/4000 series: Advanced products: indoor and outdoor AP/bridge/client
New 11ac (Wi-Fi 5) portfolio
In value series: Client only
Advanced products: Indoor/outdoor AP/bridge/client
Scope of VR – Wi-Fi 5 products

## Slide 4: AWK-3252A Series
802.11ac WLAN AP/Bridge/Client
Industrial
EMS/EMI
EN 61000-6-2/
EN 61000-6-4
IP30
Configurable universal model
NAT for easy machine integration
Full function CLI
Flexible Installation options
802.11ac wave 2
2.4/5GHz dual-band concurrent up to 1,300 Mb/s
HIGH PERFORMANCE
Built-in band pass filter
for stable wireless connection
Antenna isolation
Turbo Roaming
Latest WPA3 encryption
Dual image backup
MORE RELIABLE
EASY-TO-USE
2 GbE LAN, 1 PoE+(RJ45)
2.4GHz/5GHz concurrent
Antenna Connector
USB
Dual Power
DIDO
Relay
Console
(RJ45)
Dimensions: 130 * 100 * 45 mm
DIN-rail Mount
(Wall / Ceiling Options)
90° 2-sided
LED indicator
Notes: Refresh our memories
Indoor model
- new 11ac wave model
- dual radio, AP can communicate on both 2.4 and 5 GHz concurrently
- 2-way MIMO
- AP combined raw data rate up to 1.3 Gbps
- Two models: US model and rest of the world
- NAT/routing functions to interface easily e.g. in machines, AGVs
- full command line interface
- supports popular Turbo Roaming,
- latest WPA3 encryption
- bandpass filter – no interference from e.g. LTE/5G

## Slide 5: AWK-4252A Series
Configurable universal model
NAT for easy machine integration
Full function CLI
Flexible Installation options
802.11ac wave 2
2.4/5GHz dual-band concurrent up to 1,300 Mb/s
HIGH PERFORMANCE
Built-in band pass filter
for stable wireless connection
Enhanced Antenna isolation
IP68 housing salt spray tested
Turbo Roaming
Latest WPA3 encryption
Dual image backup
MORE RELIABLE
802.11ac WLAN AP/Bridge/Client
EASY-TO-USE
Dimensions: 244 * 157.6 * 66.5 mm
Industrial
EMS/EMI
EN 61000-6-2/
EN 61000-6-4
IP68
2 GbE LAN, 1 PoE+(RJ45)
2.4GHz/5GHz concurrent
Antenna Connector
USB
Dual Power
Console
(RJ45)
Wall Mount
(DIN / Pole Options)
DIDO
Relay
Antenna Signal
ESD: 30 kV
Surge: 6kV
Notes: Very similar to 3252A, but outdoor version
- Ingress protection: IP68 criteria used: 1 m under water; duration 2 hrs
- strong antenna isolation to ESD 30 kV, Surge 6 kV

## Slide 6: AWK-1151C Series
802.11ac WLAN Client
Industrial
EMS/EMI
EN 61000-6-2/
EN 61000-6-4
IP30
Configurable universal model
NAT for easy machine integration
Full function CLI
Flexible Installation options
802.11ac wave 2
2.4/5GHz dual-band Selectable up to 867 Mb/s
HIGH PERFORMANCE
Built-in band pass filter
for stable wireless connection
Antenna isolation
Turbo Roaming
Latest WPA3 encryption
Dual image backup
MORE RELIABLE
EASY-TO-USE
1 GbE LAN (RJ45)
2.4GHz/ 5GHz Selectable
Antenna Connector
USB
Console
(RJ45)
Dimensions: 130 * 100 * 22 mm
DIN-rail Mount (Wall Options)
90° 2-sided
LED indicator
DC Power
Notes: This is indoor client
Single radio
Client is always single radio – up to 867 Mbps
Very compact size

## Slide 7: AP/Master Mode
AP/Master Mode: Concurrent 2.4 GHz + 5 GHz SSIDs
Master mode: Concurrent support AP mode
Each SSID has its own Transmission rate settings
2.4GHz
5GHz
Master
AP
Slave
Client
Notes: AP or Master Mode
Master/Slave: MAC address transparent
Support for multiple SSIDs, with own transmission rate settings
WDS (wireless distribution system) not supported, no repeater mode

## Slide 8: Client/Slave/Client-Router mode
Channel Plan to choose scanning channels
Scan 2.4 GHz + 5 GHz channels at the same time
5GHz
2.4GHz
Scan 5GHz + 2.4GHz
Notes: Client, Slave or Client-Router mode
Client router mode adds additional flexibility
Channel plan makes turbo roaming more effective – list used channels, can be mixture of 2.4 and 5 GHz

## Slide 9: Turbo Roaming
Channel Plan
  All 5 GHz + 2.4 GHz channels can be selected as roaming scanning channel
  More channels = longer scanning time before roaming
    Scanning time: 150 ms / channel
    During scanning time → 2/3 throughput
    Scanning time is before roaming → more channels won’t affect roaming time (150 ms)
Notes: Turbo Roaming
Channel plan improves efficiency
- More channels to scan – scan time longer  device may react to rapidly dropping Rx signal slower
- Channel scanning takes CPU resources  affects bandwidth
Scanning time <> roaming time

## Slide 10: Recap
New AWK-series: AWK-3252A / AWK-4252A / AWK-1151C
  802.11ac wave 2 and WPA3
  Auto save
  UN model: Configure WiFi country code yourself
  AP & Master: Concurrent 5GHz (867 Mbps) + 2.4 GHz (400 Mbps)
  Client Mode & Turbo Roaming: Scan 5GHz + 2.4 GHz channels with channel plan
  Comparison:
 | AWK-3252A | AWK-4252A | AWK-1151C
Client / Slave | V | V | V
AP / Master | V | V | X
Antenna | R-SMA type | N type | R-SMA type
PoE | 802.3at | 802.3at | X
Ingress Protection | IP30 | IP68 | IP30

## Slide 11: Raw Data Rate Tables vs. Real Data Rates
Actual Data Rates
Packet size: 1518 bytes
Packet size: 64 bytes
Raw Data Rates
Notes: Manage expectations cleverly
Advertised rates are maximum, raw data rates
If radio conditions not ideal a ‘slower’ coding scheme is used
Raw data rate is decreased by forward error correction – at best 5 bytes in – 6 bytes on radio interface (Coding 5/6)
Further decreased by radio header, Layer 2 header, small packet size…
TCP/UDP rates are even lower…. (IP header, TCP overhead, etc)

## Slide 12: Agenda
Moxa Wi-Fi Portfolio Including AWK Wi-Fi 5 Devices (Refresher)
VR2.0 Scope, Introduction and Features
VR2.0 Security Enhancements
VR2.0 Roaming Enhancements
VR2.0 Services and Utilities
VR2.0 Demo
Notes: Introducing the VR2.0 features

## Slide 13: VR2.0 New Features Summary
Security Features | Roaming Enhancements | Services & Utilities
Password Policy | Client-based Turbo Roaming Enhancements | DHCP Server
Wi-Fi ACL | AP-based Disconnection | RADIUS User-account Authentication
Manual Client Disconnect (initiated from AP) |  | RADIUS User-account Privileges
Manual Client Disconnect (initiated from Client) |  | Multi-Language Support
Client Isolation (within SSID) |  | MXview One / MXview Wireless 1.1.0 Support
Client Isolation (within Subnet) |  | Turbo Roaming Analyser 2.0 Support
Trusted Access |  | LAN-ports Disabled during Boot-up
Certificate Management |  | Adjustable MTU-size
Renew Device Unique Key |  | 
Re-generate SSH Key |  | 
Security Status & Warning |  | 
Notes: 3 main categories
- Lots of focus on security
- Roaming enhancements
- Increasing usability by providing new services and utilities

## Slide 14: Next Generation AWK Series Feature Highlights
Background Colours:
White: Original VR1.x Feature
Green: VR2.0 New Feature
Notes: This is a table for reference.
Green ones are new or enhanced in VR2.0

## Slide 15: Next Generation AWK Series VR 2.0 Release Notes
https://www.moxa.com/Moxa/media/PDIM/COMMON/moxa-awk-1151c-3252a-4252a-series-firmware-v2.0.rom_Software%20Release%20History.pdf
Notes: Release notes is a good source of information

## Slide 16: Wi-Fi 5 AWK Series 2023 SW Milestones
2023 Feb
2023 April
…
2024 Q3
2023 Q1
V1.1
V2.0
V3.0
Product Launch
VR Release
AWK-3252A
2x2 11ac dual radio, indoor
AWK-4252A
2x2 11ac dual radio, outdoor
AWK-1151C
2x2 11ac single radio, indoor
Notes: Product Launch was about a year ago (we had trial products in 2022). Product was launched with VR 1.1
VR2.0 is not the latest, available for more than 6 months, but it is important, full of new features.
Knowledge required for MTSC troubleshooting
VR3.0 content not finalised.
- probably less new features
- TLS v1.3 support

## Slide 17: Agenda
Moxa Wi-Fi Portfolio Including AWK Wi-Fi 5 Devices (Refresher)
VR2.0 Scope, Introduction and Features
VR2.0 Security Enhancements
VR2.0 Roaming Enhancements
VR2.0 Services and Utilities
VR2.0 Demo
Notes: Most of them mandatory for IEC-62443-4-2 certification

## Slide 18: Password Policy
More password policy rules
Minimum length: 8 characters (versus 4 characters in VR1.1 and earlier)
Force to change Password after Upgrading to V2.0
VR1.1
VR2.0
Notes: Password policy
Usual suspects:
- minimum length 8 characters  no more moxa as password. Moxamoxa would still work
- can define complex passwords (capitals, numbers, special characters)
- forces a password change after upgrade to VR2.0

## Slide 19: Wi-Fi Access Control List
AP / Master
  Automatic Wi-Fi ACL
    Add Client to Block list if number of authentication failures exceed retry threshold
  Static Wi-Fi ACL
    Accept or Block list
Client / Slave / Client-Router
  Static Wi-Fi ACL
    Accept or Block list
Notes: Wi-fi ACL controls, which clients can connect and which one not.
Static is simpler: define list of client MAC addresses
- can be a white list, or Accept list: defined MACs are allowed, and only those
- or a blacklist, or Block list: only those specified are NOT allowed
On Access points list controls the clients that can connect
On Clients it controls to which access points the client can connect
On access point automatic ACL is also available
- initially all clients are allowed
- if a client fails authentication a predefined number of times, it will get on the automatic block list  rogue client cannot try indefinitely to connect.

## Slide 20: Wi-Fi ACL Accept and Block Lists
Manual Unblock Client blocked by Automatic ACL Control Mechanism
Maximum Number of Entries for Accepted and Blocked Lists
  Static list: 200 entries
  Automatic + Static lists: 1024 entries in total
Notes: If a client blocked automatically  manual unblock possible
Static list (accept or block) can be of max 200 entries
The total entries of automatic + static lists are limited to 1024  so to get around automatic blocking intruder may need to bring (or simulate) up to 1024 clients 

## Slide 21: AP & Master Modes: Manually Disconnect Client
Disconnect Clients from Associated Client List
Able to add client to Wi-Fi ACL blocked list
Notes: Manual client disconnection on APs or Masters  managing clients on an AP
When client associated with AP:
- shows up on client list
- can be selected for disconnection
- in the pop-up window possible to add to blocked client ACL list

## Slide 22: Client, Slave & Client-Router Modes: Manually Disconnect from AP
Manually Disconnect Client from AP on Wi-Fi Connections Page
Notes: Disconnection also possible from Client side
From Wireless Settings  Wi-Fi Connections page
Select icon next to current BSSID

## Slide 23: AP & Master Modes: Client Isolation
Notes: Client isolation is for managing security on AP side: which clients can talk to each other
- by default no communication is prevented between clients
- isolation within same SSID
- isolation within same subnet

## Slide 24: AP / Master Mode: Client Isolation within the Same SSID
Isolated within the same SSID (VAP = SSID + RF)
SSID | RF (5GHz/ 2.4GHz) | AP | Communicate? | Example
Same | Same | Same | X | Client 2
Same | Different | Same | V | Client 3
Same | Same | Different | V | Client 5
Same | Different | Different | V | Client 6
Different | Same or Different | Same or Different | V | Client 4
Switch
AP2
2.4GHz
SSID1
5GHz
SSID1
Client 1
Client 3
Client 4
5GHz
SSID2
Client 5
Client 2
AP1
5GHz
SSID1
2.4GHz
SSID1
Client 6
Notes: Wireless Client Isolation prevents one Wireless Client connected to an access point to communicate with another Client connected to the same access point.
It helps to prevent brute force attacks on clients' user names and passwords
Isolation is based on VAP (Virtual Access Points), not just SSID. VAP = SSID + frequency band
Look at the examples:
- if both clients are on same AP, same SSID, same frequency  cannot communicate
If anything is different, they can
- same SSID, same AP, but different band  yes
- same SSID, same frequency, but different AP  yes
- same SSID, different band or AP  yes
- different SSID and same or different band and same or different AP  yes

## Slide 25: AP & Master Modes: Client Isolation within the Same Subnet
Isolated within the same subnet
  Client can NOT communicate with devices in the same subnet, except with the gateway.
  Subnet type:
    Static: Set Subnet Mask and Gateway
    DHCP: Sniffer DHCP frame to learn Subnet and Gateway
  Allowed Subnet (from LAN or other VAP)
    Allow exceptional communications inside the subnet
    The allowed subnet refers to devices out of the VAP. (2 Clients under the same VAP cannot communicate with each other even if we set allowed subnets.)
Notes: Isolation within the same subnet means, that clients on the same subnet (even if on different access points) cannot communicate to each other, except with the gateway on the subnet.
There could be exceptions: these should be defined on allowed subnet list.
- communication is possible on those explicitly defined allowed subnet from outside of the VAP (other access point, or other frequency, or from LAN)
- within same VAP communication on same subnet is not possible, even if defined on allowed subnet list

## Slide 26: AP & Master Mode: Client Isolation within the Same Subnet
AP
Client 1
Client 3
Client 2
2.4GHz
SSID1
5GHz
SSID1
192.168.127.3
192.168.127.2
192.168.127.1
192.168.127.4
Client 4
Device 1
192.168.127.7
Device 2
192.168.127.8
192.168.127.254
Gateway
Switch
In Allowed Subnet | SSID | RF (5GHz/ 2.4GHz) | Communicate? | Example
NO | Same or Different | Same or Different | X | Client 4
YES | Same | Same | X | Client 2
YES | Same | Different | V | Client 3
YES | Different | Same | V | Client 5
YES | Different | Different | V | Client 6
YES | Devices from LAN |  | V | Device 2
Client 5
5GHz
SSID2
2.4GHz
SSID2
192.168.127.6
Client 6
192.168.127.5
Notes: This example shows the client isolation within the same subnet in practice.
Look the communication from (orange) Client 1 pont of view, which is connected to SSID1 on 5GHz.
- Client 2 is on the allowed subnet list, but on the same VAP (SSID1, 5GHz)  cannot communicate
- Client 3 is on the allowed subnet list, on different VAP (same SSID, but different band)  ok
- Client 4 is not on the allowed list  no communications
- Client 5 is on the allowed subnet list, different SSID, same frequency, so different VAP  ok
- Client 6 is on the allowed subnet list, different SSID and different band  ok
- Client 7 is not on the allowed list, coming from the LAN  no connection
- Client 8 is on the allowed subnet list, it on LAN  ok

## Slide 27: Trusted Access
Trusted Access applies to the following interfaces, databases, and services:
HTTP/HTTPS, SSH/Telnet, SNMP, New Moxa Command.
Syslog, Email notification, SNMP Inform.
DHCP Server, Wi-Fi Sniffer, Mirroring with Remote Type.
DHCP Client, NTP Client, TFTP/SFTP Client to upload/download files.
LLDP, Ping, RADIUS server for Wi-Fi WPA Enterprise.
Layer 2
Layer 3
Notes: In order to prevent the DoS attack, Trusted Access allows the management of which IP or MAC are able to access this device. (IEC-62443: CR 5.3, CR 7.1)
Layer 2: MAC address
Layer 3: IP address
Be careful, a lot of interfaces are affected!!! Trusted access typically affects all incoming connections
- HTTP/HTTPS, SSH, Telnet, SNMP are clear, all are bi-directional communications and because incoming messages are dropped when coming from not trusted source, they do not work
- New Moxa Command is the mechanism allowing broadcast search and implement commands from management tools like Mxconfig. The legacy Moxa Command used ports 4000/4001 for both search and command. The New Moxa command uses port 40404 for search and HTTPS port for command.
- SMTP mail is affected
- Syslog is only affected if TLS security is used, it is then bidirectional. RSSI reporting for TRA is similar.
- SNMP trap is one-way with UDP and not affected unless encryption is set up with v3. SNMP Informs have acknowledgments and are always affected.
- Others are similar…
Always think, when setting up trusted access, what functionalities might be affected and need to be taken care of (e.g. mail server, NMS server, DHCP server addresses, etc)

## Slide 28: TLS Connections and Certificates
Secure Connections with Certificate
TCP Server (Client authenticates AWK)
  HTTPS, Wi-Fi Sniffer/Mirroring
TCP Client (AWK authenticates server)
  Email Notification
TCP Client (Mutual authentication between AWK and server)
  Wi-Fi Client(EAP-TLS), Syslog Server, RSSI Report
Device Data (Signed and Encrypted)
  Configuration backup, One Key Info, Data Collection, Event Log Backup, Diagnostic Support, Wi-Fi Mirroring Data Download, Ping Data Download
TCP Client
TCP Server
Connect
Connect
AWK’s Certificate
Server’s Certificate
TCP Server
Connect
Server’s Certificate
AWK’s Certificate
…
…
…
Download data
Singed
Encrypted
Notes: Slides shows were certificates are used
- incoming TCP connections – like web gui
- outgoing TCP connections – sending mail
- outgoing connection with mutual authentication, typically when TLS is used
- device data
* signatures: can be checked if subsequently has changed (e.g. log file) – if signature is invalid, may not be loadable to device
* encryption: not readable

## Slide 29: Certificate Management: AWK’s Certificate
Regenerate Self-signed certificate and key
Upload Certificate and key
  Certificate (.pem, .crt, .der) + Key File (.key)
  Certificate with Key (.pem, .pfx, .p12) (.pfx and .p12: password is necessary)
Export device’s certification signing request (.csr)
Notes: Certificate management has the following functionalities:
- re-generate self-signed certificate and key increases security if periodically done.
- upload external and trusted certificates and keys to the device
* formats:…
- create a signing request to have a proper certificate signed by a trusted authority

## Slide 30: Certificate Management: Server CA Certificate
Upload Server CA Certificate (.pem, .crt, .der)
Notes: Certificate Authorities certificates are needed to be able to be uploaded to the device

## Slide 31: Renew Device Unique Key
Device’s (built-in) Unique Key is used to encrypt:
  Configuration
  Certification
  Encryption/decryption Keys
Renew Unique Key  to improve security
  Takes ~15s, then device reboots
  Generates new unique key
  Decrypts all the files with old unique key
  ReEncrypts with new unique key
Notes: This key is generated by the device itself without reliance on components that may be outside of the device’s security zone. (IEC-62443: NDR 3.13)
Used for encrypting files
Renewing takes time
- new key is generated by proper algorithm
- all certificates, encrypted files decrypted with old key
- encrypted again with new one

## Slide 32: SSH Key
Regenerate SSH Key
  Current connection will still use the old key
Notes: SSH key renewal is also a manually triggered automatic process.
Current active SSH session will use old key

## Slide 33: Security Status
Overview the security risks by risk levels
Review tool to ensure that device’s configuration meets IEC-62443-4-2 various Security Levels:
  HIGH: It has casual or coincidental violation (related to IEC-62443 Level 1)
  MEDIUM: It has intentional violation using simple means with low resources, generic skills and low motivation. (related to IEC-62443 Level 2)
  LOW: It has intentional violation using sophisticated means with moderate resources, IACS specific skills and moderate/high motivation (related to part of IEC-62443 Level 3/4)
Notes: AWK does internal audits on settings according to IEC-62443-4-2
Violations are shown in 3 categories
- red L1
- orange L2
- yellow L3/4

## Slide 34: Security Status and Warnings (1/4)
Feature Group | Security Risk Description | Risk Level | NOTE
User Interface | The device can be accessed through the unsecure HTTP interface. | HIGH | 
User Interface | The HTTPS certificate is self-signed. | LOW | Issue to = Issue by
User Interface | The device can be accessed through the unsecure Telnet interface. | HIGH | 
User Interface | The device can be accessed through the unsecure SNMP V1/V2c interface. | HIGH | 
User Interface | SNMP V3 is enabled without authentication and encryption. | HIGH | 
User Interface | SNMP V3 is enabled with weak security. | HIGH | Secured condition: One of enabled SNMP Accounts use SHA-256, SHA-384, or SHA-512 as authentication and use AES as encryption.
Notes: These pages are for reference.. Full listing in handout material…

## Slide 35: Security Status and Warnings (2/4)
Feature Group | Security Risk Description | Risk Level | NOTE
Event Logs and Notifications | Syslog server is enabled without security. | HIGH | 
Event Logs and Notifications | Syslog is disabled or not configured to support redundant event log backups. | MEDIUM | Syslog should be enabled and at least one of the Syslog server is enabled.
Event Logs and Notifications | Email notifications are enabled without security. | HIGH | 
Event Logs and Notifications | Email notifications are enabled with encryption, but without authentication. | MEDIUM | 
Event Logs and Notifications | The unsecure SNMP Trap/Inform V1/V2c is enabled. | HIGH | Trap/Inform should be set to V3
Event Logs and Notifications | SNMP Trap/Inform V3 is enabled without authentication and encryption. | HIGH | 
Event Logs and Notifications | SNMP Trap/Inform V3 is enabled with weak security. | HIGH | Secured condition: One of enabled SNMP Trap/Inform Accounts use SHA-256, SHA-384, or SHA-512 as authentication and use AES as encryption.

## Slide 36: Security Status and Warnings (3/4)
Feature Group | Security Risk Description | Risk Level | NOTE
System | LLDP is enabled and is advertising the device's and identity and capabilities to its neighbors. | MEDIUM | 
System | The device IP is assigned through the unsecure DHCP. | HIGH | One of the following condition is satisfied: Operation Mode = Client-Router AND IP Mode of WAN = Static Operation Mode != Client-Router AND IP Mode of LAN = Static
System | The device time is configured through the unsecure NTP. | HIGH | Clock Source = Internal Clock
System | Remote server IPs are obtained through the unsecure DNS protocol. | HIGH | One of the following condition is satisfied: Operation Mode = Client-Router AND DNS Server 1 of WAN == NULL AND DNS Server 2 of WAN == NULL Operation Mode != Client-Router AND DNS Server 1 of LAN == NULL AND DNS Server 2 of LAN == NULL
System | Users are able to access the device via the USB interface. | MEDIUM | 
System | Automatic event log backup is enabled without signatures. | MEDIUM | Secured options: Disable Automatic event log backup Enable Automatic event log backup with signature
System | Automatic configuration backup is enabled without signatures. | MEDIUM | Secured options: Disable Automatic configuration backup Enable Automatic configuration backup with signature
System | Automatic configuration restore is enabled without signatures. | MEDIUM | Secured options: Disable Automatic configuration restore Enable Automatic configuration restore with signature
System | Trusted Access is disabled and cannot prevent unwanted access. | LOW | 
System | Password complexity is disabled and may make the device vulnerable to malicious users. | LOW | Enable one of password complexity strength check.

## Slide 37: Security Status and Warnings (4/4)
Feature Group | Security Risk Description | Risk Level | NOTE
Service | The unsecure DHCP server is enabled and may lease IP addresses to incorrect devices. | HIGH | Disable DHCP Server
Network | Other devices are able to transfer plaintext data over Wi-Fi interfaces with OPEN security. | HIGH | 
Network | The device is allowed to use a non-secure protocol to receive captured frames over the Wi-Fi interface. | HIGH | Sniffer or Remote Wi-Fi mirroring should enable TLS
Network | Wi-Fi ACL is disabled and cannot prevent unwanted Wi-Fi access. | LOW | AP-based mode Enable Static or Auto Wi-Fi ACL Client-baded mode Enable Staic Wi-Fi ACL
Network | VLAN is not enabled to perform network segmentation. | LOW | At least 2 VLAN ID should enabled and applied.
Network | Firewall is disabled and cannot restrict network access. | LOW | 
Network | RSSI reports are sent over a non-secure protocol. | HIGH | If RSSI is enabled, TLS should be enabled.

## Slide 38: Agenda
Moxa Wi-Fi Portfolio Including AWK Wi-Fi 5 Devices (Refresher)
VR2.0 Scope, Introduction and Features
VR2.0 Security Enhancements
VR2.0 Roaming Enhancements
VR2.0 Services and Utilities
VR2.0 Demo

## Slide 39: Client-based Turbo Roaming Enhancements
Supports Turbo Roaming in Slave mode
Supports Turbo Roaming with WPA3
  [Limitation] WPA3 takes additional 200 ms to generate key than compared to WPA2. So client takes 150ms + 200 ms = 350 ms to roam to the next AP in the following conditions only:
    the 1st time connection establishment to AP
    AP renews its key every 12 hours
Support RSSI Report to Turbo Roaming Analyzer v2.0
  AP sends management frame every 100 ms
  Default RSSI Reporting interval: 50 ms ( RSSI reporting interval was fixed to 2 ms in 802.11n AWK Series)
  Support TLS for security
Notes: Turbo Roaming was of course available already when product was released.
These are some important enhancements
- support TR in slave mode (not only in client)
- support TR with WPA encryption
 increases roaming time to 350msec practically once every 12 hours, when keys regenerated. All other roaming cases are 150 msec
- RSSI reporting for TRA v2.0
* default reporting interval 50 msec
* TLS security option

## Slide 40: AP-Based Client Disconnection
For Non-MOXA Clients which do not have roaming capability
Forces clients to disconnect so they can connect to AP with better SNR.
Mechanism:
  AP checks client’s SNR / Signal Strength every second.
  If SNR / Signal Strength is below threshold for set consecutive times (Attempts) → AP disconnects Client (DISASSOC)
  If AP does not receive data frames from client over 10 seconds → AP disconnects Client (DISASSOC)
Limitation
  Please ensure that client sends frames to AP every second, so AP can get the latest SNR / Signal Strength from client.
Notes: Turbo roaming is only available on moxa clients.
AP based client disconnection is to improve 3rd party client roaming
- otherwise roaming is slow, only when connection is lost
Solution:
- AP checks client SNR/RSSI once per second
- if below threshold  AP Disassoc
- if client does not send data for 10 sec  AP Disassoc
- client must send frame every second (e.g. ping)

## Slide 41: Agenda
Moxa Wi-Fi Portfolio Including AWK Wi-Fi 5 Devices (Refresher)
VR2.0 Scope, Introduction and Features
VR2.0 Security Enhancements
VR2.0 Roaming Enhancements
VR2.0 Services and Utilities
VR2.0 Demo

## Slide 42: DHCP Server
Available in AP, Master and Client Router modes
  Definable DHCP Range for automatic IP assignments
  MAC-Based IP assignment (‘static’ IP addresses) option
Limitation
  In AP and Master modes, DHCP Server is available only if LAN interface has static IP address (not DHCP).
Notes: DHCP server
- quite typical solution
- for AP, master and client router modes
- statically assigned MAC addresses possible
For AP/Master mode LAN has to have static address

## Slide 43: RADIUS User Account Authentication
Use RADIUS server to centralize the user account management
If Diagnostic Account is used, user can log in without RADIUS server authentication.
Mechanisms
User Log in
Can reach 1st server?
Can reach 2nd server?
Yes
No
Authenticate and authorize user account locally
No
Authenticate and authorize user account
Yes
Notes: RADIUS may be used for two different purposes in AWK.
This is for User Authentication.
Not to be mixed with RADIUS based Wi-Fi client authentication.
Supports 2 RADIUS servers
Supports number of authentication types
If diagnostic account exists  works without RADIUS authentication

## Slide 44: RADIUS User Account Privileges
Feature Group | Admin Level | Engineer Level | User Level | Custom
Account System | O | X | X | ---
Advanced Diagnostics | O | O | X | ---
Auditor System | O | O | X | ---
Diagnostics | O | O | O | ---
Network Configuration | O | O | X | ---
Status Monitoring | O | O | O | ---
System Backup | O | X | X | ---
System Management | O | O | X | ---
RADIUS defines User Levels: Administrator, Engineer, User, Custom.
AWK Functionalities require certain Authority Level
Mapping between User Levels and Authorities are in below table
Details of authority required for each functionality is in AWK Manual, Appendix D
Notes: This is again a reference slides.
4 RADIUS user levels
- Admin, Engineer, User, Custom
- AWK functionalities are mapped to 3 standard levels

## Slide 45: Multi-Language Support
Besides English Japanese, Chinese (Simplified) and Chinese (Traditional) languages are supported
Language selection is only available on Web-GUI. CLI and logs are always in English.
Notes: Multi-language support
In Europe pretty much English is relevant.
But worldwide support for Japanese and Chinese is important.

## Slide 46: MXview One Support – Test Network
MXview One Server
192.168.127.5
Switch
MDS-G4012
192.168.127.246
AP2
AWK-3131
192.168.127.247
AP1
AWK-3252A
192.168.127.249
Client
AWK-3252A
192.168.127.248
Client PC
192.168.127.2
Notes: AWK now supports Mxview One.
Note: no support for legacy Mxview
Picture: test network, we use in our demo as well: 2 APs connected to a switch, one client connected to a remote computer. Mxview One manages all the devices.

## Slide 47: Others
Support for Configuration Tools:
  Mxconfig v3.1.10
LAN Interface related Features:
  LAN Ports disabled during bootup process.
  Adjustable MTU size on LAN interface
    Make sure that LAN and Wi-Fi side have matching settings
Same value
Notes: For configuration management there is support for latest version of Mxconfig 3.x (non-java)
Some other new behaviour related to wired ports
- LAN ports disabled during boot-up
- Adjustable MTU size – making sure that LAN and Wi-fi sides are in sync

## Slide 48: VR2.0 New Features Re-cap
Security Features | Roaming Enhancements | Services & Utilities
Password Policy | Client-based Turbo Roaming Enhancements | DHCP Server
Wi-Fi ACL | AP-based Disconnection | RADIUS User-account Authentication
Manual Client Disconnect (initiated from AP) |  | Multi-Language Support
Manual Client Disconnect (initiated from Client) |  | MXview One / MXview Wireless 1.1.0 Support
Client Isolation (within SSID) |  | Turbo Roaming Analyser 2.0 Support
Client Isolation (within Subnet) |  | LAN-ports Disabled during Boot-up
Trusted Access |  | 
TLS Connection and Certificate |  | 
Certificate Management |  | 
Renew Device Unique Key |  | 
Re-generate SSH Key |  | 
Security Status & Warning |  | 
Notes: Let’s summarise all the features at the end, before the demo.
- Security features
- Roaming enhancements
- Services and Utilities.

## Slide 49: Agenda
Moxa Wi-Fi Portfolio Including AWK Wi-Fi 5 Devices (Refresher)
VR2.0 Scope, Introduction and Features
VR2.0 Security Enhancements
VR2.0 Roaming Enhancements
VR2.0 Services and Utilities
VR2.0 Demo

## Slide 50: VR2.0 Feature Demo
Security Status (Ahmed)
Turbo Roaming Analyser (Ahmed)
Mxview One (Zoltan)
Mxview One with Wireless add-on (Zoltan)

## Slide 51: RSSI Reporting From Device
Client MAC Address
BSSID
SNR
Noise Floor
RSSI = Noise Floor + SNR

## Slide 52: Turbo Roaming Analyser

## Slide 53: Turbo Roaming Analyser

## Slide 54: MXview One Support – Test Network

## Slide 55: MXview One with Wireless Add-On
Device Summary Page
Displays Access Points
Shows associated Clients for each AP
  Including IP Address
  MAC address
  RSSI
  Noise Floor
  (SNR can be calculated)
Roam

## Slide 56: MXview One with Wireless Add-On
Wireless Roaming Playback
Variable speed replay of roaming events
Serving access point always visible
Timestamp and RSSI
Roaming points marked on timeline

## Slide 58: Backup

## Slide 59: AWK Series Naming Convention
AWK-3252A
Advanced Indoor
2x2 11ac dual radio
2x GbE LAN
AP
AWK-4252A
Advanced Outdoor
2x2 11ac dual radio
2x GbE LAN
AP
AWK-1151C
Value
2x2 11ac single radio
2x GbE LAN
Client

## Slide 60: Next Gen. AWK Series Regulatory Approvals
Differences Highlighted
Notes: Note here the specific VM approvals
ATEX C1D2
E1

## Slide 61: RADIUS User Levels and Authorities
Details

## Slide 62: RADIUS User Account Privilege
User Level | Service-Type (6) | Management-Privilege-Level (136) | Vendor-Specific (26)
Administrator | Administrative (6) | --- | ---
Engineer | NAS Prompt (7) | 2 | ---
User | NAS Prompt (7) | 1 | ---
Custom | NAS Prompt (7) | 0 | Defined in the next page
Feature Group | Admin Level | Engineer Level | User Level | Custom
Account System | O | X | X | ---
Advanced Diagnostics | O | O | X | ---
Auditor System | O | O | X | ---
Diagnostics | O | O | O | ---
Network | O | O | X | ---
Status Monitoring | O | O | O | ---
System Backup | O | X | X | ---
System Management | O | O | X | ---
RADIUS attributes to authorize user account privilege

## Slide 63: RADIUS User Account Privilege
Byte | 0 Byte | 1 | 2 | 3 | 4 | 5 | 6 | 7 | ...
Description | Type | Length | Vendor-ID |  |  |  | Vendor-Type | Vendor-Length | Vendor-Value
Value | Vendor-Specific (26) | *** | moxa (8691) |  |  |  | Defined in the following table. |  | 
Vendor Type | Vendor Length | Vendor Value
Product series (0x00) | 4 = 1 (type) + 1 (length) + 2 (value) | industrialWirelessLan (0x000F = 15)
Account System (0x11) NOT support because custom user shall not have account system authority. (IEC-62443) | 3 = 1 (type) + 1 (length) + 1 (value) | 0x00: disabled 0x01: enabled
Advanced Diagnostic (0x12) |  | 
Auditor System (0x13) |  | 
Diagnostic (0x14) |  | 
Network (0x15) |  | 
Status Monitoring (0x16) |  | 
System Backup (0x17) |  | 
System Management (0x18) |  | 
User Level | Service-Type (6) | Management-Privilege-Level (136) | Vendor-Specific (26)
Custom | NAS Prompt (7) | 0 | Defined below