## Slide 1: Introducing the new x86 Industrial PC platforms: BXP, DRP and RKP Series
Stefan Czoer TS
Christian Gromeier TS
Zoltan Fekete FAE
February 2024
2024 MTSC Product

## Slide 2: Agenda
Introduction to the new Moxa DRP/BXP/RKP Series
Hardware Overview
BIOS Features
Windows Licensing and Utility Framework
Linux Distribution and SDK
Demo
  Windows Utilities and Troubleshooting
  Linux Installation and Troubleshooting
Summary

## Slide 3: Agenda
Introduction to the new Moxa DRP/BXP/RKP Series
Hardware Overview
BIOS Features
Windows Licensing and Utility Framework
Linux Distribution and SDK
Demo
  Windows Utilities and Troubleshooting
  Linux Installation and Troubleshooting
Summary

## Slide 4: How Do Customers Choose IPCs?
Which computers are easy to install (e.g. in a cabinet) without the need for additional brackets?
Form Factor
What type of devices need to connect to the computer and which interfaces are required (e.g. USB/LAN/serial ports, DIOs)?
Interface Combinations
Based on data collection and processing requirements, which CPU processor is most suitable (e.g. Intel® Atom®, Celeron®, Core™ i3/i5/i7)?
Computing Power
Which product gives the best value for the asking price?
Notes: How do customers choose Industrial PCs?
- required form factor
- what interfaces are required
- CPU requirements
- memory and disk requirement
- value for money  not paying for not required features

## Slide 5: Introduction to the new Moxa DRP/BXP/RKP Series
BXP Series
DRP Series
RKP Series
DIN-Rail Computing Platform
Box-type Computing Platform
Rackmount Computing Platform
Notes: Moxa’s New Industrial PC platform
One family – form factors:
DRP – Din Rail Computing Platform
BXP – Box Type Computing Platform
RKP – Rackmount Computing Platform
All have similar base products
There are some differences – be aware (e.g. RAID is supported only on RKP)
Various processor options
Various interface options
These are Industrial PCs for cost sensitive applications
- no extras in there (like ‘luxury’ isolated interfaces – very expensive)
- wi-fi or cellular connectivity

## Slide 6: Extension Interfaces – Variations for a Product
Notes: Base products have the CPU, the chipset around it, memory, disk and all the mandatory interfaces
Extension boards can add
- serial ports
- LAN ports
- or both
Because of large number of Serial and LAN options, these are especially useful for
- data acquisition
- protocol conversion
- sensor to cloud interface
- custom networking solutions

## Slide 7: Product Naming Conventions
DRP – C100 – C7 – 8L – T
Form
factor
Product generation
CPU
type
expansion interface
Reserve
CPU
type
Wide
temperature
DRP BXP RKP | Din Rail Computing-Platform Box type Computing-Platform Rackmount Computing-Platform
A C | A: Atom CPU C: Core CPU
1 | Product generation: 1, 2, 3……
0 | Reserve for Special-1, RKP 1U
0 | Reserve for Special-2
C7 | CPU type : E2 : Atom dual core / E4 : Atom quad core C1 : Celeron / C5 : Core i5 / C7 : Core i7
8L 6C/8C 2L4C/2L3C | 8L : Qty's of LAN Ports 6C/8C : Qty's of COM Ports 2L4C/2L3C : Qty's of LAN Ports + COM Ports
T | Wide temperature: -30°C to 60°C
Notes: Naming convention for the new Moxa DRP/BXP/RKP Computers
Altogether 75 models
- Form factor DRP, BXP or RKP (3 options)
- CPU type A for Atom CPU; C for Core CPU
- Product Generation – it is always one, first reserved digit is for RKP height in Us (now only 1U available)
- CPU Type E2: Atom dual core, E4: Atom quad core, C1: Celeron, C5: CORE i5, C7: CORE i7 (5 options)
- Expansion interface:
  - If nothing: base modesl
  - 8L: for 8 LAN ports
  - 6C or 8C for 6/8 serial ports
  - 2L4C, 2L3C for expansion interface with COM and LAN ports combinations
- T for wide temperature -30°C to 60°C

## Slide 8: Standards and Certificates
EMC | EN 55032/35
EMI | CISPR 32, FCC Part 15B Class A BSMI
EMS | IEC 61000-4-2 ESD: Contact: 4 kV; Air: 8 kV IEC 61000-4-3 RS: 80 MHz to 1 GHz: 3 V/m IEC 61000-4-4 EFT: Power: 0.5 kV; Signal: 0.5 kV IEC 61000-4-5 Surge: Power: 0.5 kV, Signal: 1 kV IEC 61000-4-6 CS: 3 V IEC 61000-4-8 PFMF: 1 A/m at 50 to 60 Hz
Safety | UL 62368-1 (CB) BSMI
Shock | IEC 60068-2-27
Vibration | IEC 60068-2-64
Notes: Product certified against:
- mandatory standards (like electrical safety EN 62368)
- those necessary in generic industrial environment:
  EMC (electromagnetic compatibility) which is divided int:, EMI (EM Interference) and EMS (EM susceptibility)
  For mechanical performance: certified for shock and vibration performance.
These products are designed based on standard and widely adopted industrial specifications, without any specific enhancements to protection features.
Not having very strict and expensive special certification (such as for substation, rail, marine or explosive environment) – makes product more cost effective

## Slide 9: Supported Operating Systems
Windows
  Windows 10 IoT Enterprise LTSC 2021 64-bit
  Windows 11 Professional 64-bit
Linux
  Debian 11 (bullseye), Linux kernel 5.10
    Official Debian 11.8 netinst ISO download link
    Official Debian installation guide
  Ubuntu 22.04.03 LTS (Jammy Jellyfish), Linux kernel 5.15
    Official Ubuntu 22.04.03 LTS desktop ISO download link
    Official Ubuntu 22.04.03 LTS server ISO download link
    Official Ubuntu installation guide
  RedHat 9, Linux kernel 5.14
    Official RedHat 9 download link
    Official RedHat 9 installation guide
Notes: Supported Operating systems
Moxa supports both popular platforms for IoT: Windows and Linux
Windows:
Windows 10 IoT Enterprise LTSC 2021 64-bit
Windows 11 Professional 64-bit
Linux:
Debian 11 (bullseye), Linux kernel 5.10
Ubuntu 22.04.03 LTS (Jammy Jellyfish), Linux kernel 5.15
RedHat 9, Linux kernel 5.14
Note: no MIL support
Standard Linux distros supported
Device drivers provided for extra interfaces

## Slide 10: Agenda
Introduction to the new Moxa DRP/BXP/RKP Series
Hardware Overview
BIOS Features
Windows Licensing and Utility Framework
Linux Distribution and SDK
Demo
  Windows Utilities and Troubleshooting
  Linux Installation and Troubleshooting
Summary

## Slide 11: Block Diagram
Base board
Expansion board
*See Note
Note: *LAN#1 is Intel i219 for C-series only, while i210 for A-series. All other LAN ports are i210
Additional
  *COM
  *LAN
  *COM+*LAN
  ports
Notes: Three form factors – more or less same block diagram
- A and C version have different CPU category and generation, different chipset
Centre of Block Diagram:
- CPU and PCH connections to DRAM
- DRAM Speed on all products are set to operate at 2400MT/s . (Megatransfers per seconds = MHz )
- HDMI and VGA interfaces also directly connected to CPU/PCH
- The VGA interface is converted from the DisplayPort.
Interfaces:
- The basic models are equipped with two 1Gb copper LAN ports. The C series LAN 1 is an Intel I219 chip , while A series has an Intel i210 network chip. All other LAN ports are i210
- equipped with a watchdog.
- operating system can be installed on SDCard, CFAST
- 2.5-inch SSD connected via SATA3 on RKP only
- SD-card
- A Super I/O chip with Digital I/Os and 2 configurable RS232 RS422 RS485 serial ports. No DIO on DRP!
Additonal interfaces on expansion board:
- additional i210 based LAN interfaces, up to 8
- additional Moxa Uport chip based serial ports, up to 8.

## Slide 12: Isolation Specs
Isolated interface
  Copper Ethernet 1.5 kV (built-in)
Non-isolated interfaces
  Power
  USB
  HDMI
  VGA
  DIO
  Serial
Notes: The BXP/DRP/RKP series products are generic industrial PCs.
- Isolation is exclusively implemented in the RJ45 Ethernet copper ports,
- No isolation on other interfaces such as power, USB, display interfaces, DIO, and serial ports.

## Slide 13: Display Interfaces
HDMI
  HDMI 2.0b
  3840x2160@60Hz (Ultra HD)
VGA
  1920x1200@60Hz
RKP Series
BXP Series
DRP Series
Notes: These series of computers support
- one HDMI 2.0b display and
- one VGA display port.
All product variants can use two display interfaces to two screens.
HDMI supports 3840x2160 at 60Hz, while VGA supports 1920x1200 at 60Hz.
The built-in display controller has HDMI and DisplayPort connections. The VGA interface is internally converted from the DisplayPort output.

## Slide 14: Digital I/O Interfaces
Digital Inputs | Digital Inputs | Digital Outputs | Digital Outputs
Connector | Spring-type Euroblock terminal |  | 
Sensor Type | Dry Contact | I/O Type | Sink type
Dry Contact | Logic 0: Short to GND Logic 1: Open | Current Rating | 200mA per channel
 |  | Output Voltage | 0 to 24VDC
RKP Series
BXP Series
Note:
No DIO on DRP Series
Notes: The digital I/O support includes both digital input and digital output.
- BXP series features 4DI/4DO,
- RKP series offers 8DI/8DO.
- Note that DXP series does not implement digital I/O.
Digital inputs can handle dry contacts
Digital output is of the sink type, with DO supporting a voltage range from 0 to 24 VDC.
More information can be found in the hardware user manual.

## Slide 15: Serial Interfaces
DB9 Male Port
PIN | RS-232 | RS-422 | RS-485(4-wire) | RS-485(2-wire)
1 | DCD | TxDA(-) | TxDA(-) | -
2 | RxD | TxDB(+) | TxDB(+) | -
3 | TxD | RxDB(+) | RxDB(+) | DataB(+)
4 | DTR | RxDA(-) | RxDA(-) | DataA(-)
5 | GND | GND | GND | GND
6 | DSR | - | - | -
7 | RTS | - | - | -
8 | CTS | - | - | -
Notes: Pinout for the serial RS-232/RS422/RS485 interface in the BXP/DRP/RKP series.
The serial connectors are DB9 male connectors
The pinout is the same as on the Moxa UPort devices

## Slide 16: USB Interfaces
USB2.0 Type A
USB3.2 Gen1 - (5Gps) Type A (also called as USB 3.0)
Number of USB Ports:
  DRP: 3 x USB 3.0
  RKP: 3 x USB 3.0
  BXP: 2 x USB 3.0 + 4 x USB 2.0
Notes: The USB interfaces in all series follows the type-A format,
Each model has both USB 2.0 and USB 3.2 Gen 1 ports.
USB 3.2 Gen1 is equivalent to original USB 3.0 and it supports speeds up to 5 Gbps.
The number of ports vary with models

## Slide 17: Interfaces not included
mPCIe
M.2 storage
Wi-Fi module
Cellular module
Notes: Please be aware, that some commonly used interfaces, such as mini PCIe, M.2 SSD storage, Wi-Fi module, and cellular module, are not supported in this series of products.
These are difficult decisions but meant to keep the product prices low.

## Slide 18: Hardware Overview: Power Consumption & Suggestion
Model Series | Model Name | CPU Info | UL Test report Power consumption(Max.) | Adapter Suggestion
BXP-C100 | BXP-C100-C1 | Intel® Celeron 6305E | 75W(12V/6.25A) | 90W Adapter 12-24V
 | BXP-C100-C5 | Intel® Core™ Processor i5-1145G7E |  | 
 | BXP-C100-C7 | Intel® Core™ Processor i7-1185G7E |  | 
BXP-A100 | BXP-A100-E2 | Intel Atom® x6211E Processor | 58.2W(12V/4.85A) | 
 | BXP-A100-E4 | Intel Atom® x6245E Processor |  | 
DRP-C100 | DRP-C100-C1 | Intel® Celeron 6305E | 68.16W(12V/5.68A) | 
 | DRP-C100-C5 | Intel® Core™ Processor i5-1145G7E |  | 
 | DRP-C100-C7 | Intel® Core™ Processor i7-1185G7E |  | 
DRP-A100 | DRP-A100-E2 | Intel Atom® x6211E Processor | 49.2W(12V/4.1A) | 
 | DRP-A100-E4 | Intel Atom® x6245E Processor |  | 
RKP-C110 | RKP-C110-C1 | Intel® Celeron 6305E | 68.7W(12V/5.725A) | 
 | RKP-C110-C5 | Intel® Core™ Processor i5-1145G7E |  | 
 | RKP-C110-C7 | Intel® Core™ Processor i7-1185G7E |  | 
RKP-A110 | RKP-A110-E2 | Intel Atom® x6211E Processor | 53.76W (12V/4.48A) | 
 | RKP-A110-E4 | Intel Atom® x6245E Processor |  | 
The DC power source rating is 12 VDC @ 6.65 A or 24 VDC @ 3.30 A
Notes: This slide shows an overview on the measured power consumption of all models released so far.
Please keep in mind, to use a power source either with 12 VDC @ 6.65 A or an Adapter with 24 VDC @ 3.30 A.
We provide Product Specification for all 6 released base models in the Reference Sections of the material.

## Slide 19: Agenda
Introduction to the new Moxa DRP/BXP/RKP Series
Hardware Overview
BIOS Features
Windows Licensing and Utility Framework
Linux Distribution and SDK
Demo
  Windows Utilities and Troubleshooting
  Linux Installation and Troubleshooting
Summary

## Slide 20: BIOS Setup Utility: Main
Model name
BIOS version
Component information
  CPU
  Memory
System Time & Date
Notes: BIOS Setup is similar to usual PCs, with some interface specific extensions.
We do not cover it in detail, manual describes the setup
Main page:
- essential information about the system hardware, including the model name, BIOS version, and CPU type.
- system date and time are presented on the Main page, and they are synchronized with the operating system.

## Slide 21: BIOS Setup Utility: Chipset Configuration
Power ON after Power Failure
  ON (default)
  OFF
  Last State
Load default after cleaning RTC Battery
  Enable(default) / Disable
DO configuration
  High (Default)
  Low
Notes: Chipset Configuration has some notable options:
Power on after Power Failure
- By default, "Power On after Power Failure" is on - computer will automatically boot up after power outage.
- It can be changed to Off, or restoring last state
"Load default after cleaning RTC Battery“
- when enabled, the system will restore default settings upon detecting RTC battery loss.
- if customers wants to prevent restoring BIOS default values when RTC battery is removed the feature can be disabled.
DO configuration:
- default digital output level can be set with this option

## Slide 22: BIOS Setup Utility : Super IO (SIO IT8786E)
UART port on main board
  Enable/Disable
  UART Mode: RS232/422/485(2W)
UART Configuration (serial ports)
Notes: Another Moxa specific BIOS extension
- UART port configuration (enable/disable and serial physical interface type) can be set - Applicable for the 2 serial ports using the Super I/O chip.
Note:
- for Serial Port 1 and Port 2 only. No preset for expansion board serial ports
- operating system driver may override the default BIOS setting
- Setting the mode in BIOS will not install the serial mode driver

## Slide 23: BIOS Boot Menu
UEFI benefits
  Enhance boot and overall computer speed
  Secure Boot functionality
USB drive support format in UEFI is FAT32
*Moxa products do not support Legacy mode on Intel 11th generation CPUs and later.
Notes: BIOS Boot Menu.
Moxa prefers to use UEFI BIOS mode over legacy mode.
Note that Legacy mode is not supported on our devices with 11th generation CPUs, i.e. the –C models
- UEFI can significantly improve boot and overall computer speed,
- especially for high-capacity hard drives on your device
- UEFI includes Secure Boot functionality,
- enhancing the security of the boot process by preventing the initiation of UEFI drivers or OS boot files lacking valid digital signatures.
- UEFI boot mode streamlines the computer boot process, resulting in faster startup speeds.
UEFI allows booting from USB
- supports only FAT32 partitions
- If your USB flash drive is not detected in the Boot Manager, please check format.

## Slide 24: BIOS Network Adapters
The network adapter chip connects to the CPU through the PCIe bus.
I219 features vPro capabilities, allowing the execution of remote connection functions using the Intel Management Engine Bios Extension (AMT)
Notes: - Intel I210 and I219 used as network adapters. They connect to the CPU through PCIe bus.
- All the LAN interfaces use i210 on the A series.
- Also all, but the first LAN interface uses i210 on the C series. Only the first LAN port uses i219
- I219 features vPro capabilities, enabling the execution of remote connection functions using the Intel Management Engine BIOS Extension (AMT).
- The AMT function is supported only in the C100 series with i5 and i7 CPUs only!

## Slide 25: RAID Configuration on RKP-C100
C5 and C7 models only
Notes: All RKP Models feature two SATA interfaces.
RKP-C100-C5 and C7 Models also support RAID level 0 and RAID level 1 with Intel Rapid Storage Technology (RST).
In order to use it
- Enable "Map SATA Root Port" within VMD,
- RST can be configured in Device Manager.

## Slide 26: Agenda
Introduction to the new Moxa DRP/BXP/RKP Series
Hardware Overview
BIOS Features
Windows Licensing and Utility Framework
Linux Distribution and SDK
Demo
  Windows Utilities and Troubleshooting
  Linux Installation and Troubleshooting
Summary

## Slide 27: Windows Licensing
Certificate of Authenticity COA (License Label)
  The COA label serves as proof of license for each individual unit, and therefore cannot be transferred to other different machines or new units.
PKEA (Product Key Application) | EPKEA (Embedded Product Key Application)
Single Activation Key (One-to-One Key) All devices have a unique individual key, printed on the license proof sticker. | Multiple Activation Key (Company Key) Each OEM signing the CLA has its own set of keys that can activate multiple devices, facilitating large-scale deployments.
Notes: Two Windows licensing methods:
- PKEA (Product Key Enty Activation) constitutes a single licensing key, whereby all devices possess a unique individual key printed on the license proof sticker
- EPKEA, or Multiple Activation Key, also recognized as Company Key, involves each OEM signing the CLA having its own set of keys capable of activating multiple devices. This streamlines large-scale deployments by enabling activation on multiple devices with a single key.
In case Windows is supplied with PKEA, one needs to scratch off the security layer from the product activation key on the license (COA, Certificate of Authenticity) and type it in manually and let the system finish the activation via the internet. The activation key can be used once for the device.
In case of ePKEA an activation key from Microsoft assigned to the CLA of the OEM, which needs to be built into the image. No manual activation and internet connection is needed. All images have the same key.
It is not clear, which Windows licensing scheme is used for DRP/BXP/RKP series.

## Slide 28: Windows Licensing
Windows version | PKEA | EPKEA
Windows 10 LTSB 2016 | V | V
Windows 10 LTSC 2019 | V | V
Windows 10 LTSC 21H2 | V | V
Windows 10 Pro | EOS | X
Windows 11 Pro | V | X
Windows Server | X | X
Notes: Here is the current list of Windows versions and supported product license keys.
- Windows 10 Embedded Long-Term Support versions support both PKEA and EPKEA licensing
- Windows 10 Pro version is now End of Life and cannot be purchased
- Windows 11 Pro is available with PKEA licensing only
- Windows Server product is not supported on DRP/BXP/RKP platform.
As told earlier – we will be able to supply more information on what can be ordered later.

## Slide 29: Windows Licensing
License activation (PKEA)
Notes: Activating a PKEA license requires internet connection
During activation Windows sends a unique ID created from the motherboard resources and CPU ID
It is recorded on the Microsoft Activation Server.
On successful registration - status changes to "Active,"
Re-installation
- if you are reinstalling the same version of Windows and connect to the network, it will automatically activate.
- if you reinstall a different version of Windows, activation will not be possible.

## Slide 30: Utilities: Moxa Serial Interface Utility
Service process:
System on → Service start → Read registry → SetUartMode
Service stop → Write uart mode to registry
Utility process:
GetUartMode: Device → API(Library) → Display on utility
SetUartMode: Utility → Write uart mode to registry → API(Library) → Device
Registry address: HKEY_LOCAL_MACHINE\SOFTWARE\MOXA\SerialInterface
Notes: Serial Interface utility is a Windows-based utility and consists of two processes:
- service process
- utility process.
Upon system boot-up:
- service process reads the recorded UART mode information from the registry.
- it uses the utility process to set the UART mode accordingly.
- When service is stopped, it updates the current UART mode into the registry.
The utility provides two main functionalities by using a device API: "get UART mode" and "set UART mode.“
- "Get UART mode“ utilizes API to retrieve the current UART mode of the device and displays it on the user interface.
- "Set UART mode" uses API to write UART mode to the device and it updates this value to the registry.
The Registry address we use is HKEY_LOCAL_MACHINE\SOFTWARE\MOXA\SerialInterface.
You can use the Registry Editor to check if the registry values for the port have been properly changed.

## Slide 31: Utilities: Moxa IO Controller
Notes: MoxaIOController utility is a universal command-line utility.
It supports a range of functionalities, including SIM, LED, UART, Relay, etc
Different models have their corresponding supported IO functionalities specified in the config files. The utility can then use APIs to control these IO functions of the device.
For DRP it can be used for UART settings
For BXP and RKP it can handle UARTs, digital inputs and outputs

## Slide 32: All Windows Utilities
SerialInterface Utility
  Windows-based
  Different behaviour for Super I/O UARTs and extension MU850U UARTs
MoxaIOController
  Set of command-line utilities: mx-xxx-ctl.exe
  to handle Serial ports and DIO.
SortNetName
  command-line utility: sortnetname.exe
  sorting LAN names matching HW markings.
  Note: it requires BIOS version which SMBIOS Description contains the content for sorting network names.
WindowsRecovery
  system backup to image
  restore from previously saved images

## Slide 33: Agenda
Introduction to the new Moxa DRP/BXP/RKP Series
Hardware Overview
BIOS Features
Windows Licensing and Utility Framework
Linux Distribution and SDK
Demo
  Windows Utilities and Troubleshooting
  Linux Installation and Troubleshooting
Summary

## Slide 34: Moxa x86 Linux SDK Wizard
Easy Deployment
Components for
  peripheral drives
  peripheral control tools
  control files
Deployment features
  build and installation logs
  dry-run
  self test
Notes: Moxa does not issue its own Linux distribution for SRP/BXP/RKP
Moxa supports: Debian 11, Ubuntu 22.04 LTS and RedHat 9
Moxa provides drivers and utilities for special hardware.
The Moxa x86 Linux SDK enables an easy deployment on the Moxa x86 IPC platform.
The SDK contains components for
peripheral drivers,
peripheral control tools and
configuration files.
deployment features, such as build & installation log, dry-run, and self test on the target model.

## Slide 35: Moxa x86 Linux SDK Wizard
Install.sh
Load Configuration Files
General Functions
Log Generator
Log Files
Check OS Env.
Select Target Source Files
Start Source Build and Installation Procedure
Start Source Build and Installation Procedure
Self Test Case Function
End
Notes: How does the Moxa x86 Linux SDK Wizard work?
- run shell script install.sh,
- script loads the configuration file for specific model from Product.d directory
- check if current OS is supported
- selects the corresponding driver and utility sources.
- installs the drivers, libraries and utilities
- Finaly runs a self test to verify installation

## Slide 36: Linux Tools Summary
Install SDK and Utilities: “install.sh”
Features:
  install/uninstall
  installation log
  dry-run
  self test
UART Control Utility: mx-uart-ctl
Dependencies
  it87-gpio
  it87-serial
  moxa-mxuport
  libgpiod modules
DIO Control Utility: mx-dio-ctl
Dependencies
  it87-gpio
  libgpiod modules

## Slide 37: Agenda
Introduction to the new Moxa DRP/BXP/RKP Series
Hardware Overview
BIOS Features
Windows Licensing and Utility Framework
Linux Distribution and SDK
Demo
  Windows Utilities and Troubleshooting
  Linux Installation and Troubleshooting
Summary

## Slide 38: Windows Utilities and Troubleshooting

## Slide 39: Utilities: Moxa Serial Interface Utility
Internal COM
Expansion (MU850U) COM

## Slide 40: Windows Version
Current Installed Windows Version

## Slide 41: System Information
Save System Information as *.NFO File & provide it to Moxa as base information for any support case.

## Slide 42: Windows Troubleshooting
The version can be also check by Windows command prompt
  Check Windows version
  Check MOXA image version

## Slide 43: Windows Troubleshooting: Event Viewer
View monitoring and troubleshooting messages
Log
Categories
Log Level
Log information
Event ID

## Slide 44: Windows Troubleshooting: Event Viewer
View monitoring and troubleshooting messages
Save the selected event(s)
Save all event

## Slide 45: Linux SDK Installation and Troubleshooting

## Slide 46: Moxa x86 Linux SDK Wizard

## Slide 47: Moxa x86 Linux SDK Wizard
Please configure your network settings before installation => Connect to internet
  Note: Before building, it will need to install development tool from internet
To extract the SDK tgz tarball file under Linux environment (e.g. tar xvf <sdk>.tar.gz)
User account with sudo/root privileges
Run --dry-run before installation, to check the target host device and environment are available
Run --selftest after installation, to check the status of drivers and tools
Before you install

## Slide 48: Troubleshooting:
How to Moxa x86 Linux SDK installation logs
Moxa x86 Linux SDK provides self-test for diagnosing the status of drivers and tools after installation. To simply see the log, run the following command:
For further, the log of installation is also created on Moxa_x86_Linux_Install_Wizard_<version>_Build_<build_date>/install.log

## Slide 49: Troubleshooting:
How to get Hardware Information
BIOS exports the hardware information on DMI (Desktop Management Interface) table.
Linux utility dmidecode is dumping the DMI (SMBIOS) table content in human readable format
Install dmidecode Package:
Ubuntu/Debian: sudo apt-get install dmidecode
RHEL: sudo yum install dmidecode

## Slide 50: Troubleshooting:
How to get Hardware Information
The Option 1 (or Option 2) displays the 16 bytes information, for example: RKP A110000091
RKP A110000091 means
PCBA name = RKP
PCBA number = A110
PCBA serial = 0
PCBA type = 00
PCBA hw version = 091 (v0.91)

## Slide 51: Troubleshooting:
How to get Hardware Information

## Slide 52: Troubleshooting:
How to print kernel messages
display the kernel ring buffer, which contains messages related to the kernel and hardware events.
useful tool for troubleshooting hardware-related issues, monitoring system-level events and diagnosing hardware issues.
save the output of dmesg to a file for further analysis:
or save the error and warning level log:

## Slide 53: Agenda
Introduction to the new Moxa DRP/BXP/RKP Series
Hardware Overview
BIOS Features
Windows Licensing and Utility Framework
Linux Distribution and SDK
Demo
  Windows Utilities and Troubleshooting
  Linux Installation and Troubleshooting
Summary

## Slide 54: Summary: Hardware and BIOS
BXP/DRP/RKP Series
Essentially the same computers in 3 form factors
Includes models with Atom (A100) or Celeron/Core i3/i5/i7 CPUs (C1x0)
Base models and various serial and LAN options
Generic IPC products, without extensive features.
Windows and Linux OSs supported
Some features not available across all ranges
  No DIO on DRP family
  SATA SSDs supported in RKP only
  RAID supported on RKP-C110 with Core i5 and i7 CPUs only
The BIOS offers extensions to handle Moxa specific hardware features on top of regular ones

## Slide 55: Summary: Windows, Linux, Drivers and Tools
Windows
Licensing: PKEA or ePKEA – single or volume licensing
Utilities:
  SerialInterface Utility
  MoxaIOController
  SortNetName
  WindowsRecovery
Linux
install.sh to install, uninstall and test SDK and utilities
Utilities:
  UART Control Utility: mx-uart-ctl
  DIO Control Utility: mx-dio-ctl

## Slide 57: Backup Material
Reference Information

## Slide 58: BIOS Setup
Reference Information

## Slide 59: BIOS Setup Utility

## Slide 60: BIOS Setup Utility: Main
Model name
BIOS version
Component information
  CPU
  Memory
System Time & Date

## Slide 61: BIOS Setup Utility: Chipset Configuration
Power ON after Power Failure
  ON (default)
  OFF
  Last State
Load default after cleaning RTC Battery
  Enable(default) / Disable
DO configuration
  High (Default)
  Low

## Slide 62: BIOS Setup Utility: Super IO (SIO IT8786E)

## Slide 63: BIOS Setup Utility : Super IO (SIO IT8786E)
UART port on main board
  Enable/Disable
  UART Mode: RS232/422/485(2W)
UART Configuration (serial ports)

## Slide 64: BIOS Setup Utility: Super IO (SIO IT8786E)
Hardware Monitor
  Voltage level
  Temperature

## Slide 65: BIOS Boot Menu
UEFI benefits
  Enhance boot and overall computer speed
  Secure Boot functionality
USB drive support format in UEFI is FAT32
*Moxa products do not support Legacy mode on Intel 11th generation CPUs and later.

## Slide 66: BIOS Turbo Mode for Intel CPU
Intel® Turbo Boost
Processor can temporarily boost its clock speed when there is a demand for higher performance.
Setting of Turbo Mode
  Enable (Default)
  Disable

## Slide 67: BIOS Network Adapters
The network adapter chip connects to the CPU through the PCIe bus.
I219 features vPro capabilities, allowing the execution of remote connection functions using the Intel Management Engine Bios Extension (AMT)

## Slide 68: BIOS SATA Configuration
Starting from the 11th generation Intel CPUs Intel introduces Volume Management Device (VMD).
Currently, VMD only supports SATA hard drives.
  RKP only

## Slide 69: RAID Configuration on RKP-C100
C5 and C7 models only

## Slide 70: Windows Utilities and Troubleshooting
Reference Information

## Slide 71: Windows Licensing
Certificate of Authenticity COA (License Label)
  The COA label serves as proof of license for each individual unit, and therefore cannot be transferred to other different machines or new units.
PKEA (Product Key Application) | EPKEA (Embedded Product Key Application)
Single Activation Key (One-to-One Key) All devices have a unique individual key, printed on the license proof sticker. | Multiple Activation Key (Company Key) Each OEM signing the CLA has its own set of keys that can activate multiple devices, facilitating large-scale deployments.

## Slide 72: Windows Licensing
Windows version | PKEA | EPKEA
Windows 10 LTSB 2016 | V | V
Windows 10 LTSC 2019 | V | V
Windows 10 LTSC 21H2 | V | V
Windows 10 Pro | EOS | X
Windows 11 Pro | V | X
Windows Server | X | X

## Slide 73: Windows Licensing
License activating

## Slide 74: Utilities: Moxa Serial Interface Utility
Internal COM
Expansion (MU850U) COM

## Slide 75: Utilities: Moxa Serial Interface Utility
Utility process:
GetUartMode: Device → API(Library) → Display on utility
SetUartMode: Utility → Write uart mode to registry → API(Library) → Device
Service process:
System on → Service start → Read registry → SetUartMode
Service stop → Write uart mode to registry
Registry address: HKEY_LOCAL_MACHINE\SOFTWARE\MOXA\SerialInterface

## Slide 76: Utilities: Moxa IO Controller
Functionality:
  Allows users to GET or SET IO information in CMD format
Execution Steps:
  Navigate to the specified path (C:\Program Files\moxa\moxa IOController)
  Run the exe with administrator privileges
  Execute mx-xxx-ctl.exe --help to understand how to use the commands or refer to the User Manual for screenshots and instructions for each ctl

## Slide 77: Utilities: Moxa IO Controller

## Slide 78: Utilities: SortNetName
Functionality: Sorts LAN names to match the LAN order on chassis
  Requires BIOS version which SMBIOS Description contains the content for sorting network names
Execution Steps:
  Navigate to the designated path (C:\Program Files\Moxa\Moxa Sort Net Name)
  Run the exe with administrator privileges

## Slide 79: Utilities: Prerequisits
Installation steps (must be followed in order):
Install the 2022 C++ Redistributable Package: Download the latest supported C++ Redistributable Package from Microsoft Learn
Install .NET Framework 4.8: download link
  (For Win10 LTSC 21H2 and above, .NET Framework 4.8 is pre-installed)
Install the latest version of MxGeneraIIo driver: Currently version 1.4
Install the Serial Interface, IOController, SortNetName

## Slide 80: Windows Troubleshooting
The version can be check by Windows command prompt
  Check Windows version
  Check MOXA image version

## Slide 81: Windows Troubleshooting: Event Viewer
View monitoring and troubleshooting messages
Log
Categories
Log Level
Log information
Event ID

## Slide 82: Windows Troubleshooting: Event Viewer
View monitoring and troubleshooting messages
Save the selected event(s)
Save all event

## Slide 83: Windows Recovery Utility
Functionality:
  Build Recovery USB
  Restore the system from previously saved images
Software Dependency:
  .NET Framework 4.8
  2022 C++ Redistributable Package

## Slide 84: Windows Recovery Utility
Build a Recovery USB Medium
USB capacity: 32GB or above
  All data on the USB will be formatted during the creation of the Recovery USB.
Folder: USB:\home\partimag\
BIOS restriction: UEFI only

## Slide 85: Windows Recovery Utility
Recovery

## Slide 86: Linux Installation and Troubleshooting
Reference Material

## Slide 87: Linux Installation and Troubleshooting
Linux
  Debian 11 (bullseye), Linux kernel 5.10
    Official Debian 11.8 netinst ISO download link
    Official Debian installation guide
  Ubuntu 22.04.03 LTS (Jammy Jellyfish), Linux kernel 5.15
    Official Ubuntu 22.04.03 LTS desktop ISO download link
    Official Ubuntu 22.04.03 LTS server ISO download link
    Official Ubuntu installation guide
  RedHat 9, Linux kernel 5.14
    Official RedHat 9 download link
    Official RedHat 9 installation guide

## Slide 88: Moxa x86 Linux SDK Wizard
Easy Deployment
Components for
  peripheral drives
  peripheral control tools
  control files
Deployment features
  build and installation logs
  dry-run
  self test

## Slide 89: Moxa x86 Linux SDK Wizard
x86 Linux Install Wizard Structure
product.d/ - configuration files for products scripts/ - install wizard generic programs src/ - source code for the drivers and tools install.sh - entry program for build and install the SDK README.md - this file: introduction and build instructions CHANGELOG - change log and difference to the SDK release LICENSE - MOXA license statement file version - current version of x86 Linux Install Wizard
The current available SDK version is V1.0.
Remark: the supported Linux Distributions are:
  Debian 11
  Ubuntu 22.04 LTS
  RedHat 9
Model Name | Available SDK Version | Support Linux Distributions
BXP-A100/BXP-C100 | V1.0 | Debian 11, Ubuntu 22.04 LTS, RedHat 9
DRP-A100/DRP-C100 | V1.0 | Debian 11, Ubuntu 22.04 LTS, RedHat 9
RKP-A110/RKP-C110 | V1.0 | Debian 11, Ubuntu 22.04 LTS, RedHat 9

## Slide 90: Moxa x86 Linux SDK Wizard
Install.sh
Load Configuration Files
General Functions
Log Generator
Log Files
Check OS Env.
Select Target Source Files
Start Source Build and Installation Procedure
Start Source Build and Installation Procedure
Self Test Case Function
End

## Slide 91: Moxa x86 Linux SDK Wizard

## Slide 92: Moxa x86 Linux SDK Wizard

## Slide 93: Moxa x86 Linux SDK Wizard
Please configure your network settings before installation => Connect to internet
  Note: Before building, it will need to install development tool from internet
To extract the SDK tgz tarball file under Linux environment (e.g. tar xvf <sdk>.tar.gz)
User account with sudo/root privileges
Run --dry-run before installation, to check the target host device and environment are available
Run --selftest after installation, to check the status of drivers and tools
Before you install

## Slide 94: Moxa x86 Linux SDK:
Utilities, Drivers and Libraries
Serial Port | 
The Moxa serial port mode control tool mx-uart-ctl is for getting and setting serial UART ports mode.
Depends on the following drivers
  moxa-it87-gpio-driver
  moxa-it87-serial-driver
  moxa-mxuport-driver
Depends on the following libraries
  libgpiod
Usage of UART mode control

## Slide 95: Moxa x86 Linux SDK:
Utilities, Drivers and Libraries
Serial Port | Digital IO (DIO) Port
The Moxa serial port mode control tool mx-uart-ctl is for getting and setting serial UART ports mode.
Depends on the following drivers
  moxa-it87-gpio-driver
  moxa-it87-serial-driver
  moxa-mxuport-driver
Depends on the following libraries
  libgpiod
Usage of UART mode control
Moxa DIO port control tool mx-dio-ctl is for getting DI/DO and setting DO ports status (low/high).
Depends on the following drivers
  moxa-it87-gpio-driver
Depends on the following libraries
  libgpiod
Usage of DIO state control

## Slide 96: Moxa x86 Linux SDK:
Utilities, Drivers and Libraries
Drivers Applicable Table
Available Models | it87-gpio | it87-serial | it87-wdt | mxuport
BXP-A100/BXP-C100 | V | V | V | V
DRP-A100/DRP-C100 | V | V | V | V
RKP-A110/RKP-C110 | V | V | V | V

## Slide 97: Moxa x86 Linux SDK:
Utilities, Drivers and Libraries
moxa-it87-gpio-driver
controlling GPIO interface for IT87xx Super I/O chips
These GPIOs are utilized for switching between RS232, RS422, and RS485 modes
controlling the Digital Input/Output.
Once the gpio-it87 driver has been probed, the gpiochip interface
/sys/class/gpio/gpiochip* and /sys/class/gpio/gpio* are created by driver. e.g.
Thus, by read/write the gpio value, user can get/set the super IO gpio value.
For Linux kernel >= 5.x, default uses the libgpiod to set/get super IO gpio.
Alternatively, for Linux kernel <= 3.x, default uses the sys class gpio to set/get gpio.

## Slide 98: Moxa x86 Linux SDK:
Utilities, Drivers and Libraries
moxa-it87-serial-driver
support the RS485 automatic direction control
Once the it87_serial driver has been probed, the /sys/class/misc/it87_serial/serial[p] interface are created by driver. e.g.
The UART mode selection is import into mx-uart-ctl, please reference the above Serial Port section for more information.

## Slide 99: Moxa x86 Linux SDK:
Utilities, Drivers and Libraries
moxa-it87-wdt-driver
responsible for the hardware watchdog of the IT87xx Super I/O.
The watchdog device node /dev/watchdog0 is created by it87_wdt driver. The x86 Linux SDK Wizard will default setup the watchdog deamon configuration files and enable service for specific Linux distributions.

## Slide 100: Moxa x86 Linux SDK:
Utilities, Drivers and Libraries
moxa-mxuport-driver
The MOXA UPort series driver.
This driver remains traditional serial device properties and only dial-in ports will be created.
The device name for each serial port is /dev/ttyUSBxx which xx is a sequence number maintained by USB subsystem.
The UART mode selection is import into mx-uart-ctl, please reference the above Serial Port section for more information.

## Slide 101: Troubleshooting:
How to get Hardware Information
BIOS exports the hardware information on DMI (Desktop Management Interface) table.
Linux utility dmidecode is dumping the DMI (SMBIOS) table content in human readable format
Install dmidecode Package:
Ubuntu/Debian: sudo apt-get install dmidecode
RHEL: sudo yum install dmidecode

## Slide 102: Troubleshooting:
How to get Hardware Information
The Option 1 (or Option 2) displays the 16 bytes information, for example: RKP A110000091
RKP A110000091 means
PCBA name = RKP
PCBA number = A110
PCBA serial = 0
PCBA type = 00
PCBA hw version = 091 (v0.91)

## Slide 103: Troubleshooting:
How to get Hardware Information

## Slide 104: Troubleshooting:
How to print kernel messages
display the kernel ring buffer, which contains messages related to the kernel and hardware events.
useful tool for troubleshooting hardware-related issues, monitoring system-level events and diagnosing hardware issues.
save the output of dmesg to a file for further analysis:
or save the error and warning level log:

## Slide 105: Troubleshooting:
How to Moxa x86 Linux SDK installation logs
Moxa x86 Linux SDK provides self-test for diagnosing the status of drivers and tools after installation. To simply see the log, run the following command:
For further, the log of installation is also created on Moxa_x86_Linux_Install_Wizard_<version>_Build_<build_date>/install.log

## Slide 106: Product Specification of Released Models
Reference Information

## Slide 107: BXP-C100 Product Spec
 | BXP-C100 (base model) | BXP-C100 (+ 8LAN) | BXP-C100 (+ 8COM) | BXP-C100 (+ 2LAN/3COM)
Formfactor | Box type computer |  |  | 
CPU | 11th Gen., Core™ i7-1185G7E, i5-1145G7E, or Celeron® 6305E |  |  | 
Memory slot | 1 Slot, 8GB pre-installed, 32GB max |  |  | 
OS Support | Win10 LTSC, Win10 Pro., Win11 Pro., Linux driver support |  |  | 
Video Output | HDMI + VGA |  |  | 
LAN Ports | 2 | 10 | 2 | 4
Serial Ports | 2 | 2 | 10 | 5
USB | USB 3.0 x2 + USB 2.0 x4 | USB 3.0 x2 | USB 3.0 x2 | 
DI / DO | 4DI / 4DO |  |  | 
Storage slot | CFast SSD slot + SD card slot |  |  | 
Wireless | N/A |  |  | 
Power Input | 12 / 24 VDC |  |  | 
Certificate | CE, FCC, UL |  |  | 
Operating Temp. | -30 ~ 60°C |  |  | 
Dimension (mm) | 210 x 166 x 48 | 210 x 166 x 65.5 | 210 x 166 x 83 | 210 x 166 x 65.5
2023/Q4

## Slide 108: DRP-C100 Product Spec
2023/Q4
 | DRP-C100 (base model) | DRP-C100 (+ 8LAN) | DRP-C100 (+ 6COM) | DRP-C100 (+ 2LAN/4COM)
Formfactor | Din Rail computer |  |  | 
CPU | 11th Gen., Core™ i7-1185G7E, i5-1145G7E, or Celeron® 6305E |  |  | 
Memory slot | 1 Slot, 8GB pre-installed, 32GB max |  |  | 
OS Support | Win10 LTSC, Win10 Pro., Win11 Pro., Linux driver support |  |  | 
Video Output | HDMI + VGA |  |  | 
LAN Ports | 2 | 10 | 2 | 4
Serial Ports | 2 | 2 | 8 | 6
USB | USB 3.0 x3 | USB 3.0 x3 | USB 3.0 x3 | USB 3.0 x3
DI / DO | N/A |  |  | 
Storage slot | CFast SSD slot + SD card slot |  |  | 
Wireless | N/A |  |  | 
Power Input | 12 / 24 VDC |  |  | 
Certificate | CE, FCC, UL |  |  | 
Operating Temp. | -30 ~ 60°C |  |  | 
Dimension (mm) | 60 x 150 x 130 | 94 x 150 x 130 | 94 x 150 x 130 | 94 x 150 x 130

## Slide 109: RKP-A110 Product Spec
2023/Q4
 | RKP-A110 (base model) | RKP-A110 (+ 8LAN) | RKP-A110 (+ 8COM) | RKP-A110 (+ 2LAN/4COM)
Formfactor | Rackmount 1U computer |  |  | 
CPU | Atom® Processor Elkhart Lake, Dual Core x6211E or Quad Cord x6425E |  |  | 
Memory slot | 1 Slot, 8GB pre-installed, 32GB max |  |  | 
OS Support | Win10 LTSC, Win10 Pro., Win11 Pro., Linux driver support |  |  | 
Video Output | HDMI + VGA |  |  | 
LAN Ports | 4 | 12 | 4 | 6
Serial Ports | 2 | 2 | 10 | 6
USB | USB 3.0 x3 | USB 3.0 x3 | USB 3.0 x3 | 
DI / DO | 8DI / 8DO |  |  | 
Storage slot | CFast SSD slot + SD card slot |  |  | 
Wireless | N/A |  |  | 
Power Input | 12 / 24 VDC |  |  | 
Certificate | CE, FCC, UL |  |  | 
Operating Temp. | -30 ~ 60°C |  |  | 
Dimension (mm) | 440 x 230 x 43.6 | 440 x 230 x 43.6 | 440 x 230 x 43.6 | 440 x 230 x 43.6

## Slide 110: BXP-A100 Product Spec
2023/Q4
 | BXP-A100 (base model) | BXP-A100 (+ 8LAN) | BXP-A100 (+ 8COM) | BXP-A100 (+ 2LAN/3COM)
Formfactor | Box type computer |  |  | 
CPU | Atom® Processor Elkhart Lake, Dual Core x6211E or Quad Cord x6425E |  |  | 
Memory slot | 1 Slot, 8GB pre-installed, 32GB max |  |  | 
OS Support | Win10 LTSC, Win10 Pro., Win11 Pro., Linux driver support |  |  | 
Video Output | HDMI + VGA |  |  | 
LAN Ports | 2 | 10 | 2 | 4
Serial Ports | 2 | 2 | 10 | 5
USB | USB 3.0 x2 + USB 2.0 x4 | USB 3.0 x2 | USB 3.0 x2 | 
DI / DO | 4DI / 4DO |  |  | 
Storage slot | CFast SSD slot + SD card slot |  |  | 
Wireless | N/A |  |  | 
Power Input | 12 / 24 VDC |  |  | 
Certificate | CE, FCC, UL |  |  | 
Operating Temp. | -30 ~ 60°C |  |  | 
Dimension (mm) | 210 x 166 x 48 | 210 x 166 x 65.5 | 210 x 166 x 83 | 210 x 166 x 65.5

## Slide 111: DRP-A100 Product Spec
2023/Q4
 | DRP-A100 (base model) | DRP-A100 (+ 8LAN) | DRP-A100 (+ 6COM) | DRP-A100 (+ 2LAN/4COM)
Formfactor | Din Rail computer |  |  | 
CPU | Atom® Processor Elkhart Lake, Dual Core x6211E or Quad Cord x6425E |  |  | 
Memory slot | 1 Slot, 8GB pre-installed, 32GB max |  |  | 
OS Support | Win10 LTSC, Win10 Pro., Win11 Pro., Linux driver support |  |  | 
Video Output | HDMI + VGA |  |  | 
LAN Ports | 2 | 10 | 2 | 4
Serial Ports | 2 | 2 | 8 | 6
USB | USB 3.0 x3 | USB 3.0 x3 | USB 3.0 x3 | USB 3.0 x3
DI / DO | N/A |  |  | 
Storage slot | CFast SSD slot + SD card slot |  |  | 
Wireless | N/A |  |  | 
Power Input | 12 / 24 VDC |  |  | 
Certificate | CE, FCC, UL |  |  | 
Operating Temp. | -30 ~ 60°C |  |  | 
Dimension (mm) | 60 x 150 x 130 | 94 x 150 x 130 | 94 x 150 x 130 | 94 x 150 x 130

## Slide 112: RKP-C110 Product Spec
2024/Q1
 | RKP-C110 (base model) | RKP-C110 (+ 8LAN) | RKP-C110 (+ 8COM) | RKP-C110 (+ 2LAN/4COM)
Formfactor | Rackmount 1U computer |  |  | 
CPU | 11th Gen., Core™ i7-1185G7E, i5-1145G7E, or Celeron® 6305E |  |  | 
Memory slot | 2 Slot, 8GB pre-installed, 32GB x2 max |  |  | 
OS Support | Win10 LTSC, Win10 Pro., Win11 Pro., Linux driver support |  |  | 
Video Output | HDMI + VGA |  |  | 
LAN Ports | 4 | 12 | 4 | 6
Serial Ports | 2 | 2 | 10 | 6
USB | USB 3.0 x3 | USB 3.0 x3 | USB 3.0 x3 | 
DI / DO | 8DI / 8DO |  |  | 
Storage slot | 2.5” SSD slot x2 |  |  | 
Wireless | N/A |  |  | 
Power Input | 12 / 24 VDC |  |  | 
Certificate | CE, FCC, UL |  |  | 
Operating Temp. | -30 ~ 60°C |  |  | 
Dimension (mm) | 440 x 280 x 43.6 | 440 x 280 x 43.6 | 440 x 280 x 43.6 | 440 x 280 x 43.6