## Slide 1: OnCell G4300-LTE4
Antal Marku
Andreas Roeser
Jean-Marc Olivier
2024
September 19th

## Slide 2: Expect to Gain from This Training
Understand OnCell G4300 features
Understand where to use OnCell G4300
Understand how to operate OnCell G4300 features

## Slide 3: Agenda / Training Outline OnCell G4300 Series
Product Overview
Target Markets
Feature Highlights
  Reliable WAN Connection / WAN Redundancy
  Network Management
Application Use-Case & Summary / Take-Away
Demo

## Slide 4: Product Overview

## Slide 5: OnCell G4300 Series
Industrial LTE Cat 4 secure cellular router
Global cellular bands support EU, AU, US, JP
2x 10/100/1000BaseT(X) Ports (RJ45 connector) ports
1x 3-in-1 RS232/422/485 serial port
Highly Integrated
IEC 62443-4-2 based design
Secure boot – make sure device boots using only MOXA software
IPSec VPN & NAT & Firewall & DPI
Secure with Cybersecurity
Dual Power Input
-30 to 70°C wide operating temperature
For hazardous locations and various industrial applications
Industrial-grade Reliability
Management
MXsecurity – security & distributed device management
MXview One - local device topology management
MRC Quick Link – secure & convenient remote access

## Slide 6: Target Markets

## Slide 7: Market Segments
Airports
Highways
ITS
Smart City
Mining
Solar
Sensors
Hydro
Wind
Automation
Oil & Gas
Farming Automation
Mobility
Irrigation Systems
Weather Tracking
Monitoring
Patient Data
Mobile Devices
Marine
eBuses
Manufacturing
Utilities
Transportation
Oil & Gas
Agriculture
Healthcare
Power
Factory
Building

## Slide 8: OnCell Plays a Vital Role in IoT Networking
Reliable and Secure Cellular Connectivity
Reliable Wireless Connectivity
Versatile Deployment
Remote Monitoring and Control
Scalability and Flexibility
Security and Data Protection

## Slide 9: Feature Highlights

## Slide 10: OnCell G4300 Series
New Software Platform (MX-ROS, same platform as EDR-G9010)
(L2 Switching, Static Route, VRRP, WAN Redundancy, RADIUS…)
Security
VPN
Management
Central Security (MXsecurity)
Remote Access
(MRC)
NAT
Secure Boot
Reliable WAN Connection
Dual SIM
Cellular GuaranLink
WAN Redundancy
Firewall & DPI (Deep Packet Inspection)
Topology View (MXview One)
Next Generation Software Platform

## Slide 11: GuaranLink – Guaranteed Cellular Links
Cellular GuaranLink - OnCell key technology
  Self-healing cellular connection with dual SIM switch over
  Connection Alive Check
    Always
      send alive-check packets continuously.
    Idle Transmission
      send alive-check packets only when device doesn’t receive data transmission for a while
    Poor Signal
      send alive-check packets only when device is under poor cellular signal situation.
  GuaranLink Recovery
OnCell
Internet
Base
Station
SIM 1
SIM 2
Switch SIM if available
Reliable WAN Connection
OnCell key technology – self-healing cellular connections

## Slide 12: WAN Redundancy - Wired and Wireless Redundancy
Ensure uninterrupted connectivity in different network environments
WAN Redundancy
  The Main interface can be either
    Ethernet WAN (Default)
    Cellular
  Switching process
Switch to
Cellular
Ethernet WAN
Works
Ethernet WAN
Fails
Ping
No response
Stay at Cellular
Failover
mode
Switch back to Ethernet WAN if Available
Failback
mode
Internet
OnCell
Fixed Ethernet
Base Station
Reliable WAN Connection

## Slide 13
Software Features Designed Based on the IEC 62443-4-2 Standards
Firewall policies to protect the internal network from unauthorized access and DoS attacks
Network address translation (NAT) for IP privacy between trusted and untrusted networks
VPN functionality for secure and encrypted data communication
Data Integrity and Confidentiality
User Identification and Authentication
Network Access Control and Authentication
Security Event Notifications
Secure Patches Update
Secure Boot
Firewall
NAT
VPN
DPI
Deep Packet Inspection identifies abnormal patterns and malicious behavior and provides security monitoring.
Security

## Slide 14: MXview One
Local Site Topology View
Device Info
Topology
Management
Supported by MXview One version 1.2.0 and newer

## Slide 15: Central Management - MXsecurity
MXsecurity
Moxa Security Management
For distributed management
Cellular Status Dashboard
Remote SMS Control
*(OnCell Feature)
Report
Device Management
Inventory reports, Cellular Signals,
Data Usage, Trail report
Firmware and configuration management
Management
Supported for OnCell G4302 Series (FW v3.0 or higher, MXsecurity Agent Package v2.0.13 or higher)

## Slide 16: MRC - Simplifying Maintenance Operations
Without Moxa Remote Connect
With Moxa Remote Connect
Meters
Sensors
Inverters
BMS
PCS
Energy Management System
MRC Quick Link
Go on-site to check the issue
Access to remote device for maintenance
Energy Management System
Meters
Sensors
Inverters
BMS
PCS
Enhance Satisfaction, Save Time and Reduce Labor Costs
Management

## Slide 17: Getting Started
  Purchase Device
    OnCell G4302*
MRC Gateway
  Enter Product SN to Activate MRC Service
  https://netsecuritylicense.moxa.com
Moxa License Site
  Receive MRC Quick Link Account Registration Mail
  Free Usage Quota Included
Receive Email
How to Register for MRC Quick Link Service
  Login and Start Setting
  https://mrc.moxa.com
MRC Quick Link
*Supported with Firmware 3.9.0 and higher

## Slide 18: OnCell Cellular Router With MRC Service
Operating Owners and Equipment Supplier can Understand the Condition of the Equipment.
Cellular Router
MRC Cloud
Device Monitoring
I can access to the device to solve the problem
I can see which device has the problem
MRC Client Software
(Windows App)
Operating Owner
Equipment Supplier
Data Acquisition
Build VPN Tunnel via MRC Service

## Slide 19: Secure Your Remote Access with Trust
Multiple Access Control for Diverse Requirements
Physical-Based
Gateway
Gateway
USB inserted
No USB inserted
DI On
DI Off
Time-Based
MRC Client
Gateway
Service Period
Not in Service Period
Role-Based
Gateway
Local Device
Allowed Client List:
Client A
Client A
Client B
Application-Based
Gateway
Local Device
Allowed Type:
Modbus/TCP
Management

## Slide 20: Application Use-Case & Summary / Key Features

## Slide 21: Application – Smart Monitoring & Control
Traffic Control, Smart Lighting
Control Center
Internet
Airport Highway ITS Smart City

## Slide 22: OnCell Key Features / Key Points
Global Support
Security
Stability
Rugged Design
Global Band Coverage
Region Certification
VPN
Firewall, DPI
GuaranLink Cellular Auto Recovery
Hazardous Certification
NAT
Industrial EMC
Mobile Carrier Approval
Cybersecurity features based on IEC 62443-4-2
Dual SIM Backup
WAN Redundancy between Ethernet and Cellular
5 Years Warranty
-30 to 70°C Wide Temperature

## Slide 23: Demo