## Slide 1: AWK AeroMesh Feature Release
Product Introduction Session
Zoltan Fekete, Ahmed Hyusein Ahmed
19 September 2024, v02 (final)
2024 MTSC Product Session
Field Application Engineer, Senior Tech Support Engineer

## Slide 2: Agenda
1. Wi-Fi Mesh Introduction and Applications
2. Supported Devices and Roadmap
3. AeroMesh v1.0 Terminology and Main Features and Constraints
4. AeroMesh v1.0 Feature Details
5. AeroMesh v1.0 Configuration and Operation Aspects
6. Backup Information

## Slide 3: Agenda
1. Wi-Fi Mesh Introduction and Applications
2. Supported Devices and Roadmap
3. AeroMesh v1.0 Terminology and Main Features and Constraints
4. AeroMesh v1.0 Feature Details
5. AeroMesh v1.0 Configuration and Operation Aspects
6. Backup Information

## Slide 4
Dynamic
Wi-Fi Mesh
Static Infrastructure
Wi-Fi Mesh
Self Forming
Self Healing
Proprietary
Adaptive Topology
Note: No unified industry standard
…
“Wi-Fi Mesh” Interpretation Varies
Notes: Mesh technology provides reliable and seamless Wi-Fi coverage across larger areas
Coverage across multiple nodes
Non-deterministic network topology: self-forming or self-organizing networks.
Redundant:
  Nodes can have redundant connections
  can handle node outages and re-arrange topology automatically – this is self-healing
Scalable: nodes can be added with minimal consideration
Central management for all mesh nodes
Main types:
Static: mesh nodes are connected in a fixed topology (it still may have redundancy, but less flexible)
Dynamic: can re-arrange topology based on operational status, i.e. based on load or interference level. May also steer traffic dynamically between bands or select traffic
Moxa AeroMesh 1.0 is a static implementation, but we have plans to develop it to be more dynamic
Main standards:
IEEE 802.11s: is the standard for mesh, self-healing multi-hop networks, typically used in large enterprise installations (i.e. smart cities)
Wi-Fi Alliance’s EasyMesh: mainly targets consumer/enterprice devices interworking, so components from different vendors are interoperable. Builds on top of 802.11ac and 11ax and adds mesh capabilities on top
Standards are not mature yet.
Moxa’s AeroMesh 1.0 is a proprietary solution based on standard mesh, but since we are developing our mesh with our own performance index, we do not plan to just support standard mesh which does not allow us to have any differentiation in the future.

## Slide 5: AeroMesh Overview
One of the best solutions for extending WiFi signal coverage
Notes: Wi-Fi mesh networks are designed to cover large areas more effectively.
It has wireless backhaul - Each node in the network communicates with the others without cable connection between them, extending the WiFi signal to hard-to-reach places like basements, attics, or large outdoor areas.
These diagrams are three of our success cases.
Left: fracking system;
Upper right shows a surveillance system installed in a parking space,
Lower right depicts a mining well.

## Slide 6: AeroMesh Highlights
Wireless Backhaul
  Saving on cabling costs between mesh APs
Self-Network Formation
  Self-organizes to build up the best mesh topology.
Self-Healing
  When the upstream AP is out of service, the mesh AP will automatically reroute to an adjacent AP.
Notes: Wireless backhaul is a common advantage of all mesh Aps.
Saves on cabling costs
More flexible: think about APs mounted on vehicles or in a mine, where access points are moved around regularly as the mine is driven.
Self-network forming:
users don't need to specify the adjacent APs and
Users don't need to worry about which route is the best.
Self-healing
allows users to robustly maintain their network connection.

## Slide 7: Agenda
1. Wi-Fi Mesh Introduction and Applications
2. Supported Devices and Roadmap
3. AeroMesh v1.0 Terminology and Main Features and Constraints
4. AeroMesh v1.0 Feature Details
5. AeroMesh v1.0 Configuration and Operation Aspects
6. Backup Information

## Slide 8: Models and Version
Supported models
  AWK-3252A
  AWK-4252A
Firmware version
  Latest version: V3.2
Release Date
  Initially Released in June 2024 (V3.1 introduced Mesh)
  V3.2 released in August 2024

## Slide 9: Wi-Fi and Mesh Roadmap
2.4GHz + 5GHz
2.4GHz + 5GHz + 6GHz
Wi-Fi 7
AWK-4372
Tri-Band Concurrent
Wi-Fi Mesh AP
AeroMesh 2.0
IEC 62443-4-2 Redundant Pwr, LAN, Wireless Low Latency
High Density
688 ~ 9334 Mbps
Reliable
Mesh Support
Notes: Let’s look into the crystal ball on what is coming
Wi-Fi 4 – is for legacy market: replacement or very cost-effective solution. No mesh support
Wi-Fi 5 – this is our current mainstream market,
  well established
  Good balance between performance and price
  Security is supported, IEC-62443-4-2 certified
  First devices got the mesh upgrade, no plans AWK-1151C to support mesh
Wi-Fi 6 – products are the latest addition
  40% or more bandwidth increase compared Wi-Fi5, but more important is to handle large number of clients reliably
  Value client device AWK-116x clients and Access Points have just been released recently. No mesh support on those entry-level devices.
  Value clients and APs with 1 or 5 LAN connections (allows to eliminate a switch e.g. in an AGV or other equipment)
  High-end indoor and outdoor APs are coming early next year, and mesh support is expected around Q3 next year.
Wi-Fi 7 – is under development, prototypes expected early 2025, mass production later, in 2026.
  It will be tri-band concurrent radio, including 6 GHz as well
  Mesh will be integral part
  Almost 8x speed improvement compared to Wi-Fi 5, low latency, security.

## Slide 10: Agenda
1. Wi-Fi Mesh Introduction and Applications
2. Supported Devices and Roadmap
3. AeroMesh v1.0 Terminology and Main Features and Constraints
4. AeroMesh v1.0 Feature Details
5. AeroMesh v1.0 Configuration and Operation Aspects
6. Backup Information

## Slide 11: Mesh Terminology
Mesh Portal
  Maintains the mesh topology.
  Usually gateway to the mesh network; it bridges the wireless network to Ethernet backbone.
Mesh Node (MAP)
  The Mesh point establishes wireless links to neighbours.
  Provisioning of BSS service to support STA connection (classic AP functionality)
Backhaul Network
  Connection between AeroMesh devices.
  Provides data communication from the external Ethernet network to the Access Point of the Mesh Node
Fronthaul Network
  The connection between AeroMesh device (MAP) and Client station (STA).

## Slide 12: AeroMesh v1.0 Features and Constraints
AeroMesh topology support: tree, star and daisy chain
Mesh Backhaul connection supports 5GHz band only.
Fronthaul Data Transmission (VAP) supports both 5GHz and 2.4GHz.
  2.4GHz is recommended in spaces free from interference.
10 nodes can be connected to a Portal at a time.
Support up to 5 hops.
A Mesh Node enables the AP function only after it has successfully joined the mesh network.
  No ‘ghost’ APs

## Slide 13: Agenda
1. Wi-Fi Mesh Introduction and Applications
2. Supported Devices and Roadmap
3. AeroMesh v1.0 Terminology and Main Features and Constraints
4. AeroMesh v1.0 Feature Details
5. AeroMesh v1.0 Configuration and Operation Aspects
6. Backup Information

## Slide 14: AeroMesh v1.0 Feature Details
AeroMesh supports tree, star and daisy chain topologies.
Notes: Tree: there are multiple branch nodes, i.e. nodes with more than 2 connections possible
Star: fully centralized, all mesh nodes are connected to the Portal node
Daisy chain: nodes are linked one after the other
Combination of topologies are also allowed, i.e. star topology of daisy chained hops around the portal node.

## Slide 15: AeroMesh v1.0 Feature Details
The Mesh backhaul connection only supports 5GHz bands.
Fronthaul Data Transmission(VAP) supports both 5GHz and 2.4GHz. However, 2.4GHz is recommended in spaces free from interference.
Portal
Node
Node
Node
Node
Fronthaul (5GHz/2.4GHZ)
Fronthaul (5GHz/2.4GHz)
Backhaul(5GHz)
此相片 (作者: 未知的作者) 已透過 CC BY-SA-NC 授權
Notes: The Mesh backhaul connection only supports 5GHz bands because 5GHz is more resistant to interference. (Backhaul is more prone to interference as it is typically bridging longer distances than the distance between the Mesh node and the client STA)
The fronthaul side can be 2.4 and 5 GHz
  If both fronthaul and backhaul are set to 5GHz, the throughput will significantly decrease because the 5GHz antenna needs to switch between AP and STA (or client) modes.
  Therefore, we suggest to use 2.4 GHz for fronthaul, unless the interference is too high on 2.4 GHz.

## Slide 16: AeroMesh v1.0 Feature Details
10 nodes can be connected to a Portal at a time.
Supports up to 5 hops.
Portal
Node
Hop 1
Node
Node
Node
Node
Hop 2
Hop 3
Hop 4
Hop 5
Notes: The maximum number of nodes that can be connected to the portal node is 10.
There could be maximum of 5 hops
It means that from any mesh nodes to the portal node could be not more than 5 connections (depicted as lines on the picture)
If the number of joined nodes reaches the limit, the portal will reject any join request of new node.
Similarly, the portal will not allow more than 5 hops in a chain. Device in the sixth hop will not be able to connect. This is to avoid too much backhaul speed degradation.

## Slide 17: AeroMesh v1.0 Feature Details
A Mesh Node enables the AP function only after it has successfully joined the mesh network.
Portal
Node
Notes: An AP without an upstream connection will become a black hole or a ghost AP.
Disabling it’s Wi-Fi signal could provide stations with an opportunity to connect to other healthy Access points.

## Slide 18: AeroMesh v1.0 Join Flow
Node
Portal
Join mesh
Periodical Update scan report
Setup wireless connection
join request*
join response
send scan report
scan report ack
*multicast
Notes: Aeromesh 1.0 join flow
Wi-Fi connection establishment starts with a 4-way handshake: which securely establishes connection between access point and client, including WPA2 or WPA3 security protocols. Remember, the mesh node is both a client and access point at the same time. We are talking about when a mesh node establishes connection to the mesh portal directly or through other mesh nodes.
After the 4-way handshake is completed a Moxa proprietary AeroMesh join process starts (messages are proprietary):
the mesh node will issue a join request to the portal and wait for the response.
The Join request is multicast packet, the others are unicast packets
If the join request is successful, the portal will send join response.
Mesh node will periodically update the scan report to the portal every second.
Portal acknowledges the receipt of scan reports
After successfully joining the mesh network, the mesh node starts to provide network service;
however, the topology might not be the best. Optimisation comes later

## Slide 19: MOXA AeroMesh v1.0 Performance
(Shared Channel)
MAP
MAP
Standard Wi-Fi AP Service
Ethernet
Wi-Fi Mesh backhaul
MAP
MAP
MPR
MAP
867 Mbps
433 Mbps
216 Mbps
108 Mbps
54 Mbps
2.4GHz
5GHz
Ch. 44
Ch. 44
Ch. 44
Ch. 44
Ch. 44
MPR | Mesh Portal | Only one MPR in one Mesh Network Topology. Node physically connected to Ethernet. Can select to enable AP SSID.
MAP | Mesh AP | Meshed node/s with AP SSID enabled to service standard Wi-Fi Clients.
AeroMesh v1.0 Network Capacity |  | Max node quantity: 10 nodes. Max hop from MPR: 5 hops.
Notes: Important to understand the performance of the mesh network
The supported devices have dual-band concurrent radio stages and can transmit at the same time on both 2.4 and 5 GHz. In the recommended setup fronthaul is using 2.4 GHz and the backhaul is using 5 GHz.
The performance of fronthaul is as it is expected on 2.4 GHz (around max 400 Mbps for our Wi-Fi 5 two-way MIMO devices)
However, the backhaul needs to share its bandwidth between being a client towards the portal and the access point towards other mesh nodes.
The backhaul bandwidth is halved at each hop. The reason is that every node has to share the same 5GHz channel for every hop. As Wi-Fi is a half-duplex communication, throughput will be halved as every node has to split the throughput among the ones preceding and following the current node.
This is the main reason for having the 5 hops limitation.

## Slide 20: Agenda
1. Wi-Fi Mesh Introduction and Applications
2. Supported Devices and Roadmap
3. AeroMesh v1.0 Terminology and Main Features and Constraints
4. AeroMesh v1.0 Feature Details
5. AeroMesh v1.0 Configuration and Operation Aspects
6. Backup Information

## Slide 21: Steering
Threshold: RSSI -70(Configurable)
Portal is the first to enable AP functionality
Without steering many or all nodes may connect to it
This leads to not optimal mesh topology
Steering is based on configurable RSSI Threshold
  Default is 70 dBm
Steering helps enforcing right topology under normal circumstances
Portal
Node
Node
Node
Node
Node
-70
-80
-60
-70
-80
-70
-70
-70
Notes: Since the portal is the first one to enable the AP function, all the nodes might connect to it; however, this might not be the best topology.

## Slide 22: Key Log Messages – Mesh Portal
No. | Severity | System Log | Note
1 | Notice | [SSID] The mesh node [node's MAC] failed to join the mesh network (reason: xxxx). | Reason: The mesh group is full. Information mismatch.
2 | Notice | [SSID] The mesh node [node's MAC] has left the mesh network. | 
3 | Notice | [SSID] The mesh network has reached the steady state (xxx secs). | xxx secs: The required Time.
4 | Notice | The mesh portal determined that mesh node [node's MAC] will roam [original MAC] to [target's MAC]. | 
Notes: Here are the log messages of the Mesh Portal
All mesh nodes joined are logged
Similarly, all nodes leaving the mesh are logged
Network has reached steady state, so nodes have joined, and connections optimized based steering rules
Finally, there is a log entry when mesh portal decides to move a mesh node somewhere else (topology change)

## Slide 23: Key Log Messages – Mesh Node Logs
No. | Severity | System Log | Note
1 | Notice | [SSID] Failed to join the mesh network [portal's MAC] (Reason: xxxx). | Reason: The mesh group is full. Portal response timed out. Information mismatch.
2 | Notice | [SSID] Attempting to connect to [target's MAC] as determined by the mesh portal. | 
3 | Notice | [SSID] Left the mesh network [portal's MAC]. | 
The system LED blinks red four times per second if joining the mesh fails.
Notes: The important log messages on a mesh node:
Most important if the node failed to join the mesh network.
  This is also indicated by the red LED blinking on the device 4 times.
  There could be several reasons
    Mesh group is full (10 nodes already in mesh network)
    Portal response is not received within expected time (portal is down, or radio conditions are bad)
    There is a mismatch of information between the portal and the mesh node. This indicates a setup error

## Slide 24: Throughput Test Results
Test conditions:
Connection type: conductive
Frequency: 5 GHz
Channel width: 20-40-80 MHz
Channel: 44
Management transmission rate: HT-MCS0
Broadcast/Multicast transmission rate: HT-MCS0
Notes: Let’s look at Wi-Fi 5 performance a bit more in detail.
The raw transmission rate for a device with 2-way MIMO is 867 Mbit/s. However that is raw speed including channel coding, redundancy, protocol overhead and so on.
The top throughput measurable in downlink direction (e.g. AP to client or in our case from portal to mesh node) is slightly over 500 Mbit/s, while the uplink throughput is a bit less than 500 Mbit/s

## Slide 25: Throughput as a Function of Hops
hops | MPR to MAP | MAP to MPR | RSSI | SNR
1 | 515 | 503 | -58 | 48
2 | 285 | 273 | -58 | 48
3 | 190 | 188 | -57 | 48
4 | 136 | 136 | -58 | 48
5 | 104 | 104 | -58 | 49
Traffic type: TCP, Connection type: air
Note: When throughput is overloaded, it may cause Wi-Fi disconnect with reason code 34 (Mesh client) or 0 (Mesh AP).
Notes: These results show the backhaul throughput as a function of the hop number.
We can see that real-life measured results are showing a decrease along the subsequent hops, but it is not halved with every hop.
The speed on the fronthaul, i.e. from AP to client station is having the same behaviour as a non-mesh system, with of course the possible limitation coming from backhaul.
Test condition :FW version: v3.0 Build 2023_1229_2231, Traffic type: TCP, Connection type: air

## Slide 26: AeroMesh v1.0 System Event Timing
The backhaul network will form a topology based on the signaling conditions.
Time to stable topology: 2 min.
  The topology enters to stable state, when the topology maintains 2 mins without change
Self-healing time: 2 sec/hop with 99.5% probability (for mesh devices only)
  If Channel Plan has only 1 non-DFS channel. In case of more channels, it will take more time.
Self-healing for Client Devices: 2s typical, 45s maximum (for Windows 10)
  depends on aging time of ARP table.
Mesh node Scanning Interval: 1 sec
  Mesh node will send scanned result every second.
Mesh Node detecting the disappearance of Mesh Portal: ~12 seconds
Triggering topology re-form: 17 sec
  When uplink signal is weak and data cannot be transmitted, Mesh Node disconnects due to Join failed.
  The Mesh Node detects Join failed state in ~2 seconds.
  If Mesh Node disconnected over 17 sec, the topology will be re-formed.
Notes: The backhaul network will form a topology based on the signaling conditions.
The total required time of stable topology: 2 mins. The topology go to stable state, when the topology maintain 2 mins without change
The required time of self-healing time: 2s/hop with 99.5%. Only applicable to mesh devices.
The device behind the mesh devices will take more time to recovery. Normal: 2s, Max: 45s (windows 10), depends on aging time of ARP table.
It is possible that the L2UF (master behavior) of the device connected (by Ethernet) to the next hop mesh device will be dropped. This will result in a waiting period for normal communication until the MAC table is updated.
The channel plan has only 1 non-DFS channel. If there are more channels, it will take more time.
Mesh node scanning report interval is 1 second. All mesh nodes send scan reports every second
The Mesh Node detecting the disappearance of Mesh Portal disappear takes about ~12 seconds
The Mesh Node detects join failed state in about ~2 seconds.
It will take 17 seconds or more to re-form the mesh topology

## Slide 27: Agenda
1. Wi-Fi Mesh Introduction and Applications
2. Supported Devices and Roadmap
3. AeroMesh v1.0 Terminology and Main Features and Constraints
4. AeroMesh v1.0 Feature Details
5. AeroMesh v1.0 Configuration and Operation Aspects
6. Backup Information

## Slide 28: Event logs on Mesh portal
6 | Notice | The mesh portal has identified a more stable mesh topology.✎ | 
5 | Notice | The mesh portal determined that mesh node [node's MAC] will roam [original MAC] to [target's MAC]. ✎ | 
4 | Notice | [SSID] The mesh network has reached the steady state (xxx secs). ✎ | xxx secs: The required Time.
3 | Notice | [SSID] The mesh node [node's MAC] has left the mesh network. ✎ | 
2 | Notice | [SSID] The mesh node [node's MAC] failed to join the mesh network (reason: xxxx). ✎ | Reason: ✎ The mesh group is full. Information mismatch.
1 | Notice | [SSID] The mesh node [node's MAC] successfully joined the mesh network. ✎ | ---

## Slide 29: Event logs on Mesh node
1 | Notice | [SSID] Successfully joined the mesh network [portal's MAC]. ✎ | ---
2 | Notice | [SSID] Failed to join the mesh network [portal's MAC] (Reason: xxxx). ✎ | Reason: ✎ The mesh group is full. Portal response timed out. Information mismatch.
3 | Notice | [SSID] Attempting to connect to [target's MAC] as determined by the mesh portal. ✎ | 
4 | Notice | [SSID] Left the mesh network [portal's MAC]. ✎ |