## Slide 1: OnCell G4300-LTE4 Demo Hands-on
Antal MARKU
Andreas ROESER
Jean-Marc OLIVIER
2024
September 19th

## Slide 2: Hands-on

## Slide 3: Hands-on
WAN / SIM Redundancy
SMS remote control
  Send SMS by Expect script
  Control OnCell output by SMS message

## Slide 4: Configuration
Hands-on was configured on the following firmware version:

## Slide 5: WAN / SIM Redundancy

## Slide 6: WAN / SIM Redundancy- Topology
OnCell
Internet
Base
Station
WAN port
LAN port
PC

## Slide 7: WAN / SIM Redundancy - Configuration
Set the SIM PIN

## Slide 8: WAN / SIM Redundancy - Configuration
Check the OnCell is connected to the Internet in the „Device Summary” menu

## Slide 9: WAN / SIM Redundancy - Configuration
Create a separate VLAN for WAN port and assign the port to the VLAN

## Slide 10: WAN / SIM Redundancy - Configuration
Set the newly created VLAN ID „2” to the WAN port

## Slide 11: WAN / SIM Redundancy - Configuration
Set the WAN redundancy mode to Backup

## Slide 12: WAN / SIM Redundancy - Configuration
Enable and set the „Host IP Address” for Ethernet WAN and Cellular in the „WAN Backup Priority” setting

## Slide 13: WAN / SIM Redundancy - Configuration
Set the „Outgoing Interface” to „Any” in the „NAT” setting

## Slide 14: WAN / SIM Redundancy - Configuration
Check the GuaranLink is enabled

## Slide 15: WAN / SIM Redundancy - Status
Connect the patch cable (Internet) to port „LAN1/WAN” and check the „Routing Table” default route goes through the WAN interface

## Slide 16: WAN / SIM Redundancy - Status
Status of the active WAN port can be verified in the „WAN Redundancy” „Status” tab

## Slide 17: WAN / SIM Redundancy - Status
Another check can be via ping from the „Tools” menu 8.8.8.8 replies for ping request

## Slide 18: WAN / SIM Redundancy - Status
From PC the wired ISP can be checked by whatismyipaddress.com

## Slide 19: WAN / SIM Redundancy - Status
From PC the google.com can be ping by the wired ISP

## Slide 20: WAN / SIM Redundancy - Status
If the patch cable (Internet) is disconnected, the default route fall back to cellular network

## Slide 21: WAN / SIM Redundancy - Status
Status of the active WAN port can be verified in the „WAN Redundancy” „Status” tab

## Slide 22: WAN / SIM Redundancy - Status
From PC the cellular ISP can be checked by whatismyipaddress.com

## Slide 23: WAN / SIM Redundancy - Status
From PC the google.com can be ping by the cellular ISP

## Slide 24: SMS remote control

## Slide 25: Send SMS by Expect script

## Slide 26: Send SMS by Expect script - Topology
Use case
The SMS sending feature via script helps for engineers to deploy an SMS centralized network to send SMS messages by UC ARM computers without embedded LTE module

## Slide 27: Send SMS by Expect script - Flowchart

## Slide 28: Control OnCell output by SMS message

## Slide 29: Control OnCell output - Topology
Use case
The water station manager can send an SMS and switch on the Water Pump Station 2 if higher amount of water supply is needed. Once the requested amount of water got back to normal another message can turn off the second pump station.

## Slide 30: Control OnCell output - Configuration
Controlling output by SMS requires to enable SMS Remote Control set and password

## Slide 31: Control OnCell output - Configuration
If „Trusted Number Authentication” enabled the OnCell accepts message only from the dedicated phone number

## Slide 32: Control OnCell output - Configuration
SMS remote control command can be checked in the „Event Log table”