## Slide 1
Introducing 6000 G2 series
Christian Gromeier | Stefan Czoer
Moxa Europe Technical Support
30.January 2025

## Slide 2
Demo
What’s new on NPort 6000-G2
  Device Search Utility 3.0
  Dashboard
  Operation mode settings
  Maintenance
  Troubleshooting tools
Why NPort 6000 G2?
Introducing 6000 G2 series
1
2
3

## Slide 3: NPort 6000 G2 Demo Topology
Ethernet
Serial
Local Network
Machine B (Optional)
Serial COM
Machine A (Simulated)
Serial COM
NPort 6250 G2
Ethernet to Serial
Application using Serial COM Port
(RealCOM)
Notes: Machine which has a Serial COM port for communication
Legacy Application running on a PC which needs to communicate via Serial Port with the Machine
Using existing Ethernet Network infrastructure
-> Solution NPort 6000 G2 series with RealCOM operation mode

## Slide 4: NPort 6250 G2 Demo
Initial Configuration (for RealCOM operation mode)
On PC running the application
  Install NPort Driver (NPort Driver Manager)
    Install DSU (Device Search Utility) comes with NPort Driver Manager included.
    DSU can help to preconfigure NPort by uploading an existing configuration or set Initial IP address
  Configure NPort Driver Manager
    Map the NPort (IP and Serial Port) to a local COM port
On NPort
  Upload existing preconfigured configuration file, or
    Can be done also via DSU utility
  Start with clean factory settings
    Set Network parameter, like IP address …
    Selecting the Operation Mode, like RealCOM
    Select Serial Port Interface Mode like RS232 or RS485
Ready for Application to use the mapped COM port

## Slide 5: Initial Configuration
Config RealCOM mode
Follow the following video for setting RealCOM mode
https://www.moxa.com/en/videos/nport-g2-quick-install
https://www.moxa.com/en/videos/nport-g2-web-guide
Notes: Based on previous surveys, over 50% of customers use RealCOM mode.
To address this, the NPort 6000-G2 carton packaging includes a QR code linking to a RealCOM mode setup tutorial video. Customers can immediately see it upon opening the box and follow the instructions for setup.

## Slide 6: Initial Configuration
https://www.moxa.com/en/videos/nport-g2-quick-install
https://www.moxa.com/en/videos/nport-g2-web-guide

## Slide 7: NPort 6250 G2 Demo, Real Device setup view

## Slide 8: NPort 6250 G2 Demo
Initial Configuration with DSU (Device Search Utility)
Discover NPort
  Unlock NPort
Assign IP address
Configure NPort
  By Web UI (Console) or,
  By Uploading Configuration from
  DSU

## Slide 9: NPort 6250 G2 Demo
Existing configuration file from previous NPort 6000 series generation

## Slide 10: NPort 6250 G2 Demo
Map serial COM port

## Slide 11: NPort 6000 G2 Demo Troubleshooting
Simplified setup with PComm
Ethernet
Serial
Machine A (Simulated)
Serial COM
NPort 6250 G2
Ethernet to Serial
PComm using Serial COM Port
RealCOM
PComm using Serial COM Port
UPort USB to Serial Adapter

## Slide 12: NPort 6250 G2 Demo
Troubleshooting, PComm
Terminal connected to
UPort
Terminal connected to
NPort 6250 G2 Port 1

## Slide 13: NPort 6250 G2 Demo
Troubleshooting, Traffic Monitor

## Slide 14: NPort 6250 G2 Demo
Extended Troubleshooting, Diagnostic Information
Export the Diagnostic Information and send it to Moxa Technical Support with description of the failure details and the expected behavior.
Ideally with a description (including topology drawing) helping to reproduce the problem in our own lab.

## Slide 15: Questions?