## Slide 1
Andreas Röser
Ahmed Hyusein Ahmed
January 2025
Wi-Fi 6, 802.11ax
AWK-1160 Series

## Slide 2: Expect to Gain from This Training
Understand Wi-Fi 6 AWK Series features
Understand where to use AWK Wi-Fi 6
Understand how to operate AWK Wi-Fi 6 features

## Slide 3: Agenda
Product Overview
  AP: AWK-1161A /1165A Series
  Client: AWK-1161C /1165C Series
New Feature Highlights
  Wi-Fi 6 RF profile
  Fast Boot-up
  Link Fault Pass-Through
Target Market
Demo

## Slide 4: Product Overview
AWK-1161A /1165A
AWK-1161C /1165C

## Slide 5
2.4GHz | 5GHz
Legacy Market
Wi-Fi 4
Wi-Fi 5
Advanced Segment AWK-4000 Series AWK-3000 Series
Value Segment AWK-1000 Series
Portfolio Highlights
Wi-Fi 6
AWK-4131A
AWK-3131A
AWK-4252A
AWK-3252A
AWK-1161A
AWK-1131A
AWK-1137C
AWK-1165A
2.4GHz + 5GHz
AWK-4262A
AWK-3262A
AWK-1160 SERIES
PORTFOLIO POSITION
AWK-1160 Series
AWK-1161C
AWK-1165C
IEC 62443-4-2
High Density
~ 1201 Mbps
Reliable
IEC 62443-4-2
~ 867 Mbps
Reliable
Mainstream Market
High-end Market
300Mbps
Reliable
Q1 2025
AWK-1151C
2.4GHz | 5GHz
2.4GHz + 5GHz

## Slide 6
AWK-1161A /1165A Series
Industrial IEEE 802.11ax wireless AP
High-performance Wi-Fi 6 AP coverage in minimal size
Smallest standalone industrial Wi-Fi 6 AP for compact machine integration
Built-in Firewall filters and Client-isolation for uncompromised security
OFDMA technology for realizing greater network capacity with lower latency in high device density environments
Industrial EMC
EN 61000-6-2
EN 61000-6-4
Medical EMC
IEC 60601-1-2
Access Point / Master / Sniffer

## Slide 7
AWK-1161C /1165C Series
Industrial IEEE 802.11ax wireless Client
High-performance Wi-Fi 6 connectivity in minimal size
Smallest standalone industrial Wi-Fi 6 Client for compact machine integration
Millisecond-level client-based Turbo Roaming for always-on connectivity
OFDMA technology for realizing greater network capacity with lower latency in high device density environments
Industrial EMC
EN 61000-6-2
EN 61000-6-4
Medical EMC
IEC 60601-1-2
Client / Client-Router / Slave / Sniffer

## Slide 8
OFDMA Benefits
Allowing multiple users to simultaneously transmit data, enabling lower latencies in large-scale, high-density deployments

## Slide 9
 | AWK-1161 | AWK-1161-T | AWK-1165 | AWK-1165-T
Wi-Fi Standard | IEEE 802.11ax - Wi-Fi 6 |  |  | 
Frequency Band | Selectable 2.4 GHz / 5 GHz Dual Band |  |  | 
RF Data Rate | 2.4 GHz: Up to 573.5 Mbps / 5 GHz: Up to 1,201 Mbps |  |  | 
Operating Temp. | -25 to 60°C | -40 to 75°C | -25 to 60°C | -40 to 75°C
Width | 34.2 mm | 47.2 mm | 53 mm | 66 mm
Height x Depth | 100 mm x 60 mm |  |  | 
Ethernet LAN | 1 * 10/100/1000 BaseT(X) |  | 5 * 10/100/1000 BaseT(X) | 
AP Models | AWK-1161A-US AWK-1161A-UN | AWK-1161A-US-T AWK-1161A-UN-T | AWK-1165A-US AWK-1165A-UN | AWK-1165A-US-T AWK-1165A-UN-T
Client Models | AWK-1161C-US AWK-1161C-UN | AWK-1161C-US-T AWK-1161C-UN-T | AWK-1165C-US AWK-1165C-UN | AWK-1165C-US-T AWK-1165C-UN-T
Height
Width
Depth
DIN rail mount

## Slide 10: New Feature Highlights

## Slide 11: Wi-Fi 6 RF Profile
2.4 GHz
5 GHz
RF Type
AX Only
N/AX Mixed
G/N/AX Mixed
B/G/N/AX Mixed
Channel Width
20 MHz
20/40 MHz
RF Type
AX Only
AC/AX Mixed
N/AC/AX Mixed
A/N/AC/AX Mixed
Channel Width
20 MHz
20/40 MHz
20/40/80 MHz
MCS11: 574 Mbps
MCS11: 1201 Mbps
Max Tx Power: 18 dBm
Note:
Wi-Fi 6 OFDMA
enabled with 11ax RF type.
No additional configuration

## Slide 12: Higher data rate
Moxa Wi-Fi 5 Series
  MCS9 (256QAM), 2 Spatial Stream
    2.4GHz: 400 Mbps
    5GHz: 867 Mbps
Moxa Wi-Fi 6 Series
  MCS11 (1024QAM), 2 Spatial Stream
    2.4GHz: 574 Mbps
    5GHz: 1201 Mbps

## Slide 13: Fast Boot-up
Voice of Customer Requirement:
  AWK security boot time too long,
  optimize boot time UX without compromising security architecture.
Enabled > Average Boot-time reduces around 20%

## Slide 14: Fast Boot-up – How To Enable > Reboot > Apply Mechanism > 2nd Reboot
Disabled (Default)
In Effect on 2nd Reboot
Application
Kernel
CPU
MEM
FLASH
Config run time generated
Enabled (1st Reboot)
Application
Kernel
CPU
MEM
FLASH
Config run time generated
Config
Application
Kernel
CPU
MEM
FLASH
Config
Run time Config from Flash
Boot-time reduces ~20%

## Slide 15: Link Fault Pass-Through
Feature Description:
  A) Local check:
    AP/Master mode:
      Selected LAN link down > Wi-Fi interface off; Selected LAN link up > Wi-Fi interface on
    Client/Client-Router/Slave mode:
      Selected LAN link down > Wi-Fi interface off; Selected LAN link up > Wi-Fi interface on
      Wi-Fi disconnected > Selected LAN link down; Wi-Fi connected again > Selected LAN link up
  B) Remote check:
    AP/Master/Client/Client-Router/Slave mode:
      Ping remote host to determine Wi-Fi interface’s on/off

## Slide 16: A) Link Fault Pass-Through – Local Check
Configuration Options:
State machines:
LAN OK
LAN FAIL
(AP/Master)
(Client/Client-Router/Slave)
Interface
LAN1
LAN2
LAN3
LAN4
LAN5

## Slide 17: B) Link Fault Pass-Through – Remote Check
Configuration Options: State machine:

## Slide 18: Link Fault Pass-Through
Event logs:

## Slide 19: Target Market
High Bandwidth requirements
High Density

## Slide 20
High-bandwidth
Medical Imagery Backhaul
APPLICATION SUMMARY
Medical Equipment Builders need APs for integration with medical radiography machines. These APs serve as the wireless interface for diagnostic tablet to connect and offload acquired patient medical images.
Why Moxa
Smallest Standalone Industrial Wi-Fi AP
High Reliability and Long Product Life
Medical EMC IEC 60601-1-2 Certified
Wi-Fi 6 Bandwidth for Efficient Data Offload
UN Model Solution for International Compliance

## Slide 21
High-density
Autonomous
AMH Robots
APPLICATION SUMMARY
Material Handling AMR Builders need compact clients for integration with growing robot fleets. Clients must be compact enough for space-constrained AMRs, while also supporting multiple LAN ports to simplify integration on more complex AMR models.
AWK-1165C
Why Moxa
Smallest Standalone Industrial Wi-Fi Client
High Reliability and Long Product Life
AP Agnostic Client-based Turbo Roaming
Wi-Fi 6 OFDMA to Support High Density Deployment
UN Model Solution for International Compliance

## Slide 22: AWK-1160 Series
High-density
OFDMA technology for greater network capacity with lower latency for environments with high device density
High-performance, compact Wi-Fi 6 (IEEE 802.11ax) Aps and Clients enable seamless connectivity for your industrial assets
Value Proposition
Cost Effective
AWK-1165A/C Series offers both AP/Client and built-in 5-port switch to simplify integration overheads
1
2
3
Compact
Smallest standalone industrial Wi-Fi 6 APs/Clients for compact machine integration

## Slide 23
Wi-Fi 6, 802.11ax​ AWK-1160 Series
Demo

## Slide 24: Pre-learned Knowledge
How to look up data rate from MCS table (https://mcsindex.com/)
✓
✓
✓
✓
Notes: How to look up data rate from MCS table with different Wi-Fi generations under various combinations of parameters such as modulation, code rate, channel bandwidth... and so on

## Slide 25: Agenda
Hands-On Practice
Hands-On #1: Throughput test(Wi-Fi 6)
Hands-On #2: Link fault passthrough

## Slide 26: Hands-On #1 Throughput test (Wi-Fi 6)

## Slide 27: Hands-On #1
Throughput test: Wi-Fi 6
Topology for Wi-Fi 6 throughput test:
AWK-1161C 192.168.127.243
AWK-1161A 192.168.127.253
iPerf Client 192.168.127.10
iPerf Server 192.168.127.40

## Slide 28: Step 1
Setup AWK-1161A: Wireless Settings
AP mode
SSID Settings

## Slide 29: Step 2
Setup AWK-1161A: Configure SSID Settings

## Slide 30: Step 3
Setup AWK-1161A: Wireless Settings
RF Settings

## Slide 31: Step 4
Setup AWK-1161C: Wireless Settings
Client mode
SSID Settings
Security Settings

## Slide 32: Step 5
Setup AWK-1161C: RF Settings
RF Type
Channel Width
Channel Plan

## Slide 33: Step 6
Check Wi-Fi Connection Status on Client
Wireless Settings > Wi-Fi Connections

## Slide 34: Step 7
Check Wi-Fi Connection Status on AP
Wireless Settings > Wi-Fi Connections > Associated Client List

## Slide 35: Step 8
Set up iPerf Server & Client
Server command:
  iperf3.exe -s -i 1
Client command:
  Iperf3.exe –c Server_IP –t 30 –i 1 –u –b xxxM

## Slide 36: Step 9
Check throughput result on iPerf Server
Average around 929Mbps

## Slide 37: Hands-On #2 Link Fault Passthrough

## Slide 38: Hands-On #2
Link fault passthrough
Topology:
AWK-1161A
AWK-1165A
Wi-Fi Client
- - - connected - - -
Link down or cable issue
Server
Unable to access server
AWK-1161A
Wi-Fi AP
192.168.127.253
AWK-1165A
Wi-Fi AP
192.168.127.252
AWK-1161C Wi-Fi Client
192.168.127.243
- - - connected - - -
Server
Scenario:
Client PC
Client PC
192.168.127.40
192.168.127.10
EDS-505A 192.168.127.40

## Slide 39: Hands-On #2
Link fault passthrough
Topology:
AWK-1161A
AWK-1165A
Wi-Fi Client
Link down or cable issue
Server
AWK-1161A
Wi-Fi AP
192.168.127.253
AWK-1165A
Wi-Fi AP
192.168.127.252
AWK-1161C Wi-Fi Client
192.168.127.243
- - - connected - - -
Server
Scenario:
Client PC
Client PC
192.168.127.40
192.168.127.10
Can access server again
- - - connected - - -
LFPT triggers WLAN OFF
EDS-505A 192.168.127.40

## Slide 40: Step 1
Ensure Wi-Fi Client connect to one of AWK-116xA and can ping the server
Wi-Fi Client can be laptop, AWK-1161C or any other Wi-Fi enabled device. Here we take AWK-1161C as example

## Slide 41: Step 2
Setup link fault passthrough on both AWK-116xA
Wi-Fi > Connection Management > Link Fault Pass-through
Select ”Local” and/or “Remote”
Here we use “Local” as example

## Slide 42: Step 3
Simulate the condition of cable issue or link down
Unplug ethernet cable between the connected AWK-1161A and the switch
AWK-1161A
AWK-1165A
AWK-1161C Wi-Fi Client
- - - connected - - -
Link down or cable issue
Server
Unable to access server
Client PC

## Slide 43: Step 4
Check Wi-Fi Client’s connection status
Verify if Wi-Fi Client connects to AWK-1165A and can still ping the server
AWK-1161C Wi-Fi Client
AWK-1161A
AWK-1165A
Link down or cable issue
Server
LFPT triggers WLAN OFF
- - - connected - - -
Can access server again
Client PC

## Slide 44: Step 5
Check AWK-1165A’s Event log
Reconnect ethernet cable between the originally connected AWK-1165A and the switch. Navigate to Diagnostics > Event Logs and Notifications > Event Log