## Slide 1
Introducing 6000 G2 series
Christian Gromeier | Stefan Czoer
Moxa Europe Technical Support
30.January 2025

## Slide 2: Agenda
Demo
What’s new on NPort 6000-G2
  Device Search Utility 3.0
  Dashboard
  Operation mode settings
  Maintenance
  Troubleshooting tools
  2-Way Installation
Why NPort 6000 G2?
Introducing 6000 G2 series
1
2
3

## Slide 3
Why NPort 6000 G2?
Introducing 6000 G2 series
1
Notes: Why do we need the NPort 6000-G2 Series? <CLICK>

## Slide 4: Why NPort 6000-G2?
Enhance Serial-To-Ethernet cybersecurity
Yet 2024, the cyber attack in critical facility continues to rise in past decades
Notes:   Our Goal is to ensure enhanced Security for IEC-62443 Compliance
  As an example, <CLICK>
  we remember about the Ukraine Power Grid Attack in 2015 where serial-to-Ethernet converter used in a power-grid attack resulted in a blackout affecting over 230,000 people
  <CLICK>
  As of 2024, cyber attacks in critical facilities continues to rise in the past decades

## Slide 5: Why Serial-to-Ethernet Cybersecurity Matters?
Select Secure Device
Protect Your Networks
Identify Network Status
Management
Device
Network
Holistic Security Strategy, aligned with IEC 62443
Engineering Station
SCADA Server
Application Server
Maintenance Server
IPC
Industrial PC
PLC
IED
HMI
PLC
Traffic Lights
Solar Panels
Switch Gears
Pumps
Conveyors
Robotic Arms
OT Network
MANAGEMENT
SUPERVISORY
CONTROL
Industrial Network
Industrial IPS/IDS
Industrial
Secure Router
Industrial IPS Firewall
Industrial
Ethernet
Switch
Network Management Software
Network Security Management
Industrial IPS/IDS
Industrial IPS/IDS
Serial Device Server
Remote I/O
Protocol Gateway
Industrial IPS/IDS
Industrial IPS/IDS
IT/Enterprise Network
Industrial Network
OT-IT Integrated Network Security Solution
Serial Device Server
Last mile to the equipment/device
Defense-in-depth for OT network security
Notes: The goal is to ensure that Moxa's product portfilio<CLICK>
includes IEC-62443<CLICK>. -compliant solutions also at the edge level <CLICK>.
This allows a robust cybersecurity protection even at the OT network edge. <CLICK>

## Slide 6
NPort 6000-G2 Series
1/2/4/8/16/32-port RS-232/422/485 Secure Serial Device Server
Features and Benefits
  Developed following Secure by Design Process
    Team certified for IEC 62443-4-1
    Product lifecycle / design following IEC 62443/NIS2/CRA
    IEC 62443-4-2 Secure Level 2 Certified*
  Secure Management
      Hardware Secure Boot that only runs trusted firmware & config
      User authentication w/ Role-based access control with first
      login process w/o default username & password
      Syslog for Incident Auditing
  Secure Communication
  Secured Serial Data Stream & Management Interface with encryption & authentication
  Strong Enough Encryption Method (ECC-256 = RSA 3072)
  Enterprise Integration
  Supporting remote syslog (RFC3164) for SIEM
  Supporting remote authentication server for with
  RADIUS/ TACACS+ server
  Continuous Service
  Continuous vulnerability & patch service
*will be certified by 2025/E with 4-32 port product launch
Product Launch Schedule
4 - 32 Port: Nov. 2025
Model Selection | Serial Port | Secure Boot | SD Card for Serial Buffer | Operating Temperature
NPort 6150-G2 | 1 | v | - | -10 – 60°C
NPort 6150-G2-T | 1 | v | - | -40 – 75°C
NPort 6250-G2 | 2 | v | v | -10 – 60°C
NPort 6250-G2-T | 2 | v | v | -40 – 75°C
Notes: The NPort 6000-G2 series is designed to meet IEC-62443 compliance for edge devices.
Key Features and Considerations: <CLICK>
  Compliant with IEC-62443-4-1:
  This Ensures that the design and development process aligns with the standards for secure product development lifecycle requirements.
  <CLICK>
  Secure Management: Facilitates secure configuration and control of devices.
    Secure boot,
    User authentication with role based access
    NPort 6000G2 removed HTTP, telnet and SSH console for security reason.
  <CLICK>
  Secure Communication
    Secured Serial Data Stream & Management Interface
    Strong encryption method
  <CLICK>
  Enterprise Integration
    Remote syslog for SIEM（Security Information and Event Management)
  <CLICK>
  Ongoing Maintenance and Vulnerability Patching
<CLICK>
We now launched The 1 and two port Nport 6K G2 series. Product Launch of 4 to 32 port devices is estimated in November
FIFO size 128(G1)>> 512(G2)

## Slide 7: NPort Security Design Comparison
 | NPort 6000 | NPort 6000-G2
User Profile | Systematic security for enterprise | 
Hardware Platform | Mature core chipset | Main-stream CPU with Secure Boot Capability for further upgrade
Secured Management | Access control (IP filtering) Local user authentication / log Forced changing default account/password (SB327) | Access control (IP filtering) Local user authentication / log Forced changing account/password (SB327) >> at least 8 characters
Secured Communication | Secure Operation Mode Secure Real COM Secure TCP Server TLS 1.2 HTTPS / SSH SNMP V3 Method support RSA 1024 | Secure Operation Mode Secure Real COM Secure TCP Server TLS 1.2 & Certificate authentication HTTPS with TLS v1.2* (v1.3 in 2025) SNMP V3 Support ECC 256 (= RSA 3072)
Enterprise Integration | Enterprise authentication RADIUS & TACACS+ One centralized syslog RFC 3164 | Enterprise authentication RADIUS & TACACS+ Dual centralized syslog with failover RFC 3164 Event format ISO8601 Timestamp
IEC 62443 Conformity | IEC 62443-4-2 FR Support | Secure by Design – IEC 62443-4-1 IEC 62443-4-2 SL2 Certified*
Vulnerability Service | Continue, but potential performance limitation | Continuous Service with capability for further upgrade
Notes: Here is a table, where you can compare the security design between NPort 6000 G1 and G2 series.
Including
ISO8601 Timestamp: Supports millisecond-level precision, compared to second level timestamp limitation of RFC3164
And Dual Centralized Syslog with Failover which Allows configuration of two Syslog servers for backup, ensuring reliability.

## Slide 8: Going Extra Mile on Product Performance
Boot-up 30% Faster
< 8 sec boot-up time to be ready
Faster & More Precise
40.5% lower latency
88.5% lower jitter variation
Serial-to-Ethernet Performance
Provisioning & Troubleshooting
Guided Quick Setup
RealCOM Quick Setup with Device Search Utility
Traffic Monitoring
Web-based traffic monitoring for both serial & Ethernet troubleshoot
Easy-of-Use Experience
2-way Installation
Classic front-mount & new side-mount for compact cabinet
New Web Console
Thematic re-category to find out all you need for Security, Maintenance
Notes: We are going the Extra Mile on product performance :
<CLICK>
Bootup time is 30% better than with Nport 6K G1
40.5 % lower read and write latency
88.5% lower jitter variation
<CLICK>
Guided Quick Setup
Traffic Monitoring
<CLICK>
2-way Installation ( front mount and new side- mount)
New Web Console
<CLICK>
<CLICK>
[Latency: Read + Write latency for 1 byte data in 9600, 8N1, FIFO disable
Jitter: Jitter in 1/32/64/128/256/512/1024 byte variation (highest – lowest) ]

## Slide 9
What’s new on NPort 6000-G2
  Device Search Utility 3.0
Why NPort 6000 G2?
Introducing 6000 G2 series
1
2
Notes: Now you are wondering what else is new on the new Nport 6000 G2 series? <CLICK>
Let’s start with Device search utility version 3.0

## Slide 10
New Device Search Utility (DSU) Setup Experience
Provisioning & Maintenance Tool
    Certificate Import
    Allowlist setting
COM 1
One-stop Real COM Setup Experience
    Search to Find New Unbox Device
    Setup Username/Password (First login process for security)
    Setup Device IP Address
    Driver COM mapping
Multiple Language Support
    English
    繁體中文
    简体中文
    日本語
    한국어
    Deutsch
    Français
    Русский
    Español
Notes: Based on research do over 50% of our customers use the NPort RealCOM mode. <CLICK>
  With DSU 3.0 A streamlined one-stop RealCOM mode configuration process will be introduced. <CLICK>
We added support for certificate import and allowlist settings. <CLICK>
Support for multiple languages.

## Slide 11: Device Search Utility 3.0
Notes: Key Updates in DSU 3.0:
  <CLICK>New Web UI
  With the new Device Search Utility (DSU) 3.0 we decided to include the <CLICK> NPort Windows Driver Manager as part of the download package. <CLICK>
  Import certificate and allowlist
Unlike previous versions, DSU 3.0 uses mDNS for safer device discovery.
That means the NPort 6000-G2 can only be detected using DSU 3.0; older versions of DSU cannot locate the NPort 6000-G2.

## Slide 12: Device Search Utility 3.0
mDNS protocol is used for searching devices in LAN.
Then TLS 1.2 handshake begins.
more secure
Notes: DSU3.0 uses mDNS multicast packets (_moxa._tcp.local) on Port 5353 to discover Moxa devices that support mDNS. <CLICK>
TLS handshake begins once Moxa devices(here NPort 6250-G2_C98CF4._moxa._tcp.local) are discovered.
DSU3.0 also sends <CLICK>UDP packets to Port 4800 for legacy devices (e.g., NPort 6000-G1) that do not support mDNS.

## Slide 13
What’s new on NPort 6000-G2
  Device Search Utility 3.0
  Dashboard
Why NPort 6000 G2?
Introducing 6000 G2 series
1
2

## Slide 14: Dashboard
Device status at a glance.
Notes: On the new WebUI we added a dashboard with an overview of the most important information and status of the new NPort 6000 G2 series.
The Dashboard will be shown immediately when logging in to the WebUI.

## Slide 15
What’s new on NPort 6000-G2
  Device Search Utility 3.0
  Dashboard
  Operation mode settings
Why NPort 6000 G2?
Introducing 6000 G2 series
1
2

## Slide 16: Operation Mode Settings
Notes: If the Customers is unsure which OP mode to use he can click on instructions <CLICK> in the web console for more information about the Operation modes.

## Slide 17: Operation Mode Settings
Notes: The new step-by-step Operation Mode configuration is designed to be more logical and user-friendly.
Just click on Configure on the right upper side <CLICK> and at first step you can select the mode you want to use.

## Slide 18: Operation Mode Settings
Notes: Now during the step-by-step setup, we illustrate now examples for each of the operation mode.
Similar to the configuration examples in MGate Manager, each mode provides diagrams showing the devices and traffic flow directions specific to that mode.

## Slide 19: Operation Mode Settings
Notes: Second Step is basic settings
<CLICK> Third Step Advanced settings which includes <CLICK> Connection Settings and <CLICK> Data Transmission settings <CLICK>
Finally, before confirming the new settings, you can see an overview of your new set operation mode

## Slide 20: Reorganized Operation Modes
Category | NPort 6000-G1 | Category | NPort 6000-G2
Disable | N/A |  | N/A
Device Control | Real COM |  | Real COM
 | RFC2217 |  | RFC2217
 | Reverse Real COM |  | Reverse Real COM
Socket | TCP Server | Socket | TCP Server
 | TCP Client |  | TCP Client
 | UDP |  | UDP
Pair Connection | Pair Connection Master | Pair Connection | Pair connection Client
 | Pair Connection Slave |  | Pair Connection Server
Reverse Terminal | Reverse Telnet |  | 
 | Reverse SSH |  | 
Terminal | Terminal (TERM_ASC) |  | 
 | SSH |  | 
Dial in/out | PPP |  | PPP
 | SLIP |  | SLIP
Unused operation modes are removed.
Terminal (TERM_BIN)
PPPD
SLIPD
Dynamic
Ethernet Modem
N/A
Printer RAW_PRN
LPT_PRN
Change of some Categories.
No Operation
COM-based Control
Connect Console
Connect Modem
Terminal
Reverse Terminal
Some Operation modes are reclassified for better clarity.
Max connections have been increased from 8 in G1 to 10 in G2.
Notes: With NPort 6000-G2 we reorganize the Operation Modes compared to Nport 6000 first Generation.
<click>We change Category names from
  <click > Disable to No Operation
  <click>. From Device Control to COM-based Control
  <click> Reverse terminal and terminal to Connect Console
  <click> Dial in/out to Connect Modem
<click> Unused operation modes are removed.
  <Click> Terminal (TERM_BIN), PPPD , SLIPD, Dynamic, Category: Ethernet Modem And Category Printer including RAW_PRN and LPD_PRN
<click> And we reclassified some Operation modes for better clarity
  <Click> Reverse telnet and Reverse SSH moved to Connect Console Reverse Terminal
  <Click> terminal ASC and SSH to Terminal
<click> Max connections have been increased from 8 in G1 to 10 in G2.

## Slide 21
What’s new on NPort 6000-G2
  Device Search Utility 3.0
  Dashboard
  Operation mode settings
  Maintenance
Why NPort 6000 G2?
Introducing 6000 G2 series
1
2

## Slide 22: NPort 6000-G1 configuration import
✅ Import NPort 6000-G1 configs to NPort 6000-G2.
✅ Import multi-port configs from NPort 6000 to fewer ports on NPort 6000-G2.
Notes: The NPort 6000-G2 is designed for a seamless transition from the NPort 6000-G1.
Key Feature: <CLICK>
  Supports importing NPort 6000-G1 configurations into the NPort 6000-G2. <CLICK>
  Allows configuration transfer from multi-port NPorts to models with fewer ports.
Note in FW 1.0.0:
  the configurations in NPort 6610 series cannot import to NPort6000-G2.
  If you import an OP mode that is no longer available in the NPort 6000-G2, the import will display as successful, but the affected port will show as "No Operation" in the NPort 6000-G2.

## Slide 23: Reset to customized default
Reset default to a customized configuration
Notes: Customers may prefer different default configurations instead of the factory settings.
With the NPort 6000-G2, customers can set a custom default configuration, allowing the device to reset to their preferred defaults instead of the factory settings.

## Slide 24
Why NPort 6000 G2?
Introducing 6000 G2 series
1
2
What’s new on NPort 6000-G2
  Device Search Utility 3.0
  Dashboard
  Operation mode settings
  Maintenance
  Troubleshooting tools
    One-Click Data Collection
    Traffic monitor
    Event Log

## Slide 25: What info should customer collect before opening a TS case?
One-Click Data Collection
Notes: If a device encounters an issue and the customer needs to contact Technical Support (TS), the One-Click Data Collection feature
  - Saves time for TS by streamlining the data collection process and it Reduces the risk of customers exporting incorrect data.
This feature helps TS and R&D teams with troubleshooting.
<CLICK>
Before exporting, an information consent notice is provided, detailing what information will be exported and ensuring the data is encrypted for secure transmission to TS.
The file size is approximately 100–200 KB.

## Slide 26: Realtime traffic Monitoring
Statistics Summary
Port Operation Mode/Connection Status
Ethernet & Serial Tx/Rx Count
Serial Error Count
1
2
3
Quick View & Status Check
Realtime Traffic Monitoring
Investigate & Troubleshoot
Select Port to Pinpoint Issue
Bidirectional Serial & Ethernet Packet
Export Detail Data in Files
1
2
3
Notes: For Advanced users to troubleshoot an issue on the Nport you need to see real-time data streams to identify the problem. <CLICK>
“Operation Mode Statistics” provides an overview for each serial port. <CLICK>
The Traffic Monitor feature allows users to view real-time traffic for individual serial or Ethernet ports. <CLICK>

## Slide 27: Event log
More types of event can be logged
Notes: With the new Eventlog, we increased the event types for a clear overview, what is happening on the Nport.

## Slide 28
Why NPort 6000 G2?
Introducing 6000 G2 series
1
2
What’s new on NPort 6000-G2
  Device Search Utility 3.0
  Dashboard
  Operation mode settings
  Maintenance
  Troubleshooting tools
  2-way Installation

## Slide 29: 2-Way Installation
New Side-mount Options
Classic
Notes: Mounting Options:
Beside the NPort 6000 G2 device servers includes a wall-mounting kit in the box, customer can also have a classic DIN-rail mounting kit.
As a new option, a side-mounting kit can be ordered separately, which helps to save space in a cabinet.

## Slide 30: 2-Way Installation
Notes: Finally, here you can see the drawings for both installations.

## Slide 31
Demo
What’s new on NPort 6000-G2
  Device Search Utility 3.0
  Dashboard
  Operation mode settings
  Maintenance
  Troubleshooting tools
Why NPort 6000 G2?
Introducing 6000 G2 series
1
2
3

## Slide 32: Questions?