## Slide 1
MX-NOS v5.0 MACsec
MTSC Product Session | May 2025
Alvaro Borges – Field Application Engineer (FAE)
Okan Guelder – Technical Support Engineer (TS)

## Slide 2: Agenda
Monitoring & Analysis
MKA Status View and Frame Analysis
1
2
3
DEMO
Overview of MACsec
Purpose, Benefits, and Standards
Use Cases & Topologies
Applications in Networks, Hop-by-Hop Protection
How MACsec Works Layer 2 Security, Threat Prevention, and Frame Format
4
6
5
Configuration & Keys
CKN/CAK Setup, Key Roles, and Best Practices

## Slide 3: MX-NOS Feature Lists
System/ Interface Management | V1.0 | Configuration Import / Export
 | V1.0 | Device Virtual Panel
 | V1.0 | IPv4 and IPv6 Management
 | V1.0 | SNMP v1/v2c/v3
 | V1.0 | SNMPv3 Trap
 | V1.0 | Account Management
 | V1.0 | Telnet/SSH
 | V1.0 | Console – CLI
 | V1.0 | Web UI
 | V1.0 | DHCP Client/Server
 | V1.0 | Email Warning
 | V1.0 | Event Notification
 | V1.0 | Ethernet Management Interface
 | V1.0 | Port Setting
 | V1.0 | Reset Button
 | V1.0 | System Health Monitor
 | V1.0 | TFTP
 | V1.0 | SFTP
 | V1.0 | PoE at/af
 | V2.0 | PoE bt
 | V2.0 | Jumbo Frame
 | V2.0 | Backup and Restore Storage
 | V4.0 | DHCP Relay Agent
 | V4.0 | DHCP Option 82
 | V5.0 | Multi. Language WebUI
VLAN Management | V1.0 | 802.1Q Bridge VLAN
 | V1.0 | GVRP
Multicast Application | V1.0 | IGMP Snooping v1/v2/v3
 | V1.0 | GMRP
 | V1.0 | Static Multicast
Time Management & Synchronization | V1.0 | Manual Time Settings
 | V1.0 | SNTP
 | V1.0 | NTP Server/Client
 | V1.0 | NTP Authentication
 | V3.0 | IEEE 1588 PTP
 | V4.0 | 1588 PTP Power Profile IEC 61850-9-3
 | V4.0 | 1588 PTP Power Profile C37.238-2017
Security Management | V1.0 | Login Authentication – Radius/TACACS+/Local account
 | V1.0 | Management Interface Control
 | V1.0 | Trusted Access Control
 | V1.0 | Authentication Certificate
 | V1.0 | IEEE 802.1X
 | V2.0 | Secure Boot
 | V1.0 | Traffic Storm Control
 | V1.0 | Port Security – Static Port Lock and MAC Sticky
 | V1.0 | Rate Limit – Disable Mode/Port Shutdown Mode
 | V2.0 | Online Account Monitor
 | V2.0 | Customer Key Management
 | V3.0 | Access Control List
 | V3.0 | MAC Authentication Bypass
 | V4.0 | 802.1x with 802.1 AR (Dev ID) compatible
 | V5.0 | 802.1x with 802.1 AE (MACsec)
 | V4.0 | DHCP Snooping
 | V4.0 | IP Source Guard
 | V4.0 | Dynamic ARP Inspection
 | V5.0 | Dynamic VLAN Assignment
Diagnostic | V1.0 | LLDP
 | V1.0 | Port Mirror(SPAN)
 | V1.0 | Event Log
 | V1.0 | Power Consumption Monitoring
 | V1.0 | System Resource Monitoring
 | V1.0 | Traffic Statistics
 | V1.0 | Bandwidth Utilization
 | V1.0 | Syslog
 | V1.0 | RMON
 | V1.0 | Ping
 | V1.0 | Secure System Diagnostics
 | V2.0 | SYSLOG Authentication
 | V4.0 | Remote Port Mirror (RSPAN)
 | V4.0 | Fiber Check
Industrial Protocol | V4.0 | Modbus TCP
 | V4.0 | EtherNet/IP
 | V5.0 | PROFINET
Quality Of Service | V1.0 | 802.1P/Default/DSCP Mapping
 | V1.0 | Egress Scheduler
 | V1.0 | Classification of QoS
 | V1.0 | Rate Limit and Shaper of QoS
 | V1.0 | Queue and Scheduler of QoS
L2 Redundancy | V1.0 | STP/RSTP
 | V1.0 | Turbo Ring v2
 | V1.0 | Turbo Chain
 | V1.0 | Redundant with Trunk Support
 | V1.0 | Static Port Trunk
 | V1.0 | Link Aggregation
 | V1.0 | BPDU Guard and BPDU FIlter
 | V1.0 | Dual-Homing
 | V1.0 | Link Healthy Check
 | V3.0 | Network Loop Protection
 | V3.0 | MSTP
 | V4.0/ V5.0 | MRP(Media Redundancy Protocol) MRP Interconnection (RC mode)
 | V5.0 | Tracking
 | V5.0 | Multiple Network coupling Multiple dual-Homing
 | V5.0 | PRP/HSR
L3 Unicast Routing | V2.0 | IP Interface
 | V2.0 | IPv4 on IP Interface
 | V2.0 | Static Route
 | V2.0 | OSPF
 | V2.0 | Unicast Routing Table
 | V2.0 | ARP Table
L3 Redundancy | V2.0 | VRRP
L3 Multicast Routing | V5.0 | Multicast Local Route
 | V5.0 | PIM-DM
 | V5.0 | PIM-SM
 | V5.0 | PIM-SSM
Power Substation | V3.0 | MMS
 | V5.0 | GOOSE Check
Others | V2.0 | Proxy ARP
Current Only Available on RKS-(G)4000 L3 models

## Slide 4
MACsec
(Media Access Control Security)
Protect the data on Ethernet networks. (encrypting and authenticating)
What does MACsec do?
Encrypts the data no one can read it.
Data Origin Authentication
Integrity
Confidentiality
MACsec is defined by two standards:
IEEE 802.1AE (for encryption)
IEEE 802.1X (for authentication)

## Slide 5
Where does MACsec work?
Works at Layer 2 (Data Link Layer)
Who uses MACsec?
Users who want to enhance their network security.
Why is MACsec important?
Stops hackers from eavesdropping and tampering.
Helps meet security rules and standards.
MACsec Overview: Function, Users, and Benefits

## Slide 6
Data Protection Through the OSI Layers
Data travels through 7 OSI layers — from sender to receiver and back.
Originally, the OSI and TCP/IP models had no built-in security.
Today’s cyber threats make security at each layer essential.
Application
Presentation
Session
Transport
Network
Data Link Layer
Application
 | OSI Layer | Security Protocol​ | What It Protects​
Layer 2 | Data Link​ | MACsec | confidentiality and integrity of transmitted data
Layer 3 | Network | IPSec | IP traffic by authenticating and encrypting IP Packets.
Layer 4 | Transport | TLS 1.3 | both endpoints of the session between a client a server

## Slide 7: Application Scenario
Source: https://iebmedia.com/technology/iiot/encryption-technology-provides-solutions-for-ethernet-security/
MACsec can secure switch to switch encrytion in LAN, when end devices do not support MACsec.

## Slide 8: MACsec in Action: Preventing Packet Sniffing and MitM Attacks
Man-in-the-Middle (MitM)
Packet Sniffing
Source: https://iebmedia.com/technology/iiot/encryption-technology-provides-solutions-for-ethernet-security/

## Slide 9: Value to clients of MACsec
Cost effective way in Layer 2 to take care of data integrity, confidentiality and authenticity during transmission.
Vendor-Neutral encryption protocol(IEEE standard IEEE802.1AE and 802.1X.).
MACsec provides high-speed encryption through hardware acceleration (Hardware mechanism compared to SW mechanism in IPsec).

## Slide 10: Design Concept: switch to switch (Point-to point MACsec v.s. End-to-end MACsec)
Point-to-point MACsec between directly linked switches:
  All switches in the data transmission line should be configured MACsec in between to protect the exchanged data.
End-to-end MACsec between switches (there are intermediate transparent transmission devices)
  SwitchC, SwitchD, and SwitchE are deployed between SwitchA and SwitchB, and point-to-point MACsec is configured between SwitchA and SwitchB to protect exchanged data.
Source: https://www.cisco.com/c/zh_tw/support/docs/routers/asr-1000-series-aggregation-services-routers/221079-troubleshoot-wan-macsec-on-routers.html
CRC remains in MACsec packets, so the intermediate switch w/o MACsec enabled can forward the MACsec frame.

## Slide 11
Protect the data on a hop-by-hop basis
Encrypted!
Decrypted!
Decrypted!
Encrypted!
Decrypted!
Encrypted!
Cleartext
Cleartext
Cleartext
Cleartext

## Slide 12: Design Concept: Pre-shared key for switches
MACsec
Key client
Key server
Share same CKN andCAK
Key server use CAK to generate SAK and notify Key client
Use SAK to encrypt Key server client.
CAK: Connectivity Association Key
CKN: Connectivity Association Key Name
SAK: Secure Association Key
SourceG: https://blogs.keysight.com/blogs/tech/traf-gen.entry.html/2020/07/30/macsec_mka_validatio-MqLY.html
Note: MACsec enable >> Restart , system will take 60s~100s to recover to normal operation.

## Slide 13: MACsec frame format

## Slide 14: Configuration Suggestion for different topologies.
Enable MACsec on every redundant port is must.

## Slide 15: Screenshot for MACsec frame

## Slide 16: Configuring MAC Security
To enable MAC security, under MAC security choose Enabled from the
dropdown menu, and then click Apply.
Security > Network Security > MAC security
Enable IEEE 802.1X is required to be enabled before enabling MACsec.
Enable MACsec for your
device.

## Slide 17: Configuring MAC Security
To configure MAC security on a given port, click the corresponding [Edit] and
then configure all of the following:

## Slide 18: Configuring MAC Security
Enable or disable MAC security for this port.
Specify the Connectivity association Key Name (CKN) to use for
the port.
Specify the Connectivity Association Key (CAK) to use for the
port.
Enable or disable specifying the port as a key server.
• Enabled: The port is a key server.
• Disabled: The port is a key client.

## Slide 19: Participant CKN/CAK Guideline
The CKN/CAK must match the connected port on the peer switch.
One CKN and one CAK are allowed per port.
CKNs/CAKs should not be reused on the same device.
Allowed caracters: letters(a-z, A-Z), numbers(0-9), @%^*()-_+={}[]:.,~$`.
CKNs/CAKs must be configured in pairs and cannot be partially configured
Deleting a CKN/CAK may also delete its corresponding CAK/CKN.

## Slide 20: Status Display: MACsec MKA Status
Display the other connected switch’s identity
Display the number of communication between the connected two switches.
Display the tunnel ID for the channel created between the two connected switches. Source port + mac address
There are two status for Peer List Type: Potential or LivePeerList.
  Potential Peer List: If the MI from senders cannot be recognized by receiver, the entry will be Potential Peer List.
  Live Peer List: If the MI from sender can be recognized by receiver and MN from sender is larger than MN recorded in receiver, the entry will be Live Peer List.

## Slide 21: DEMO
Turbo Ring V2
1/1
1/1
1/2
1/2
TAP
A
B
Wireshark
C
PC A
PC B

## Slide 22: DEMO
Turbo Ring V2
1/1
1/1
1/2
1/2
TAP
A
B
Wireshark
C
PC A
PC B
192.168.127.240
192.168.127.241
192.168.127.40
192.168.127.101