## Slide 1
5th February 2026
MGate MB3x70-G2 Introduction The Next Generation Modbus Protocol Gateway
Lubos Kucharek
Senior Technical Support Engineer

## Slide 2: Agenda
Modbus Overview
MGate & NPort in Modbus Applications
MGate MB3x70-G2 Series Introduction
Applications
Demo
Key Takeaways

## Slide 3: Modbus Overview

## Slide 4: Modbus Protocol & Key Benefits
Developed by Modicon, 1979
Transparency, Simplicity & Reliability
  Open standard protocol
  Standardized register access, Request / Response mechanism
  Built-in Exception Codes
REQUEST [Slave Address] [Function Code] [Data...]
NORMAL RESPONSE: [Slave Address] [Function Code] [Data...]
EXCEPTION RESPONSE [Slave Address] [Function Code + 0x80] [Exception Code]
Modbus Client (Master)
Modbus Server (Slave)

## Slide 5: New Learning Content Industrial Connectivity Foundations
Soft Launch & Survey
Content Enrolment
Mandatory to complete
before 6th March 2026
Q2/2026
Overview of Industrial Connectivity (MTC-CON-100 | 18 min)
Ethernet Based IO Basics (MTC-CON-105 | 15 min)
Serial Communication Fundamentals (MTC-CON-110 | 20 min)
Basics of Serial to Ethernet Technology (MTC-CON-115 | 25 min)
Introduction to Industrial Automation Protocols (MTC-CON-120 | 15 min)
Protocol Translation with Gateways (MTC-CON-125 | 22 min)
Modbus Overview (MTC-CON-130 | 15 min)
7 Lectures & 7 Quizzes & Survey
Login https://moxa.litmos.com.au
Home > My Training > Not Started

## Slide 6: MGate & NPort in Modbus Applications

## Slide 7: Upgrading Modbus Legacy Devices
Modbus RTU Application Client (Master)
Beginning
Power Meter Modbus RTU Server (Slave)
Serial
Problem?
1. Unable to connect physically
Modbus TCP Application Client (Master)
Power Meter Modbus RTU Server (Slave)
Serial
Ethernet
After Upgrade
2. The Modbus TCP application can not understand Modbus RTU.

## Slide 8: Selecting the NPort
Power Meter Modbus RTU Server (Slave)
Serial
Ethernet
Modbus RTU
TCP header
NPort add TCP header
“I don’t understand what is Modbus RTU + TCP header”
❌ Protocol-Agnostic – No Modbus awareness
❌ Frame Fragmentation – Splits Modbus frames across packets
❌ Timing Violations – Cannot maintain 3.5 character gaps
❌ CRC/Error Issues – Incomplete frames fail validation
❌ Intermittent Failures – Unreliable Modbus communication
❌ Basic Diagnostics – Generic serial troubleshooting only
“I cannot establish communication!”
“Communication works, but not stable!”
“Everything works fine, after firmware upgrade it doesn´t works anymore!”
Modbus TCP Application Client (Master)

## Slide 9: Moxa Recommends Select the MGate for Modbus
Modbus TCP Application Client (Master)
Power Meter Modbus RTU Server (Slave)
Serial
Ethernet
Modbus RTU
Modbus TCP
MGate translates
All Clear!
I am a super translator!
✓ Modbus-Aware – Understands protocol structure
✓ Frame Integrity – Guarantees complete frame delivery
✓ Timing Compliance – Maintains Modbus timing requirements
✓ Error Recovery – Modbus-specific handling & retry
✓ Reliable Operation – Consistent, predictable performance
✓ Protocol Diagnostics – Modbus-specific monitoring tools

## Slide 10: Selecting the Proper Product Line
Beginning
After Upgrade
Problem?

## Slide 11: Introduction to MGate MB3x70-G2

## Slide 12: Product Highlights – MGate MB3170/3270/3470-G2
MGate MB3170/3270/3470-G2 Family
1, 2, 4-port Advanced Modbus Gateway
Certifications
Features and Benefits
Supports high-performing and low-latency Agent Mode to actively poll Modbus devices and cache data
Supports Modbus serial extensions or proprietary serial for various devices
Supports route by TCP port or IP address for different system architectures
Supports Modbus serial client to Modbus serial server communications
Ethernet cascading or dual subnet for flexible network system design
Web based traffic monitoring/diagnostic information for easy troubleshooting
Various models for different scenarios: serial port with 2 kV isolation (-I models), wide temperature range of -40 to 75°C (-T models), and fiber Ethernet models
Developed according to IEC 62443-4-2 with Secure Boot
UL, CE, FCC, DNV*, ATEX*, C1D2*, IECEx*
*Currently undergoing certification, with completion planned by the end of June 2026

## Slide 13: MGate MB3170/3270/3470-G2 Appearance
2 Power Inputs (12~48VDC)
1 Relay Output
1 microSD Card (Config. Backup)
Reset Button
LED Indicators
Power status
Protocol status
TX/RX serial receive/transmit
1-2-4 Serial Interfaces
Modbus RTU/ASCII
Terminal block/ DB9 serial port
2 Ethernet Interfaces
Modbus TCP
MGate MB3170/3270/3470-G2 Family
1, 2, 4-port Advanced Modbus Gateway
DB9 serial port
Terminal block serial port

## Slide 14: Material Upgrade & Ports Layout
Generation 1
Generation 2

## Slide 15: Wide-temperature
Generation 1
Generation 2
Operating Temp.
0 ~ 60 °C
-40 ~ 75 °C (-T)
Operating Temp.
-10 ~ 60 °C
-40 ~ 75 °C (-T)

## Slide 16
Pull High/Low & Terminator Resistors
Software configurable

## Slide 17: New Features in G2

## Slide 18: Transparent mode
1
2
3
4
SCADA
Modbus TCP
Modbus RTU
Transparent Conversion
Ethernet
Serial
Available since
MGate MB3000 Series “1st Generation”
“On-the-fly” protocol translation
Modbus Client (Master)
Modbus Server (Slave)
G a t e w a y
Request
Response
Ethernet
Serial

## Slide 19: Agent Mode for Better Performance
1
2
SCADA
Modbus TCP
Modbus RTU
Ethernet
Serial
A
B
Agent Mode
MGate will be an agent to collect data for you
MGate actively polls the device and caches the data
The SCADA gets data from MGate immediately
Available since
MGate 5000 Series
MGate MB3x70 Series – 2nd Generation
Active “polling” to refresh a Data Table
Modbus Client (Master)
Modbus Server (Slave)
G a t e w a y
Response
Ethernet
Serial
Request
Request
INTERNAL MEMORY
Response

## Slide 20: Specifications
Product Highlights
Roles: Client/Server
Function supported: 1, 2, 3, 4, 5, 6, 15, 16, 23
Max No. of cmd: 128 (per connection or serial port)
Tags/Total tag size:
  MB3170: 150 / 2048 bytes
  MB3270: 300 / 3072 bytes
  MB3470: 600 / 4096 bytes
Modbus TCP/ RTU/ASCII (Agent)
Mode: Request/Response, Produce/Consume
Max No. of cmd: 128 (per serial port)
Tags/Total tag size:
  MB3170: 150 / 2048 bytes
  MB3270: 300 / 3072 bytes
  MB3470: 600 / 4096 bytes
Proprietary Serial (Agent)
MGate MB3170/3270/3470-G2 Family
1, 2, 4-port Advanced Modbus Gateway

## Slide 21: From Modbus Registers to Tags How MGate Use The Memory
Modbus Registers
Tags
Internal Memory

## Slide 22: Specifications
MGate MB3170/3270/3470-G2 Family
1, 2, 4-port Advanced Modbus Gateway
Support Transparent Mode
Support Modbus TCP client/server
Support Modbus RTU client/server
Support Ethernet cascade
Existing Features
Provides a variety of connectivity up to 4 Serial ports
  Serial connector: DB9、terminal block
  Ethernet connector: RJ45、optical fiber
Support Agent Mode
Support Dual Subnet
Support Proprietary Serial client
Web-built-in testing tools
Secure Boot, developed per IEC 62443-4-2
New Features
Features are already supported in G1 models
New supported features in G2 models

## Slide 23: Use in Different Subnets Dual IP LAN Mode
Flexible System Architecture
Modbus TCP devices can belong to different subnets by using dual IP in MGate
Modbus TCP
Modbus RTU/ASCII
Real COM
Modbus TCP
Modbus RTU/ASCII
Real COM
MGate
Client
Server
Can belong to different subnets

## Slide 24: Graphical Topology

## Slide 25: Proprietary Serial Device Concept
Non-standard Modbus and Serial Proprietary to Modbus TCP conversion
  Supports Agent mode
  Simultaneously with standard Modbus RTU/ASCII Server
Supported Modes
  Request / Response = Time-Based (Scheduled/Periodic)
  Produce / Consume = Time-Independent (Continuous/Event-Based)
Modbus TCP
Client
Serial Proprietary Server
and / or
Data cached in MGate for active polling
New Supported Architecture
Modbus RTU/ASCII Server

## Slide 26: Proprietary Serial Settings The Frame Format
Take the response of the Modbus RTU function code 03 as an example
The function block settings would be:
Function Code
Slave ID
Byte Count
Data
CRC
Supports 4 Function Blocks
  Node Address: Like Device ID
  Constant: A tag with a fixed length and an unchanging value
  Data: A tag with a fixed length but a variable value
  Checksum: Used for checksum calculation

## Slide 27: Troubleshooting

## Slide 28
Configuration & Monitoring
Basic configuration
  Web console (No MGate Manager)
  Moxa Windows Driver Manager v3.7/4.4 (Real COM, Proprietary Serial)
For mass configuration
  Device Search Utility v3.0 or newer
  CLI Tool
  MXconfig
Monitoring
  MXview One Series

## Slide 29: Clear Overview with Dashboard

## Slide 30: Traffic Monitor

## Slide 31: Trouble Shooting New Build-in Diagnostic Tools
No additional tools need to be installed for testing

## Slide 32: Trouble Shooting New Build-in Diagnostic Tools
One click diagnostic information log collection

## Slide 33: Reliable Protection

## Slide 34
First-time Login
Import Configuration
  Configuration backup file from MGate MB3000 1st generation or MGate MB3000-G2
The same default IP address
  https://192.168.127.254
Create Account and Password
  No default account/password

## Slide 35: Cybersecurity Compliance Developed according to IEC 62443-4-2 with secure boot
Modbus TCP
Modbus RTU
Meters
SCADA

## Slide 36: Reliable Protection Secure boot
Generation 1
Generation 2
Bootloader
OS
Unsigned software with Hash Code
AC5WBCEIL:AKLEO
CPU
Bootloader
OS
AC5WBCEIL:AKLEO
CPU
Moxa
Sign Service
Signed
Software with Hash Code
Moxa
Software Engineer
Use Moxa Sign Service to sign the software and release the signed software and the corresponding public key to manufacture.
Moxa Factory

## Slide 37: Why choose the MGate 3x70-G2?
Ease-of-Use
Better Performance
Reliable Protection
Guided Quick Setup
Graphical topology setup—no advanced protocol knowledge required
One-click import from generation 1 device
Connector Options
ST/SC and SFP fiber options, with additional RJ45 port
Serial port with DB9 and TB options
Troubleshooting
Web-based traffic monitor and protocol diagnostics
Web built-in Modbus testing tool
Higher Performance
Agent Mode for active polling end devices and cache data in MGate
Broader Applications
Non-standard Modbus and serial Proprietary to Modbus TCP conversion
Cybersecurity DNA
Hardware secure boot
Security features compliant with IEC62443-4-2
Stronger encryption algorithm: SHA-256, SHA-384, RSA-3072, RSA-4096

## Slide 38: Applications

## Slide 39: TOP 5 Target Market & Applications
Chart: 
| Data Centers | Marine | Power Transmission and Distribution | Power Generation | Oil and gas | Others
銷售 | 0.5049 | 0.1057 | 0.0753 | 0.059 | 0.0572 | 0.1979
Others
Data Center
Switchgear
ATS (Automated Transfer Switch)
Power distribution or performance monitoring
Marine/Ship
Power monitoring
Environment monitoring
Oil and Gas
Upstream monitoring
Power Transmission and Distribution
AWR (Automated Meter Reading)
Feeder automation
Power monitoring in substation
Power Generation
Power monitoring

## Slide 40: Demo

## Slide 41: Moxa Tech Note: The Migration Guide for the MGate MB3170-G2 & MB3270-G2
https://www.moxa.com/en/products/industrial-edge-connectivity/protocol-gateways/modbus-tcp-gateways/mgate-mb3170-g2-mb3270-g2-mb3470-g2-series#resources

## Slide 42: Key Takeaways
The New MGate MB3x70-G2 supports
  Up to 4 serial interfaces (DB9/Terminal block)
  Agent mode + Proprietary device
  Dual IP expands application possibilities
  Web-based configuration (No MGate Manager)
  Developed according to IEC 62443-4-2 with secure boot
  Migration Guide from G1 to G2
Industrial Connectivity Foundations,
  Follow-up e-learning (due by 6 March)
Modbus in use? Moxa recommends
  MGate guarantees frame integrity, reliable communication and advanced diagnostics
  Choose the device designed for the job