## Slide 1
NPort IA5000-G2 Series
Christian Gromeier
Moxa Europe Technical Support
5. February 2026

## Slide 2: Agenda
Demo
What’s new on NPort IA5000-G2
  Device Search Utility 3.x
  Dashboard
  Operation mode settings
  Maintenance
  Troubleshooting tools
Why NPort IA5000 G2?
NPort IA5000 G2 Series
1
2
3

## Slide 3
Why NPort IA5000 G2?
NPort IA5000 G2 Series
1

## Slide 4: Edge Security Challenges - Authentication
Machine B
Legacy Design
The Device is using default credential or Never change password with all admin right…
“Ouch! I want to access machine A but accidently configure machine B and stop the process!”
“Hehe! I social phishing to get the OT network access! Let me try all the devices credential to steal data and blackmail to sabotage!”
Machine B
Attacker
OT network
workstation
Username: abcd
Password: abcd
Secure Design
Role-based-access-control (RBAC) with minimum privilege and no default username/password design
“Oh, I only have view right on this device that I cannot modify (or I can’t login; I must use the wrong one)”
“Oh, it seems this device has no default credential exposed online, and the username password is strong enough!”
Other Crew
Machine A
Attacker
workstation
Only the authorized staff has the designated privilege by account based
No default credential. New First login design to setup credential (batch supported)
Other Crew
Machine A
Machine out of service
by accident or intent

## Slide 5: Edge Security Challenges – Logging on Incident
Legacy Design
User A
1. Setup Config a.
SCADA
2. Setup Connect a.
Attacker
3.
Try to login to
Setup Config b.
Setup Connect b.
Auditor
Periodic manual retrieve System Log
User A
1. Setup Config a.
SCADA
2. Setup Connect a.
Attacker
3.
Try to login to Setup Config b.
Setup Connect b.
In-time Response to suspicious incident
Complete syslog for NIS2 audit
SNMPv3 Trap/Inform
1/1/1970 system start
1/1/1970 system restart
1/1/1970 system restart
</empty>
Few or NO system incident are record on syslog
2025/3/11 09:05 system start
2025/3/11 09:07 user A login from IP ..
2025/3/11 09:32 user A update config
2025/3/11 10:47 SCADA connect to a.
2025/3/11 19:57 Login failure from IP
…
Secure Design
Complete incident detail with local syslog database
Risk: Failing NIS2 Security Incident Report Responsibility
(Precise time, sequence, event)
Auditor
Access NPort to monitor/review the syslog

## Slide 6: Edge Security Challenges – Data Encryption
Legacy Design
The Field Data Are Transmitted in Plain Text
Secure Design
Field Data Encrypted and Authenticated with NPort
abc
abc
abc
abc
Infected node in OT network
abc
SCADA Room
Man-in-the-middle
Silence theft of production data
False Value to Sabotage
Lost Remote Control Capability
***
abc
Infected node in OT network
SCADA Room
CA
CA
***
abc
***
***
Only authorized user can setup serial data tunnel (CA Exchange)
Strong Cipher Suite with RSA4096 or ECC521
Protect sensitive production data integrity
Hard to aware until consequences observed

## Slide 7: How NPort IA5000-G2 Can Secure the Edge?
Preventing Unauthorized Access
Only the authorized staff has the designated privilege by account group based
First Login to setup credential
Visibility & Reinforce Systemic Security
In-time Response to suspicious incident
Complete syslog for NIS2 audit
Maintaining Data Integrity
Only authorized user can setup serial data tunnel (CA Exchange)
Strong Cipher Suite with RSA4096 or ECC521
Protect sensitive production data integrity

## Slide 8: Introducing the NPort IA5000-G2 Series

## Slide 9: Product Introduction – NPort IA5100/IA5200/IA5400-G2
DB9 serial port
NPort IA5100/5200/5400-G2 Family
1/2/4-port RS-232/422/485 Serial Device Server for Industrial Automation
Certifications
Features and Benefits
  Design by Secure, IEC 62443-4-2 SL2 compliant
  Secure Management
      Hardware Secure Boot that only runs trusted firmware and configuration
      User authentication using role-based access control (RBAC)
      First login process without default username and password
  Secure Communication
  Secured serial data stream and management interface with encryption and extra authentication on G2
  Easy Installation
  Ethernet cascading or dual subnet for flexible network system design
  Web based traffic monitoring/diagnostic information for easy troubleshooting
  Continuous Service
  Continuous commitment to addressing and patching vulnerabilities
UL, CE, FCC, DNV*, ATEX*, C1D2*, IECEx*
Terminal block serial port
Ethernet ports
with dual subnet
*Pending approval. Refer to the product datasheet for the latest certification status.

## Slide 10: NPort Security Design Comparison
 | NPort IA5000/IA5000A | NPort IA5000-G2 | NPort 6000-G2
User Profile | Device self-protection for small/medium business | Device self-protection for small/medium business (hazardous zones) | Systematic security for enterprise
Hardware Platform | Mature core chipset | Main-stream CPU with Secure Boot Capability for further upgrade | Main-stream CPU with Secure Boot Capability for further upgrade
Secured Management | Access control (IP filtering) Local user authentication / log | Access control (IP filtering) Local user authentication / log Forced changing default account/password (SB327) | Access control (IP filtering) Local user authentication / log Forced changing default account/password (SB327)
Secured Communication | HTTPS (For 5000A, 5400, 5600 Series) SNMP V3 (For NPort 5400 & 5600 Series) | Secure Operation Mode Secure Real COM (driver) Secure TCP Server (socket) TLS 1.2 & Certificate authentication HTTPS with TLS v1.2 SNMP V3 Supports up to RSA 4096 (or ECC 521= RSA 15360) | Secure Operation Mode Secure Real COM (driver) Secure TCP Server (socket) TLS 1.2 & Certificate authentication HTTPS with TLS v1.2* (v1.3 in 2025) SNMP V3 Supports up to RSA 4096 (or ECC 521= RSA 15360)
Enterprise Integration | Local database for authentication Local syslog with: RFC 3164 Event format ISO8601 Timestamp | Local database for authentication Local syslog with: RFC 3164 Event format ISO8601 Timestamp | Enterprise authentication RADIUS & TACACS+ Dual centralized syslog with failover RFC 3164 Event format ISO8601 Timestamp
IEC 62443 Conformity | IEC 62443-4-2 FR Support | Secure by Design – IEC 62443-4-1 IEC 62443-4-2 SL2 compliant | Secure by Design – IEC 62443-4-1 IEC 62443-4-2 SL2 Certified*
Vulnerability Service | Continue, but potential performance limitation | Continuous Service with capability for further upgrade | Continuous Service with capability for further upgrade
Notes: Compared to Nport 6000-G2, Nport 5000-G2 does not support dual way mounting, only DIN rail

## Slide 11: NPort IA5000/IA5000A vs NPort IA5000-G2
 |  | NPort IA5000 | NPort IA5000A | NPort IA5000-G2
Portfolio | Models available | No. of serial ports: 1 or 2 Serial port connector: DB9 Fiber option (10/100M): M-SC, M-ST, S-SC | No. of serial ports: 1, 2 or 4 Serial port connector: DB9 | No. of serial ports: 1, 2, or 4 Serial port connector: DB9, Terminal block (2, 4-port model) Fiber option (10/100M): M-SC, M-ST, S-SC, SFP
Performance | Operation mode | Real COM, TCP Server/Client, UDP, RFC2217, Pair Connection, Reverse Telnet |  | Real COM, TCP Server/Client, UDP, RFC2217, Pair Connection, Reverse Telnet Secure Real COM, Secure TCP Server/Client, Secure Pair Connection
Reliability | EMC level | EN 55032 / EN 55035 (Commercial EMC) |  | EN 61000-6-2 / EN 61000-6-4 (industrial EMC)
 | Security | Authentication and HTTPS/SNMPv3 for NPort management |  | Hardware-based secure boot and security features compatible with IEC 62443-4-2
Ease-of-use | Network architecture | Single subnet (switch) | Single subnet (switch), Dual subnet | Single subnet (switch), Dual subnet
 | Trouble-shooting | Network / serial status monitor |  | Real time traffic monitor, one-click information download, fiber-diagnostics (web-based) Serial port monitor (web, Moxa MXview One)

## Slide 12
What’s new on NPort IA5000-G2
  Device Search Utility 3.x
Why NPort IA5000 G2?
NPort IA5000 G2 Series
1
2

## Slide 13
New Device Search Utility (DSU) Setup Experience
Provisioning & Maintenance Tool
    Certificate Import
    Allowlist setting
COM 1
One-stop Real COM Setup Experience
    Search to Find New Unbox Device
    Setup Username/Password (First login process for security)
    Setup Device IP Address
    Driver COM mapping
Multiple Language Support
    English
    繁體中文
    简体中文
    日本語
    한국어
    Deutsch
    Français
    Русский
    Español

## Slide 14: Device Search Utility 3.x
Notes: Key Updates in DSU 3.1:
  <CLICK>New Web UI
  With the new Device Search Utility (DSU) 3.1 we decided to include the <CLICK> NPort Windows Driver Manager as part of the download package. <CLICK>
  Import certificate and allowlist
Unlike previous versions, DSU 3.x uses mDNS for safer device discovery.
That means the NPort IA5000-G2 can only be detected using DSU 3.x; older versions of DSU cannot locate the NPort IA5000-G2.

## Slide 15: Device Search Utility 3.x
mDNS protocol is used for searching devices in LAN.
Then TLS 1.2 handshake begins.
more secure
Notes: DSU3.x uses mDNS multicast packets (_moxa._tcp.local) on Port 5353 to discover Moxa devices that support mDNS. <CLICK>
TLS handshake begins once Moxa devices(here NPort 6250-G2_C98CF4._moxa._tcp.local) are discovered.
DSU3.x also sends <CLICK>UDP packets to Port 4800 for legacy devices (e.g., NPort 6000-G1) that do not support mDNS.

## Slide 16
What’s new on NPort IA5000-G2
  Device Search Utility 3.x
  Dashboard
Why NPort IA5000 G2?
NPort IA5000 G2 Series
1
2

## Slide 17: Dashboard
Device status at a glance.
Notes: On the new WebUI we added a dashboard with an overview of the most important information and status of the new NPort IA5000 G2 series.
The Dashboard will be shown immediately when logging in to the WebUI.

## Slide 18
What’s new on NPort IA5000-G2
  Device Search Utility 3.x
  Dashboard
  Operation mode settings
Why NPort IA5000 G2?
NPort IA5000 G2 Series
1
2
Notes: We have some changes in the Operation Mode settings

## Slide 19: Operation Mode Settings
Notes: If the Customers is unsure which OP mode to use he can click on instructions <CLICK> in the web console for more information about the Operation modes.

## Slide 20: Operation Mode Settings
Notes: The new step-by-step Operation Mode configuration is designed to be more logical and user-friendly.
Just click on Configure on the right upper side <CLICK> and at first step you can select the mode you want to use.

## Slide 21: Operation Mode Settings
Notes: Now during the step-by-step setup, we illustrate now examples for each of the operation mode.

## Slide 22: Operation Mode Settings
Notes: Second Step is basic settings
<CLICK> Third Step Advanced settings which includes <CLICK> Connection Settings and <CLICK> Data Transmission settings <CLICK>
Finally, before confirming the new settings, you can see an overview of your new set operation mode

## Slide 23
What’s new on NPort IA5000-G2
  Device Search Utility 3.x
  Dashboard
  Operation mode settings
  Maintenance
Why NPort IA5000 G2?
NPort IA5000 G2 Series
1
2

## Slide 24: NPort IA5000 G1 configuration import
✅ Import NPort IA5000-G1 configs to NPort IA5000-G2.
✅ Import multi-port configs from NPort IA5000 to fewer ports on NPort IA5000-G2.
Notes: The NPort IA5000-G2 is designed for a seamless transition from the NPort IA5000-G1.
Key Feature: <CLICK>
  Supports importing NPort IA5000-G1 configurations into the NPort IA5000-G2. <CLICK>
  Allows configuration transfer from multi-port NPorts to models with fewer ports.

## Slide 25: Reset to customized default
Reset default to a customized configuration
Notes: Customers may prefer different default configurations instead of the factory settings.
With the NPort IA5000-G2, customers can set a custom default configuration, allowing the device to reset to their preferred defaults instead of the factory settings.

## Slide 26
Why NPort IA5000 G2?
NPort IA5000 G2 Series
1
2
What’s new on NPort IA5000-G2
  Device Search Utility 3.x
  Dashboard
  Operation mode settings
  Maintenance
  Troubleshooting tools
    One-Click Data Collection
    Traffic monitor
    Event Log

## Slide 27: Before opening a Technical Support case?
One-Click Data Collection
Notes: If a device encounters an issue and the customer needs to contact Technical Support (TS), the One-Click Data Collection feature
  - Saves time for TS by streamlining the data collection process and it Reduces the risk of customers exporting incorrect data.
This feature helps TS and R&D teams with troubleshooting.
<CLICK>
Before exporting, an information consent notice is provided, detailing what information will be exported and ensuring the data is encrypted for secure transmission to TS.
The file size is approximately 100–200 KB.

## Slide 28: Realtime traffic Monitoring
Statistics Summary
Port Operation Mode/Connection Status
Ethernet & Serial Tx/Rx Count
Serial Error Count
1
2
3
Quick View & Status Check
Realtime Traffic Monitoring
Investigate & Troubleshoot
Select Port to Pinpoint Issue
Bidirectional Serial & Ethernet Packet
Export Detail Data in Files
1
2
3
Notes: For Advanced users to troubleshoot an issue on the Nport you need to see real-time data streams to identify the problem. <CLICK>
“Operation Mode Statistics” provides an overview for each serial port. <CLICK>
The Traffic Monitor feature allows users to view real-time traffic for individual serial or Ethernet ports. <CLICK>

## Slide 29: Event log
More types of event can be logged
Notes: With the new Eventlog, we increased the event types for a clear overview, what is happening on the Nport.

## Slide 30: Network Management Integration with MXview One
Serial Status Visibility
Topology/event display and alert
User-defined threshold (Tx/Rx/Parity, CRC, frame error)
Minimizing Downtime
Saves troubleshooting efforts between Ethernet and serial
Serial device link down, not responding, interface/data error
Serial Port Monitoring
Security View
Device Security Status
Oversees security status and spots unsecure settings
Configure and Protect
Updates unsecure services on MXview One and protects overall network security
Patch Management
Keep Device Updated
Automated online check for the most recent device firmware along with a security patch suggestion and release notes
Schedule and Sequence
Schedules firmware updates based on chosen maintenance time
Sequential update based on network topology

## Slide 31
Demo
What’s new on NPort IA5000-G2
  Device Search Utility 3.x
  Dashboard
  Operation mode settings
  Maintenance
  Troubleshooting tools
Why NPort IA5000 G2?
NPort IA5000 G2 Series
1
2
3

## Slide 32: NPort IA5000 G2 Demo Topology
Ethernet
Serial
Local Network
Machine A (Simulated)
Serial COM
NPort IA5450 G2
Ethernet to Serial
Application using Serial COM Port
(RealCOM)
Machine B (Optional)
Serial COM
Machine C (Optional)
Serial COM
Notes: Machine or Sensors which has a Serial COM port for communication
Legacy Application running on a PC which needs to communicate via Serial Port with the Device
Using existing Ethernet Network infrastructure
-> Solution NPort IA5450 G2 series with RealCOM operation mode

## Slide 33: NPort IA5000 G2 Demo
Initial Configuration (for RealCOM operation mode)
On PC running the application
  Install NPort Driver (NPort Driver Manager)
    Install DSU (Device Search Utility) comes with NPort Driver Manager included.
    DSU can help to preconfigure NPort by uploading an existing configuration or set Initial IP address
  Configure NPort Driver Manager
    Map the NPort (IP and Serial Port) to a local COM port
On NPort
  Upload existing preconfigured configuration file, or
    Can be done also via DSU utility
  Start with clean factory settings
    Set Network parameter, like IP address …
    Selecting the Operation Mode, like RealCOM
    Select Serial Port Interface Mode like RS232 or RS485
Ready for Application to use the mapped COM port

## Slide 34: Initial Configuration
Config RealCOM mode
Follow the following video for setting RealCOM mode
https://www.moxa.com/en/videos/nport-g2-quick-install
https://www.moxa.com/en/videos/nport-g2-web-guide
Notes: Based on previous surveys, over 50% of customers use RealCOM mode.
To address this, the NPort IA5000-G2 carton packaging includes a QR code linking to a RealCOM mode setup tutorial video. Customers can immediately see it upon opening the box and follow the instructions for setup.

## Slide 35: Initial Configuration
https://www.moxa.com/en/videos/nport-g2-quick-install
https://www.moxa.com/en/videos/nport-g2-web-guide

## Slide 36: NPort IA5450-G2 Demo
Initial Configuration with DSU (Device Search Utility)
Discover NPort
  Unlock NPort
Assign IP address
Configure NPort
  By Web UI (Console) or,
  By Uploading Configuration from
  DSU

## Slide 37: NPort IA5450-G2 Demo
Existing configuration file from previous NPort IA5450 series generation

## Slide 38: NPort IA5450-G2 Demo
Map serial COM port

## Slide 39: NPort IA5450-G2 Demo Troubleshooting
Simplified setup with PComm
Ethernet
Serial
Machine A (Simulated)
Serial COM
NPort IA5450-G2
Ethernet to Serial
PComm using Serial COM Port
RealCOM
PComm using Serial COM Port
UPort USB to Serial Adapter

## Slide 40: NPort 6250 G2 Demo
Troubleshooting, PComm
Terminal connected to
UPort
Terminal connected to
NPort IA5450-G2 Port 1

## Slide 41: NPort 6250 G2 Demo
Troubleshooting, Traffic Monitor

## Slide 42: NPort 6250 G2 Demo
Extended Troubleshooting, Diagnostic Information
Export the Diagnostic Information and send it to Moxa Technical Support with description of the failure details and the expected behavior.
Ideally with a description (including topology drawing) helping to reproduce the problem in our own lab.

## Slide 43: Questions?