## Slide 1
Alvaro Borges
Okan Gülder
Technical Support Engineer
March 2026
MTSC 2026
MAC-SEC
Syslog over TLS
Access Control List (ACL)
Field Application Engineer

## Slide 2: Agenda
1
2
3
4
ACL Basics — Port/VLAN, Ingress/Egress
ACL Configuration — Rules, DSCP/Redirect, Status, Hands-on
MACsec Overview — Purpose, Benefits, Standards
How MACsec Works — Layer 2 Protection, Frame/MKA, Keys (CKN/CAK)
6
Syslog Basics & Security Problem
Syslog over TLS — Certificates, Setup, Verification, Hands-on
5
MACsec Operations — Use Cases, Monitoring, Demo
7

## Slide 3
MACsec

## Slide 4
MACsec
(Media Access Control Security)
Protect the data on Ethernet networks. (encrypting and authenticating)
What does MACsec do?
Encrypts the data no one can read it.
Data Origin Authentication
Integrity
Confidentiality
MACsec is defined by two standards:
IEEE 802.1AE (for encryption)
IEEE 802.1X (for authentication)

## Slide 5
Where does MACsec work?
Works at Layer 2 (Data Link Layer)
Who uses MACsec?
Users who want to enhance their network security.
Why is MACsec important?
Stops hackers from eavesdropping and tampering.
Helps meet security rules and standards.
MACsec Overview: Function, Users, and Benefits

## Slide 6: MACsec in Action: Preventing Packet Sniffing and MitM Attacks
Man-in-the-Middle (MitM)
Packet Sniffing
Source: https://iebmedia.com/technology/iiot/encryption-technology-provides-solutions-for-ethernet-security/

## Slide 7
Protect the data on a hop-by-hop basis
Encrypted!
Decrypted!
Decrypted!
Encrypted!
Decrypted!
Encrypted!
Cleartext
Cleartext
Cleartext
Cleartext

## Slide 8: MACsec frame format

## Slide 9: Configuration Suggestion for different topologies.
Enable MACsec on every redundant port is must.

## Slide 10: Screenshot for MACsec frame

## Slide 11: Configuring MAC Security
To enable MAC security, under MAC security choose Enabled from the
dropdown menu, and then click Apply.
Security > Network Security > MAC security
Enable IEEE 802.1X is required to be enabled before enabling MACsec.
Enable MACsec for your
device.

## Slide 12: Configuring MAC Security
To configure MAC security on a given port, click the corresponding [Edit] and
then configure all of the following:

## Slide 13: Configuring MAC Security
Enable or disable MAC security for this port.
Specify the Connectivity association Key Name (CKN) to use for
the port.
Specify the Connectivity Association Key (CAK) to use for the
port.
Enable or disable specifying the port as a key server.
• Enabled: The port is a key server.
• Disabled: The port is a key client.

## Slide 14: Participant CKN/CAK Guideline
The CKN/CAK must match the connected port on the peer switch.
One CKN and one CAK are allowed per port.
CKNs/CAKs should not be reused on the same device.
Allowed caracters: letters(a-z, A-Z), numbers(0-9), @%^*()-_+={}[]:.,~$`.
CKNs/CAKs must be configured in pairs and cannot be partially configured
Deleting a CKN/CAK may also delete its corresponding CAK/CKN.

## Slide 15: Status Display: MACsec MKA Status
Display the other connected switch’s identity
Display the number of communication between the connected two switches.
Display the tunnel ID for the channel created between the two connected switches. Source port + mac address
There are two status for Peer List Type: Potential or LivePeerList.
  Potential Peer List: If the MI from senders cannot be recognized by receiver, the entry will be Potential Peer List.
  Live Peer List: If the MI from sender can be recognized by receiver and MN from sender is larger than MN recorded in receiver, the entry will be Live Peer List.

## Slide 16
Syslog over TLS for MX-NOS Switches
March 2026

## Slide 17
What is Syslog?
A standard way to send log messages
From a device (client) to a server
Lets you collect all logs in one place
Example log server: rsyslog (Ubuntu)

## Slide 18
The Problem: Syslog is Not Secure
Not Reliable: Uses UDP (Port 514). Messages can be lost.
Not Encrypted: Uses Plaintext.
Big Risk: Anyone can read your secret logs (like login failures).

## Slide 19
The Solution: Syslog over TLS (TCP/6514)
TLS = Transport Layer Security (Like HTTPS for websites)
Why it's the Solution?
Privacy: Locks your data.
Integrity: No one can change the log.
Reliability: All logs arrive safely.
Authentication: Proves the server and switch are real.

## Slide 20
The "ID Cards" for TLS: What are Certificates?
We need digital "ID Cards" to prove who we are.
    The CA (Certificate Authority):
      The "Passport Office“
    The Server Certificate:
      The Server's ID Card
    The Client Certificate:
      The Switch's ID Card
      Secret Files: .key files are the Private Keys. Keep them secret!

## Slide 21
How We Create These Certificates
Openssl
Step 1: Create the CA (Certificate Authority)
Step 2: Create the Server’s Certificate
Step 3: Create the Switch’s Certificate
Step 4: Use the CA (from Step 1) to sign the ID cards from Steps 2 and 3.
Software Library

## Slide 22
Goal: Listen for secure connections.
Port: TCP/6514
Config File: /etc/rsyslog.conf
Actions:
  Load the TLS module (gtls).
  Add paths to the CA, Server Certificate, and Server Key files.
  Tell it to listen on port 6514.
  Use a template to sort logs by IP.
Configure rsyslog on Ubuntu

## Slide 23
Configure the Moxa RKS-G4000 Series Switch
Sync Time:
Go to System > System Time
Set the correct Time and Time Zone

## Slide 24
Configure the Moxa RKS-G4000 Serie Switch (Cont.)
Upload Certificates: Create the Client's ID Card
Go to Event Logs and Notifications > Syslog > Authentication.
Upload `cacert.pem`, `clientcert.pem`, `clientkey.key`

## Slide 25
Configure the Moxa RKS-G4000 Serie Switch (Cont.)
Set Server Details:
Syslog > General.
Server 1: Enabled
Authentication: TLS
IP Address: 192.168.127.64
TCP Port: 6514
Click Apply

## Slide 26
Check: Did it work?
On the Server (Check Connection):
  Run Command: netstat -at
  Look for LISTEN (on port 6514) and Look for ESTABLISHED (from the switch's IP)

## Slide 27
Check: Did it work?
On the Server (Check Logs):
  Run Command: `tail -f /var/log/switch_logs/192.168.127.250/system.log
  See your "log in failed" message arrive!

## Slide 28: Access Control List(ACL)
What is an Access Control List?
An ACL is a set of rules used to control network traffic.
Each rule says Permit (Allow) or Deny (Block).
What can an ACL filter?
Source and Destination (IP or MAC)
Protocol (ICMP / TCP / UDP)
Optional fields like port number (TCP/UDP) or ICMP type
Why do we use ACL?
Improve security (block unwanted access)
Reduce unnecessary traffic
Protect critical devices (PLC / HMI / servers)
Make clear “who can talk to whom” rules

## Slide 29: Access Control List(ACL)
Golden Rules
Rules are evaluated from top to bottom.
First match wins: the switch uses the first rule that matches the packet, then stops checking the rest.
Best practice: add an explicit “deny any” rule at the end (so unmatched traffic is blocked on purpose).
(Implicitly permit by default)

## Slide 30: Access Control List(ACL)
ACL is stateless:
it does not track sessions, it checks each packet alone.
Firewall is stateful:
  it tracks connections and allows return traffic automatically.
So with ACL, you may need rules in both directions (request + reply), depending on ingress/egress placement.
ACL vs Firewall

## Slide 31: Access Control List(ACL)
Navigation path
Security → Network Security → Access Control List

## Slide 32: Access Control List(ACL)
Click “+” to create a new access list.
Access List Type
IP-based: match by IP information
MAC-based: match by MAC address.
Index
Choose the access list Index
Max Index number:16
Name
Enter a Name to describe the list.
Name helps you identify the list later.
Notes: “Now we will create an Access List. First, we click the plus button. This opens the ‘Create an Access List’ window.
We must choose the Access List Type. If we select IP-based, we filter traffic using IP information, like source and destination IP and protocol. If we select MAC-based, we filter using MAC addresses.
Next is the Index. Index is like the ID number of the access list. On this switch, the maximum index number is 16, so we can create IP-1 up to IP-16.
Finally, we enter the Name. Name is just a label for us. It makes it easy to remember what this access list is for. After we set type, index, and name, we click Create.”

## Slide 33: Access Control List(ACL)
After creating the Access List , choose where it will apply.
Interface Type
Port-based
  ACL works on selected physical ports.
VLAN-based
  ACL works on one VLAN.
Ingress Port (Incoming)
Traffic enters the switch from this port.
ACL checks packets as they come in.
Egress Port (Outgoing)
Traffic leaves the switch from this port.
ACL checks packets as they go out.

## Slide 34: Access Control List(ACL)
Egress
Ingress
For ingress, the ACL is processed as the packet enters the interface (inbound).
For egress, the ACL is processed as the packet leaves the interface (outbound).
Ingress Port vs Egress Port

## Slide 35: Access Control List(ACL)
PC A
Server B
Ping Request: Ingress 1/1 → Egress 1/2
Ping Reply: Ingress 1/2 → Egress 1/1
Ping Reply: Ingress 1/2 → Egress 1/1
1/1
1/2
“Send a ping to Server B.”

## Slide 36: Access Control List(ACL)
Click “+” icon to create a Rule Index

## Slide 37: Access Control List(ACL)
Rule Index: Rule order number (1, 2, 3…). Smaller index is checked first.
Enabled: Enable/disable this rule.
Rule Type:
Permit = allow matching traffic
Deny = block matching traffic
Protocol: Any / ICMP / TCP / UDP etc.
Source IP Address + Source IP Mask: “Who sends?
Destination IP Address + Destination IP Mask: “Who receives?”
DSCP (0–63): QoS marking in the IP header.
Any = ignore DSCP

## Slide 38: Access Control List(ACL)
DSCP & Redirect
DSCP: QoS marking value (0–63)
DSCP = Any: applies to all DSCP-tagged traffic
Redirect = Enabled: matching packets are re-routed
Redirect Port (Required): choose the target port

## Slide 39: Access Control List(ACL)
Hit Count = how many packets matched this rule.
Every time a packet matches a rule, the switch adds +1 to that rule’s Hit Count.
Shows how many ACLs are activated right now.
Index: the ACL list ID
Name: The ACL name you provided.
Activated: if it is running
Direction: where it is applied

## Slide 40: MACSec – Hands-on
1/1
1/1
1/2
1/2
TAP
A
B
Wireshark
C
PC A
PC B
Switch1
CKN:1234
CAK:12345
Switch2
CKN:1234
CAK:12345
Requirements (Success Criteria)
Configure MACSec between Switch1 and Switch2
Observe MACSec traffic via Wireshark using tap device.

## Slide 41: Access Control List – Hands ON
PC-B
192.168.127.20
PC-A
192.168.127.10
GOAL: Participants will create a Port-based ACL in RKS-G4028-L3 and control ICMP (ping) and HTTPS access to the switch using rule order.
1/1
1/2
Requirements (Success Criteria)
PC-B can open the switch Web UI via HTTPS (TCP/443 → 192.168.127.253)
PC-B can ping the switch (ICMP → 192.168.127.253)
PC-A can access the switch via SSH (TCP/22 → 192.168.127.253)
PC-A can ping the switch (ICMP → 192.168.127.253)
All other traffic is denied

## Slide 42: Syslog over TLSHands – on
Rsyslog Server
RKS-G4028-L3
Group2
RKS-G4028-L3
Group1
RKS-G4028-L3
Group3
RKS-G4028-L3
Group17
RKS-G4028-L3
Group18
CENTRAL SWITCH
Requirements (Success Criteria)
The logs should appear on the rsyslog server based on the IP address of your switch.

## Slide 43
Syslog over TLS – Hands ON
ID​ | Model​ | Table​ | Group​ | IP​ | User​ | Password​
1​ | RKS-G4028-L3​ | 1​ | 1​ | 192.168.127.101​ | admin​ | moxa​
 |  |  | 2​ | 192.168.127.102​ |  | 
2​ | RKS-G4028-L3​ | 2​ | 1​ | 192.168.127.103​ | admin​ | moxa​
 |  |  | 2​ | 192.168.127.104​ |  | 
3​ | RKS-G4028-L3​ | 3​ | 1​ | 192.168.127.105​ | admin​ | moxa​
 |  |  | 2​ | 192.168.127.106​ |  | 
4​ | RKS-G4028-L3​ | 4​ | 1​ | 192.168.127.107​ | admin​ | moxa​
 |  |  | 2​ | 192.168.127.108​ |  | 
5​ | RKS-G4028-L3​ | 5​ | 1​ | 192.168.127.109​ | admin​ | moxa​
 |  |  | 2​ | 192.168.127.110​ |  | 
6​ | RKS-G4028-L3​ | 6​ | 1​ | 192.168.127.111​ | admin​ | moxa​
 |  |  | 2​ | 192.168.127.112​ |  | 
7​ | RKS-G4028-L3​ | 7​ | 1​ | 192.168.127.113​ | admin​ | moxa​
 |  |  | 2​ | 192.168.127.114​ |  | 
8​ | RKS-G4028-L3​ | 8​ | 1​ | 192.168.127.115​ | admin​ | moxa​
 |  |  | 2​ | 192.168.127.116​ |  | 
9​ | RKS-G4028-L3​ | 9​ | 1​ | 192.168.127.117​ | admin​ | moxa​
 |  |  | 2​ | 192.168.127.118​ |  | 
10​ | RKS-G4028-L3​ | 10​ | 1​ | 192.168.127.119​ | admin​ | moxa​
 |  |  | 2​ | 192.168.127.120​ |  |