## Slide 1
IPsec VPN on MX-ROS
Branislav Radak
Field Application Engineer
March 2026
Mohamed Hamza
Field Application Engineer
MTSC 2026

## Slide 2: Learning Objectives
Understand the technology and use cases of IPsec VPN
Learn to configure and troubleshoot IPsec VPN on MX-ROS-based router

## Slide 3: Agenda
What is IPsec VPN
IPsec configuration interface on EDR-G9004
Typical IPsec VPN use-cases
Hands-ons

## Slide 4: What is a VPN
A VPN establishes a secure connection between networks by creating an encrypted tunnel over an untrusted network like the Internet, protecting data from interception and modification.

## Slide 5: Type of VPNs
Site to site
Site multi-site (remote access)

## Slide 6: Commonly used VPN: IPSec
RFC: starts from 2401
Works at IP Layer
IP Security
Unicast Traffic
2 modes:
  Tunnel mode
  Transport mode
2 protocols:
  ESP: encapsulation security payload
  AH: authentication header
2 phases (Steps)
  Phase 1: Prepare for phase 2 
  Phase 2: Phase 2  

## Slide 7: IPSec encapsulation
AH: transport mode
AH: tunnel mode
ESP: transport mode
ESP: tunnel mode

## Slide 8: IPSec: Phase 1
Association and key Management: ISAKMP
Key exchange and authentication: IKE
UDP: port 500
2 modes for IKE v1
  Main
  Aggressive
IKE v2
Parameters:
  Encryption
  Integrity
  DH group
  Timeout
  Authentification

## Slide 9: IPSec: Phase 2
IPSec Parameters
ESP
Encryption Algorithm
SA lifetime: regeneration time
Perfect Forward Secrecy
Dead Peer Detection

## Slide 10: Typical use cases: Remote Access to PLC / SCADA Systems (Secure Maintenance)
Purpose: - Allow engineers to securely access PLCs, RTUs, HMIs, or SCADA systems from outside the plant. How it works: - A secure IPsec VPN tunnel connects the remote user to the industrial network. - Only authorized devices and users can access specific systems. Benefits: - Safe remote troubleshooting and maintenance - Keeps sensitive industrial systems protected from Internet threats

## Slide 11: Typical use cases: Site-to-Site Connectivity Between Plants
Purpose: - Connect multiple factories, substations, or remote industrial sites to a central control center. How it works: - IPsec VPN links each site securely over the Internet or other networks. - Central systems can monitor production, collect data, or manage operations. Benefits: - Centralized monitoring and control - Secure data exchange between sites - Supports industrial operations without expensive dedicated lines

## Slide 12: Hands-ons

## Slide 13: Hands-on 1: Airport Augmentation
Scenario:
A company doing airport signaling (lighting and aircraft guidance) has requested your help. They need a secure way to connect their systems between two small nearby airports. There is a private fiber link between two sites, but since it goes over the public land, securing all the traffic on the link is mandatory. You decide to recommend IPsec VPN.
LAN 1
VPN
LAN 2

## Slide 14: Hands-on 1: Airport Augmentation
Scenario:
A company doing airport signaling (lighting and aircraft guidance) has requested your help. They need a secure way to connect their systems between two small nearby airports. There is a private fiber link between two sites, but since it goes over the public land, securing all the traffic on the link is mandatory. You decide to recommend IPsec VPN.
WAN 1
WAN 1
IPsec
LAN
LAN 1
LAN
LAN 2
PC1
PC2
PC3
PC4
SW1
SW2
R1
R2

## Slide 15: Hands-on 1: Airport Augmentation
Device | IP address
R1 WAN1 | 10.0.0.(2*T-1)/24
R1 LAN | 192.168.TG.254/24
R2 WAN1 | 10.0.0.(2*T)/24
R2 LAN | 192.168.TG.254/24
SW 1 | 192.168.TG.1/24
PC 1 | 192.168.TG.2/24
PC 2 | 192.168.TG.3/24
SW 2 | 192.168.TG.1/24
PC 3 | 192.168.TG.2/24
PC 4 | 192.168.TG.3/24
T  Table number (1-9)
G  Group number (1-2)
Device Table 5 | IP address
R1 WAN1 | 10.0.0.9/24
R1 LAN | 192.168.51.254/24
R2 WAN1 | 10.0.0.10/24
R2 LAN | 192.168.52.254/24
SW 1 | 192.168.51.1/24
PC 1 | 192.168.51.2/24
PC 2 | 192.168.51.3/24
SW 2 | 192.168.52.1/24
PC 3 | 192.168.52.2/24
PC 4 | 192.168.52.3/24
WAN 1
WAN 1
IPsec
LAN
LAN 1
LAN
LAN 2
PC1
PC2
PC3
PC4
SW1
SW2
R1
R2

## Slide 16: Hands-on 1: Airport Augmentation
Constraints:
You must use German Federal Office for Information Security Technical Guideline TR-02102-3 to select the appropriate ciphers when setting up IPsec.
You must ensure the Perfect Forward Secrecy so that encrypted communications and sessions recorded in the past cannot be decrypted if secret keys or passwords are compromised in the future.

## Slide 17: Hands-on 1: Airport Augmentation
Task 1:
Enable VPN Event logging to Local Storage.
Build the IPsec tunnel with the above constraints in mind. Choose “Startup Mode: Initiate Automatically” on both routers. Verify with the table coach if the selected parameters are appropriate.
Verify that all four PCs can communicate with each other, for example via ping.
Questions (answer to the table coach):
What does IPsec Status in the WebGUI show?
What does the VPN LED show?
What do System log and VPN log show?
What does the routing table show?

## Slide 18: Hands-on 1: Airport Augmentation
Task 2:
Verify that all the LAN1 ↔ LAN2 traffic on the link between two routers is indeed encrypted. Recommended topology:
Questions (answer to the table coach):
What transport layer protocol does ISAKMP use?
What port does ISAKMP use? Can you modify the port?
What port does ESP use?
Change one side to "Startup Mode: Wait for Connection". What is the difference in Wireshark?
What happens if both sides are configured as "Startup Mode: Wait for Connection“?
Mirror
Mirror

## Slide 19: Hands-on 2: Gas Network Gaffe
Scenario:
You are working on a project with a national LNG provider that connects 200 gas pumping/metering/condition monitoring stations. Your proposed solution is to connect all remote stations to one central location by using IPsec VPNs. Customer attempted to set up a PoC by themselves but could never establish a VPN tunnel. They approach you for further help, providing configuration files for central and remote routers.
LAN 1
VPN
NMS
LAN 200
VPN
Remote router
Remote router
…
Central router

## Slide 20: Hands-on 2: Gas Network Gaffe
Scenario:
You are working on a project with a national LNG provider that connects 200 gas pumping/metering/condition monitoring stations. Your proposed solution is to connect all remote stations to one central location by using IPsec VPNs. Customer attempted to set up a PoC by themselves but could never establish a VPN tunnel. They approach you for further help, providing configuration files for central and remote routers.
WAN 1
LAN
PC1
PC2
SW1
RKS-G4028
R1
MXview One
Central router
WAN 1
LAN
PC3
PC4
SW2
R2
Table 1
Table 9
…
IPsec
IPsec
IPsec
IPsec

## Slide 21: Hands-on 2: Gas Network Gaffe
Device | IP address
R1 WAN1 | 10.0.0.(2*T-1)/24
R1 LAN | 192.168.TG.254/24
R2 WAN1 | 10.0.0.(2*T)/24
R2 LAN | 192.168.TG.254/24
SW 1 | 192.168.TG.1/24
PC 1 | 192.168.TG.2/24
PC 2 | 192.168.TG.3/24
SW 2 | 192.168.TG.1/24
PC 3 | 192.168.TG.2/24
PC 4 | 192.168.TG.3/24
Central router WAN | 10.0.0.100/24
MXview One | 192.168.0.100/24
T  Table number (1-9)
G  Group number (1-2)
Device Table 5 | IP address
R1 WAN1 | 10.0.0.9/24
R1 LAN | 192.168.51.254/24
R2 WAN1 | 10.0.0.10/24
R2 LAN | 192.168.52.254/24
SW 1 | 192.168.51.1/24
PC 1 | 192.168.51.2/24
PC 2 | 192.168.51.3/24
SW 2 | 192.168.52.1/24
PC 3 | 192.168.52.2/24
PC 4 | 192.168.52.3/24
Central router WAN | 10.0.0.100/24
MXview One | 192.168.0.100/24
WAN 1
LAN
PC1
PC2
SW1
RKS-G4028
R1
Central router
WAN 1
LAN
PC3
PC4
SW2
IPsec
IPsec
R2
MXview One

## Slide 22: Hands-on 2: Gas Network Gaffe
Task 3:
Central router configuration is correct, and the config file is provided for your reference. IPsec pre-shared key is MTSC2026 for each tunnel.
Examine the provided config file for your table and group and fix customer’s configuration errors.
Ask the table coach connect your EDR’s WAN1 to the central location.
Success criteria:
Your group’s router successfully establishes a VPN tunnel with the Central router.
Your PC is successfully monitored by MXview One at the central location.
You explained to the table coach what fixes you implemented to the configuration.
Go back to step 1 if necessary.

## Slide 23: Q&A