## Slide 1
Ahmed Hyusein Ahmed
Sr.Technical Support Engineer
March 2026
eCoS - Enhancing Cyber Security
MTSC 2026
Hugo HT Chan
Lead Application Engineer

## Slide 2: AGENDA
1
2
3
New features
Enhancements
Hands-On Practice

## Slide 3: Why eCos Matters?
芳林新葉催陳葉，流水前波讓後波
Notes: Just as new leaves replace old leaves and new waves follow old waves, every generation naturally replaces the previous one.

## Slide 4: AGENDA
1
2
3
New features
Enhancements
Hands-On Practice

## Slide 5: New Features
Port Mirror: RSPAN
Security: BPDU attack prevention mechanism

## Slide 6: Models
Din-Rail series
  EDS-G500E
  EDS-500E
  EDS-P506E
Rack mount series
  IKS-G6000A
  IKS-6700A
  ICS-G7000A
Model | FWR version (>=)
EDS-510E | V5.6
EDS-518E | V6.4
EDS-528E | V6.4
EDS-G500E | V6.5
EDS-P506E | V5.9
IKS-G6524A | V5.11
ICS-G7526/28A | V5.11
ICS-G7748/50/52A | V5.10
ICS-G7826/28A | V5.11
IKS-G6824A | V5.10
ICS-G7848/50/52A | V5.10
IKS-6700A | V5.10
IKS-6728A-8PoE | V5.10

## Slide 7: RSPAN

## Slide 8: RSPAN Concept
VLAN Setting
  Trunk port PVID=1, Tagged VLAN= 5
  Access PVID= 1
  Access PVID= 5
  Access PVID= 5
SWB
SWC
SWA
Traffic
Remote Switched Port Analyzer
let the data can be monitored to remote single/multiple terminal ports on the other switches.

## Slide 9: Port Mirror: RSPAN
New
Previous

## Slide 10: RSPAN Setting
RSPAN Setting
  SWA/B:
  SWC:
  > Monitored port=
  > Reflect port & Mirror port=
VLAN Setting
  Trunk port PVID=1, Tagged VLAN= 5
  Access PVID= 1
  Access PVID= 5
  Access PVID= 5
SWB
SWC
SWA
Traffic

## Slide 11: RSPAN – Note
CPU port traffic can’t be mirrored remotely.
Reflect port will be reserved for RSPAN use only. Once a port is set as a reflect port, it will lose connectivity until RSPAN is disabled.
Assign RSPAN VLAN with a separate none-used VLAN.
  Not use the management VLAN as RSPAN VLAN
Enabling GVRP while using RSPAN is NOT allowed.
Reflect port LED will be ON
EDS-G500E don’t support fiber port as reflect port. (chip limitation)
EDS-510E does not support RSPAN. (chip limitation)

## Slide 12: BPDU Attack Prevention

## Slide 13: What is BPDU?
Bridge Protocol Data Unit
  It is widely used for STP/RSTP/MSTP and other redundancy protocols(TR, TC)
  Exchange the control information
    Root Bridge, Path Cost, Port Role, Port State and Network topology changes
  Destination MAC address is reserved as 01:80:C2:00:00:00
Notes: MRP frames use as destination MAC addresses 01:15:4E:00:00:xx
Turbo Ring v2 and Turbo Chain frames use as destination MAC addresses 01:80:C2:00:00:xx

## Slide 14
Confidential
Spanning Tree Protocol
Designated / Root / Blocked Port Decisions
PC2
PC1
Priority: 32768
Priority: 32768
Priority: 32768
00:00:00:00:00:01
00:00:00:00:00:02
00:00:00:00:00:03
On the Root Bridge, all active ports are Designated Ports.
On non-root switches, one port with the lowest path cost toward the Root Bridge becomes the Root Port.
All other ports on the same segment that are not forwarding become Blocked (Alternate) ports.
Link Speed | Cost
10 Mbps | 100
100 Mbps | 19
1 Gbps | 4
DP | Designated Port
RP | Root Port
B | Blocked Port
Root Bridge
Port Roles

## Slide 15: Why Are BPDU Attacks Dangerous?
BPDU attack!!!
Launch DoS (Denial of Service)
  Make switch busy with the BPDU packets

## Slide 16: Security: BPDU attack prevention mechanism
Prevent BPDU attack to crash the network
  Enabled on the Non-redundant port.
  No UI to disabled
Port will shutdown to protect the network
  Receive >=100 consecutive BPDU in 1 Sec.
Event Log shows the port is shutdown
Recovery
  Port disable-Enable
  Switch power off-on
BPDU attack!!!

## Slide 17: AGENDA
1
2
3
New features
Enhancements
Hands-On Practice

## Slide 18: Enhancements
VLAN: Trunk port PVID egress rule
Rate Limiting: Port shutdown behavior
Syslog: Authentication through TLS
Login Authentication: Support 2nd RADIUS Server
MAB: Support more auth. type
MRP: User-Defined UUID
CLI: Import SSL certificate through CLI
Industrial protocol related

## Slide 19: VLAN: Trunk port PVID egress rule
 |  | Ingress |  | Egress
Tagged Frame |  | Access Port Tagged ID = PVID, received Tagged ID = PVID, dropped Trunk & Hybrid Port Specified= Unchanged Not specified= Drop |  | Access Port If Tag = PVID: Remove Tag If Tag = PVID: Not forward Trunk Port If Tag = PVID: Remove Tag If Tag = PVID: Unchanged Hybrid Port Follow specified
Untagged Frame |  | Tagged PVID |  | 
A
B
Switch
???
???
* In the new firmwares, the PVID VLAN number can be set in the Tagged VLAN field on both trunk and hybrid ports. The old firmware only allows setting the PVID VLAN number in the Tagged VLAN field on hybrid ports; it does not allow it on trunk ports.
Notes: In the new firmware, the PVID VLAN number can be set in the Tagged VLAN field on both trunk and hybrid ports. The old firmware only allows setting the PVID VLAN number in the Tagged VLAN field on hybrid ports; it does not allow it on trunk ports.

## Slide 20: VLAN: Trunk port PVID egress rule
A
B
Switch
Egress rule change on the VLAN Trunk port
When packet’s VID= PVID
  Current version:
  > PVID is specified in the Tagged VLAN field: Remain VID
  > PVID is Not specified in the Tagged VLAN field: Remove VID
  Previous version:
  > PVID cannot be specified in the Tagged VLAN field
  > VID Always Removed
VID=55
PVID=55
VID=??
Notes: In the new firmware, the PVID VLAN number can be set in the Tagged VLAN field on both trunk and hybrid ports. The old firmware only allows setting the PVID VLAN number in the Tagged VLAN field on hybrid ports; it does not allow it on trunk ports.

## Slide 21: Rate Limiting: Port shutdown behavior
New FW:
  When triggered, port is Shutdown. User can re-enable the port in port settings page instead of waiting for the duration time. After the duration time, the transmission will recover automatically.
  Unit= minutes
  Old FW upgrade to New FW: Rounding up, e.g. 30 sec-> 1 min, 110 Sec-> 2 min
Previous FW:
  When triggered, port is Blocked. User cannot re-enable the port before the time expiration. After the duration time, the transmission will recover automatically.
Notes: Old-> New: round up, e.g. 535 sec-> 9 min
New -> old: 0 sec

## Slide 22: Quick Reminder! IP Address Types & Ethernet Addresses
H1
H2
H2
H3
H4
H5
H6
H1
H6
H6
Unicast – Message to a single destination
IP: unique
Multicast – Message to a group of devices
IP: 224...... until .239......
Broadcast – Message to all nodes in a subnet
IP: 255.255.255.255
H2
H4
H1
FF : FF : FF :
FF : FF : FF
00 : 80 : 64 :
xx : xx : xx
01 : 00 : 5E :
xx : xx : xx

## Slide 23: Why 4464 fps?
A 64‑byte Ethernet frame is 672 bits on wire including overhead.
100,000,000 / 672 ≈ 148,809 fps
FPS | Approx % of 100 Mbps
4464 | ~3%
7441 | ~5%
14881 | ~10%
22322 | ~15%
37203 | ~25%
52084 | ~35%
74405 | ~50%
FPS means Frame Per Second
100,000,000(FE) / 672 (64byte) ≈ 148,809 fps
148,809 * 0.03 ≈ 4464 fps
148,809 * 0.05 ≈ 7441 fps
Notes: Why 672: A 64-byte Ethernet frame is the minimum frame size.
But on the wire, more bits are actually transmitted due to: 8 bytes (preamble + SFD) + 12 bytes inter-frame gap (IFG)= Total extra overhead = 20 bytes
64 + 20 = 84 bytes -> 84 × 8 = 672 bits
A 100 Mbps link can transmit about 148,809 minimum-size packets per second. This is the theoretical maximum packet rate at 100 Mbps for 64-byte frames.
100 Mbps ≈ 148.8 kpps

## Slide 24: Syslog: Authentication through TLS

## Slide 25: Login Authentication: Support 2nd RADIUS Server
Existing FW: Support two servers for both login auth. and 802.1x
  Previous version: One server for login authentication, two servers for 802.1x
Auth. reply timeout from the Server.
The switch will go to the 2nd Server if:
> No ping reply (x3) from the 1st Server. > 1st Server reply the ping but RADIUS service is not running.

## Slide 26: MAB: Support more authentication type
Auth. Type
  PAP, CHAP, MS-CHAPv2
Previous version
  Only CHAP

## Slide 27: MRP: User-Defined UUID
New
Previous
* UUID = Universally Unique Identifier

## Slide 28: CLI: Import SSL certificate through CLI
STEP
Enter copy tftp ssl-certificate { <STRING:password> }
Enter file name of certification and TFTP server IP.
Waiting TFTP working.
* Error message: Importing had some error, please check password or the file.
STEP
Example
MOXA# copy tftp ssl-certificate moxa
Address or name of remote host [192.168.127.1]? 192.168.127.131
Source file name ? SSL_Certificate.pfx
Importing SSL certificate, please wait.....
Save ssl certification to flash? [Y/n]
Saving ssl certification ...Success

## Slide 29: Industrial protocol related
[PROFINET] Support MRP in GSD file
[EIP] add MRP mode in Redundant Device Mode (MOXA Networking Object, Attr. 26)
[EIP] user-defined RPI value
[Modbus] add MRP information

## Slide 30: AGENDA
1
2
3
New features
Enhancements
Hands-On Practice

## Slide 31: Proposed Timing
Please follow the above timing
Some topics require lot of work one may not get to the end. Partial results also give good foundation for further self-study.
Time from Start | Topic | Length
00:00 | Introduction & Refresh | 00:35
00:35 | HO1: Syslog authentication over TLS | 00:25
01:00 | HO2: BPDU attack prevention | 00:25
01:25 | HO3: Rate Limit Port Shutdown | 00:25
01:50 | Debrief | 00:10

## Slide 32: Proposed Setup
Server
192.168.127.2
192.168.127.1
RSTP

## Slide 33: Hands-On 1 : Syslog authentication over TLS
MXviewOne
192.168.127.2
192.168.127.1
RSTP

## Slide 34: Hands-On 1 Test Setup
Make sure the certificates files are ready
  (Client Certificate, Client Key, Server CA Certificate )
Make sure the switches are ready to login
  Switches IP must be different
Make sure the topology is ready on MXviewOne.
  Use only one MXviewOne per table(two groups work together).
  Use one MxviewOne per table. Table coach will assist you.
  MXviewOne version v1.6.1 and v1.7.0(latest) has been tested.

## Slide 35: Tasks-I
Enable the Syslog over UDP and config the server IP & port accordingly.
Trigger a log
  Could you see it on local log entries?
  Check it on MxviewOne syslog viewer, make sure your IP and log message is there.
  Check the traffic on wireshark.
  Save the capture or take some screenshots from wireshark for the comparison. (Or simply keep wireshark running)
Import the proper certificates into the switch accordingly.
  Can the information of Client Certificate and Server Certificate be shown correctly?
  Does the start time and end time valid?
  Is the system time in switch correct?
Enable the Syslog over TLS-auth(tcp) and config the server IP & port accordingly.
Trigger a log
  Could you see it on local log entries?
  Check it on MxviewOne syslog viewer, make sure your IP and log message is there.
  Check the traffic on wireshark. Explain the difference between UDP and TLS-auth(tcp)
  Save the capture or take some screenshots from wireshark for the comparison. (Or simply keep wireshark running)

## Slide 36: Tasks-II
Import the different certificates into the switch
  Can the information of Client Certificate and Server Certificate be shown correctly?
  Does the start time and end time valid?
  Is the system time in switch correct?
Enable the Syslog over TLS-auth(tcp) and Config the server IP & port accordingly.
Trigger a log
  Could you see it on local log entries?
  Check it on MxviewOne syslog viewer, do you see any log message there? If not why? Explain.
  Check the traffic on wireshark. Find error message if there is any.
  Save the capture or take some screenshots from wireshark for the comparison. (Or simply keep wireshark running)
Enable the Syslog over TLS(tcp) and Config the server IP & port accordingly.
Trigger a log
  Could you see it on local log entries?
  Check it on MxviewOne syslog viewer, make sure your IP and log message is there.
  Check the traffic on wireshark. Explain the difference between UDP, TLS(tcp), TLS-auth(tcp)

## Slide 37: Hands-On 2 : BPDU attack prevention
Attacker
192.168.127.2
192.168.127.1
RSTP

## Slide 38: Hands-On 2 Test Setup
Make sure the redundant protocol is enabled and loop-free
Create a BPDU on Colasoft
  Destination MAC address is important!

## Slide 39: Colasoft Packet Builder
How to create a new packet
Click “Add” to have a new packet
  Choose the Template based on your need
    ARP Packet/IP/TCP/UDP
  Medium Type
    Ethernet/CAN/… etc (New version supported)
Modify the value in Decode Editor
  Modify the destination Address to BPDU format

## Slide 40: Colasoft Packet Builder
How to modify the existing packets
Select the packet you would like to modify by clicking it in Packet List
  The Decode Editor displays the corresponding value and fields
  The Hex Editor shows the packet in Hex value
Modify the value in Decode Editor
  If the Colasoft Packet Builder could identify the field, it will automatically dissector
  You can directly type the Number or String in corresponding field
Modify the value in Hex Editor
  If the value is like bits, hex string, please use the Hex Editor
  You can modify the value by bytes in Hex

## Slide 41: Colasoft Packet Builder
How to send out the packets
There are two ways to send out the packet
  Send and Send all
  You can select the packets by ctrl or shift
Select the network adaptor

## Slide 42: Colasoft Packet Builder
How many packets you want to send and delay
Burst Mode
  To send out the packets immediately
    Depends on your computer performance
Loop Sending
  How many loops you want to have
  Delay between loops
    You could set lower

## Slide 43: Tasks
Act as a hacker to generate BPDU attacks to switch
  Could you add a packet
  What should be the destination address?
Send out the BPDU packets through Colasoft
  Check the event log
  Check the port status
If you could not see the log message – “Port X BPDU attack”, why?
  Use Wireshark to check how many packets you sent to switch
  Make sure Colasoft be able to send out the packets
  Have you tried “Burst mode” and “loop”?
How could you revert it back?

## Slide 44: Hands-On 3 : Rate Limit Port Shutdown
Attacker
192.168.127.2
192.168.127.1
RSTP

## Slide 45: Hands-On 3 Test Setup
Make sure the redundant protocol is enabled and loop-free
Configure the switch to be prepare for the test
  Enable Rate Limit - port shutdown
    Under QoS
  Configure the corresponding port
  Select 4464 fps
  Set the duration as 5 minutes
Create the packets for triggering the rate limit and sent to the switch
  Is the packet unicast, multicast or broadcast?

## Slide 46: Tasks
Act as a hacker to create unusual traffic to switch
Send out the packets
If you could not see the log message – “Excessive traffic, port X disabled”, why?
  Use wireshark to check how many packets you sent to switch
  Make sure the packet generator be able to send out the packets
  Have you tried “Burst mode” and “loop”?
How could you to revert it back?

## Slide 47: Recap

## Slide 48: Recap
Hands-on 1 Syslog over TLS
  How to setup the syslog over TLS via switches and MXview
  The difference between the TLS modes in syslog
Hands-on 2 BPDU attack prevention
  How to generate a BPDU packets and send out periodically
Hands-on 3 Rate Limit Port Shutdown
  What is the performance limitation on your personal computer

## Slide 49: Models
Din-Rail series
  EDS-G500E
  EDS-500E
  EDS-P506E
Rack mount series
  IKS-G6000A
  IKS-6700A
  ICS-G7000A
Model | FWR version
EDS-510E | V5.6
EDS-518E | V6.4
EDS-528E | V6.4
EDS-G500E | V6.5
EDS-P506E | V5.9
IKS-G6524A | V5.11
ICS-G7526/28A | V5.11
ICS-G7748/50/52A | V5.10
ICS-G7826/28A | V5.11
IKS-G6824A | V5.10
ICS-G7848/50/52A | V5.10
IKS-6700A | V5.10
IKS-6728A-8PoE | V5.10