## Slide 1
Troubleshooting Best Practices:
A Practical Case-Based Approach – 2026 MTSC Troubleshooting
A strategic decision-making framework for technical support and field application engineers
Jean-Marc Olivier and Hans Igeler

## Slide 2: Where Do You Start?
A customer reports unstable communication after adding a new fiber uplink, and you receive the call. What is your first move?
CARD 01
Ask for logs
CARD 02
Ask what changed
CARD 03
Replace the hardware

## Slide 3: Reactive Instincts are the Enemy of Resolution
Let’s participate in a remote access with the customer
Escalate the case immediately

## Slide 4: What Happens When Cases Arrive Without Evidence?
Days of email back-and-forth
Your product does not fulfil the specifications, product returns.
Customer loses confidence
Time is money
Resolution in hours
Problem reproduced and isolated
Customer sees a competent partner
Evidence-ready cases move directly to resolution
INCOMPLETE CASE
STRUCTURED ESCALATION
Magnifying
Glass
Checkmark

## Slide 5: Three Gates Must Open Before You Submit a Case
ANALYZE
PROVE
DOCUMENT
Understand the
Incident.
Gather evidence
and reproduce.
Submit complete
case documentation.
GATE RULE: If you cannot explain it, show evidence of it by reproducing it,
before you escalate it.

## Slide 6: From Symptom to Structured Problem Definition
Symptom | Structured Problem Statement | Facts (Observed) | Assumptions (Unverified) | Questions to Clarify
The switch port is flapping | Port 10 shows intermittent link loss with rising CRC errors since 14:32 on March 3rd, following the addition of a new fiber uplink | Port flapping logged since 14:32Rising CRC errors on fiber uplink Issue started after new uplink added | SFP module is defective Switch hardware is unstable New uplink caused the issue | What changed before 14:32? Was any maintenance performed? Is the new uplink on the same fiber path?
The computer keeps rebooting | Industrial PC reboots intermittently with Windows Event ID 41; hardware sensors show temperature spikes while voltage remains stable | Reboots logged with Event ID 41Temperature spikes observed Voltage stable | PSU failure Motherboard instability Thermal protection triggered | What is the ambient temperature? Is cooling functioning properly? Any recent hardware changes?
The PLC keeps disconnecting | PLC connection drops during network switchover events, although switch recovery time is confirmed at 20 ms | Connection drops during switchoverSwitch recovery time measured at 20 ms | PLC timeout too short Application not tolerant to 20ms gap | What is the PLC timeout setting? Is redundancy protocol configured correctly? Are retries implemented at application level?

## Slide 7: Business Impact – Classify the Incident first.
CRITICAL (Safety/Stop)
Immediate – open case in parallel with investigation.
DEGRADED (Operational)
Structured Investigation with a defined window.
NON-CRITICAL (Monitoring)
Scheduled analysis.

## Slide 8: Evidence Collection: The 5 Ps
PARTS
PEOPLE
POSITION
PAPER
PARAMETERS
Interview the site engineer. Is there a change compared to before?
Hardware, cables, SFPs. Is there any physical damage?
Physical location.
Near high voltage or heat?
Wiring diagrams, logs.
Does the setup match the docs?
Config files, firmware version.
Are the settings correct?

## Slide 9: Your Evidence Collection Toolkit
Digital Diagnostics:
MXView, Logs, Wireshark, Serial Analyzers
Physical Crash Cart
Console cables, Impedance testers, Fiber kits.
⛔ Export logs before you touch anything.

## Slide 10: The 5 Whys Technique
1. Define the Problem Statement (Specific incident, not a symptom)
2. Ask 'Why?' Support the answer with observed or collected evidence
3. Continue Asking 'Why?' Each answer becomes the input for the next question; do not skip steps
4. Stop When Evidence Runs Out If the next 'Why?' cannot be supported, return to the 5 Ps
5. State Your Support Request Best evidence-supported explanation for case documentation

## Slide 11: The 5 Whys Technique — Interrogating Your Evidence
Step | Question | Anchor
Why 1 | Why is this happening? | Based on observed facts
Why 2 | Why is that occurring? | Based on collected evidence
Why 3 | Why did that happen? | Based on 5 Ps findings
Why 4 | Why was that allowed? | Based on documentation / Paper
Why 5 | Why does that condition exist? | Based on process / Parameters
Step | Answer
Why is the port flapping? | 
HOW IT WORKS:
APPLIED TO RUNNING CASE:

## Slide 12: The 5 Whys Technique — What Evidence Would You Interrogate?
Running case applied:
Port flapping and rising CRC errors on fiber uplink, starting after a new uplink was added
Exercise (3 minutes):
Using the 5 Ps, what evidence would you collect? What would you try to reproduce?

## Slide 13: Case Study I: The “Invisible” Fiber Problem
PROBLEM:
Industrial switch shows intermittent port flapping and increasing CRC errors on fiber uplink.
THE TRAP:
Assuming SFP module defect or switch hardware instability.
INVESTIGATION:
Port statistics show rising CRC and alignment errors, Replacing SFP did not solve issue.
CAUSE:
Physical layer degradation caused by dirty fiber connector leading to unstable optical signal.
PREVENTIVE ACTION:
Implement “Inspect → Clean → Inspect” policy, Provide certified fiber cleaning kit at site.

## Slide 14: The 5 Whys Technique — Interrogating Your Evidence
Step | Question | Anchor
Why 1 | Why is this happening? | Based on observed facts
Why 2 | Why is that occurring? | Based on collected evidence
Why 3 | Why did that happen? | Based on 5 Ps findings
Why 4 | Why was that allowed? | Based on documentation / Paper
Why 5 | Why does that condition exist? | Based on process / Parameters
Step | Answer
Why is the port flapping? | Signal quality is degraded.
Why is signal quality degraded? | High optical loss on the fiber link
Why is optical loss high? | Fiber connector is contaminated
Why is it contaminated? | No inspection was done after installation
Why was no inspection done? | No fiber cleaning protocol exists on-site.
HOW IT WORKS:
APPLIED TO RUNNING CASE:

## Slide 15: Case Study I — What Evidence Would You Interrogate?
Running case applied:
Port flapping and rising CRC errors on fiber uplink, starting after a new uplink was added
Exercise (3 minutes):
Using the 5 Ps, what evidence would you collect? What would you try to reproduce?
P | Evidence to Collect | Why it Matters
Parts | Inspect fiber connectors with scope | Contamination found — direct cause identified
People | Ask who installed the new uplink and when | Confirmed: no inspection was performed at installation
Position | Check cabinet temperature and fiber routing | Fiber bend radius acceptable — ruled out
Paper | Verify fiber spec matches SFP requirements | Specs matched — ruled out incompatibility
Parameters | Check interface statistics and error counters | CRC + alignment errors confirmed — physical layer

## Slide 16: Every Failure Has a Chain Map
Symptom
Switch Port Flaps /
CRC Errors
Direct Cause
Weak optical
Signal
Contributing Factor
Dirty fiber optic connector
Cause
Lack of maintenance protocol or a cleaning kit on-site
Physical
(Hardware malfunction)
Human
(Configuration error)
Organizational
(Process failure)

## Slide 17: Know Your Support Path
DISTRIBUTOR
Solve:
Known issues
Configuration
Physical layer
Open a case when:
Evidence collected
Reproduction confirmed
hypothesis formed.
R&D
Solve:
Firmware defects
Hardware designs
Requires:
Full field evidence +
LAB reproduction.
LOCAL TS / GLOBAL TS
Solve:
Advanced protocol.
Firmware behavior
System integration issues.
Go to next level when:
Lab reproduction attempted.
Full case documentation package ready
Each tier adds investigation depth, not just a new pair of hands. Submit evidence, not confusion.

## Slide 18: Five Components of a Case Documentation Package
Device Profile: Model, serial number, firmware version, network topology diagram
Reproduction Steps: Provide clear steps to reproduce the failure.
It’s broken
Here is the Evidence Data
Log Bundle: System log, event log, CLI output exported before restart
Evidence Record: Screenshots, port statistics, protocol captures, and inspection results.
There is no room for I believe
It's broken: please advise." ✅ "Port flapping confirmed. CRC errors logged. SFP swap did not resolve. Fiber connector inspection shows contamination.
Hypothesis: physical layer degradation from installation without inspection. Reproduction: disconnect and reconnect fiber flapping recurs within 60 seconds.

## Slide 19: Case Studies: Patterns You Will Recognize
Notes: SLIDE 19 — Case Studies: Patterns You Will Recognize
We're going to run through five cases quickly. As you read each one, ask yourself: would I have fallen into the trap?

## Slide 20: Case Study II: The “Thermal” Reboot on IT Computing
PROBLEM: Industrial computer performs poor boots intermittently, Windows Event ID 41.
THE TRAP: Assuming OS corruption or power supply instability.
INVESTIGATION: HW-sensor and performance monitoring showed temp spikes, Voltage was stable.
ROOT CAUSE: Gradual Physical Failure. Thermal grease degradation + vibration.
PREVENTIVE ACTION: 3-year maintenance cycle for thermal integrity. OT Rack Thermal management analysis.
Dried Thermal
Paste

## Slide 21: Case Study III: The over usage.
PROBLEM:
UC-3100 series devices fail to boot after running customer scripts. Symptoms: kernel panic and lost partition tables, after some time these devices fail to boot.
THE TRAP:
Assuming Filesystem corruption due to scripts or used commands
INVESTIGATION:
eMMC log analysis with Storage Vendor revealed excessive read/write operations.
ROOT CAUSE:
HW Spec for physical component. eMMC failure was related to the MLC’s P/E cycle exhausted — 4.3K cycles recorded vs. 3K spec limit.
PREVENTIVE ACTION:
5-year maintenance cycle for hardware. Replacing eMMC component. Implement device health mechanism.

## Slide 22: Case Study IV: Redundancy vs. Application Timeout
PROBLEM:
PLC Connection drops during switchover despite <=20ms recovery.
THE TRAP:
Blaming the switch for slow recovery.
INVESTIGATION:
Protocol analysis confirmed 20ms recovery. PLC config check showed 10ms tolerance.
ROOT CAUSE:
PLC Application expectations are tighter than hardware capabilities.
PREVENTIVE ACTION:
Adjust the PLC watchdog to 50ms.
Failure Zone
PLC Watchdog Timer
20ms
10ms
Network Recovery (Turbo Ring)

## Slide 23: Case Study V: Bluescreens on Industrial Computer
PROBLEM: Random Blue Screens 1–3 times per day during “normal work”. Windows and Computer was just updated with latest Windows updates, drivers and firmware.
THE TRAP: hardware vs. software/driver incompatibility from the updates, or security agents.
INVESTIGATION: collect dumps and logs. Create a BSOD playbook. Debugging shows inconsistent bugchecks and signs of memory corruption. Run MemTest86 ⭢ isolate failing DIMM.
ROOT CAUSE: intermittent RAM errors from a defective or marginal DIMM. Memory corruption produced inconsistent bugcheck codes and made crash dumps blame unrelated drivers and core Windows modules.
PREVENTIVE ACTION: Use tested RAM, perform diagnostics after upgrades. Record hardware- and software changes in an asset system.
*******************************************************************************
* *
* Bugcheck Analysis *
* *
*******************************************************************************
DRIVER_IRQL_NOT_LESS_OR_EQUAL (d1)
An attempt was made to access a pageable (or completely invalid) address at an
interrupt request level (IRQL) that is too high. This is usually
caused by drivers using improper addresses.
If kernel debugger is available get stack backtrace.
Arguments:
Arg1: 0000000000000010, memory referenced
Arg2: 0000000000000002, IRQL
Arg3: 0000000000000000, value 0 = read operation, 1 = write operation
Arg4: fffff806401c4404, address which referenced memory
💡 This Windows dump blamed the driver. The actual cause was the DIMM. This is why evidence interrogation matters more than symptom reading.

## Slide 24: Before You Submit a Case — Run This Check
Self-assessment checklist:
Analyzed — Do I have a clear problem statement (not just a symptom)?
Classified — Have I assessed business impact and urgency?
Separated — Have I separated facts from assumptions?
Collected — Have I applied the 5 Ps and preserved volatile data?
Reproduced — Can I trigger the failure on demand (or explain why not)?
Hypothesized — Do I have an evidence-based hypothesis?
If you cannot check all six boxes, your case documentation is not ready. Go back one step.

## Slide 25: Tabletop Game Apply the framework. Work as a team. Document before you act

## Slide 26: Now It’s Your Turn - Why a Tabletop Game?
Our MTC training explains how our technology works; this game trains how to apply it.
Simulates real post-sales support situations
Uses a real, anonymized customer case
Encourages discussion, decision-making, and teamwork
Creates a safe environment to make mistakes and learn

## Slide 27: Tabletop Core Objective
Primary Objective
Train distributor engineers to apply the correct troubleshooting mindset, not just find a technical fix
Focus Areas
Asking the right questions
Structuring troubleshooting steps
Correctly identifying Type 0 vs Type 1 cases
Choosing the right actions and escalation path

## Slide 28: Tabletop Game Concept
How It Works
Each table
  2 teams
  2 participants per team each
  Teams collaborate towards a shared resolution
Roles
  Presenters act as the Customer Owner and Moxa Technical Support
  Table Coach acts as the Customer Maintenance Engineer with basic network knowledge.
  Participants act as Technical Support Engineers
Only basic information is provided initially, just enough context to prepare, without revealing details that would give away the answer or bypass their troubleshooting process.
Additional information is revealed progressively
Teams must continuously decide:
  What to ask
  What to check
  What to do next

## Slide 29: Game Realism by Design
Key Design Principles
Incomplete basic information (just like real cases)
Self-brainstorming and then a decision.
Process and mindset matter more than speed
Additional information is revealed progressively
Goal
  Prevent guesswork; expectations should be fact-based.
  Reinforce structured troubleshooting

## Slide 30: Learning Outcomes and Business Value
By the end of the session, participants will:
Understand how to approach Type 0 and Type 1 cases
Apply a structured troubleshooting methodology
Communicate more effectively with customers
Handle cases more efficiently and independently
For Distributors
Clear expectations
Faster onboarding
Increased confidence
For Internal Support
Better case quality
Reduced unnecessary escalation
Faster resolution times
For Customers
More consistent and professional support

## Slide 31: Q&A

## Slide 32: The Customer Incident:
5:30 PM

## Slide 33: The Customer Incident:
QUESTION 01
What is missing from this report?
QUESTION 03
Is this information sufficient to open and validate a support case?
QUESTION 02
What is your immediate next step?
Many of our industrial devices randomly become unreachable, causing loss of communication in
the automation system. Rebooting the units usually restores operation, but the issue keeps
coming back.
CONNECTION LOST, CUSTOMER HANG UP CALL THIS IS ALL THE INFORMATION YOU HAVE.
CASE ID: 2026-X77-TTS
Stop. You Have 5 minutes. Identify every gap using the Framework.

## Slide 34: The Customer Incident:
QUESTION 01
What is missing from this report?
QUESTION 03
Is this information sufficient to open and validate a support case?
QUESTION 02
What is your immediate next step?
Many of our industrial devices randomly become unreachable, causing loss of communication in
the automation system. Rebooting the units usually restores operation, but the issue keeps
coming back.
CONNECTION LOST, CUSTOMER HANG UP CALL THIS IS ALL THE INFORMATION YOU HAVE.
CASE ID: 2026-X77-TTS
Stop. You Have 5 minutes. Identify every gap using the Framework.