## Slide 1: Mastering NAT-108 - IP Twins Mapping Feature
Andreas Röser & Amjad Badar
March 2026
2026 MTSC
Field Application Engineer

## Slide 2: Learning Objectives
NAT-108 Product Knowledge
NAT introduction
NAT configuration
IP Twins Feature overview
IP Twins Feature of NAT-108
How to configure NAT & IP Twin Feature in NAT-108

## Slide 3: Agenda
NAT Series and Features
NAT-108 IP Twins Mapping Feature
NAT Selection
NAT Hands-on practice
  Tech Recap N-1 NAT / 1-1 NAT / Double NAT
  NAT Hands-on Task 1 (NAT Rules)
  NAT Hands-on Task 2 IP Twins Mapping

## Slide 4: Introducing NAT Series

## Slide 5: Why NAT Series
Market Trend
Top OT Challenges
110M+ additional IP connections driven by Industry 4.0 & AI expansion in manufacturing, making network structures more complex.
An increasing number of Machines, PLCs, and systems are transitioning from air-gapped isolation to centralized management.
Growing need for simplified OT network integration with minimal configuration changes.
Increasing demand for enhanced security features to protect connected industrial systems.
Network resource conflicts: Large-scale OT networks with multiple IP devices are prone to IP conflicts, disrupting connectivity and operations.
Operational efficiency: Same IP architecture systems need to be integrated or duplicated into the same network.
Security challenges: Exposing private IP addresses to external networks introduces significant cybersecurity risks, including unauthorized access and data breaches.
*Estimated based on the assumption that each $1M market growth adds 500 connected devices. Calculation: 2028 Total Demand (~192M) - 2023 Total Demand (~75M) = ~117M new connections.

## Slide 6
NAT Series: NAT-102 & NAT-108
NAT-102 Series (For single Connection)
User-friendly NAT functionality simplifies network integration
Hands-free network access control through automatic allowlisting of locally connected devices
Ultra-compact size and robust industrial design suitable for cabinet installation
Ideal for single connection scenarios: Centralized management of single production line communications
Switch
NAT-108 Series (For Multiple Connections)
User-friendly NAT functionality simplifies network integration
IP Twins Mapping remaps duplicate LAN IP addresses for conflict-free communication
Hands-free network access control through automatic allowlisting of locally connected devices
Ideal for multiple connection scenarios: Centralized management of multiple production line communications

## Slide 7: Recap NAT-102

## Slide 8: Recap: NAT-102
Complete NAT Functionality
Adapt your machines to specific network scenarios without complicated, costly, and time-consuming configurations.
Industrial Grade Design
-40 to 75°C wide temperature operation
Industrial certificates for EN50121-4, NEMA TS2 and ATEX / C1D2
Zero-config Network Access Control
Automatically learns the IP and MAC address of locally connected devices and binds them to the access list.
Auto Learning Lock
NAT
Firewall
20 mm
90 mm
73 mm
Ultra-compact Size
Allow the device to be easily installed into cabinets.
NAT-102
  -10 to 60oC, 2 x FE ports industrial NAT devices, 12/24/48 VDC input
NAT-102-T
  -40 to 75oC, 2 x FE ports industrial NAT devices, 12/24/48 VDC input

## Slide 9: NAT-102 Functionalities
NAT
Basic Functions
N to 1
1 to 1
PAT
Unique Functions
Double NAT
NAT Loopback
Security
Basic Functions
L3 Firewall
Account privilege & password policy
Login policy & Trust Access
Unique Functions
L2/L3 Port Security Auto Learning
NAT
Security

## Slide 10: NAT-108

## Slide 11: NAT-108
Complete NAT Functionality
Adapt your machines to specific network scenarios without complicated, costly, and time-consuming configurations.
NEW: NAT IP Twins Mapping remaps duplicate LAN IP addresses for conflict-free communication
Industrial Grade Design
-40 to 75°C wide temperature operation
Zero-config Network Access Control
Automatically learns the IP and MAC address of locally connected devices and binds them to the access list.
Auto Learning Lock
NAT
Firewall
36 mm
90 mm
73 mm
NAT-108
  -10 to 60oC, 8 x FE ports industrial NAT devices, 12/24/48 VDC input
NAT-108-T
  -40 to 75oC, 8 x FE ports industrial NAT devices, 12/24/48 VDC input
Ultra-compact Size
Allow the device to be easily installed into cabinets.

## Slide 12: NAT-108: Extending NAT-102 Functionalities
NAT
Basic Functions
N to 1
1 to 1
PAT
Unique Functions
IP Twins Mapping
Double NAT
NAT Loopback
Security
Basic Functions
L3 Firewall
Account privilege & password policy
Login policy & Trust Access
Unique Functions
L2/L3 Port Security Auto Learning
NAT
Security

## Slide 13: NAT-108 IP Twins Mapping

## Slide 14: IP Twins Mapping on NAT-108
Customer Pain Points:
In the factory automation industry, PLC machines often have the same default LAN IP, requiring hours for user configuration. This makes IP modifications time-consuming and labor-intensive.
The Solution without IP Twins Mapping:
To address this, users may need to deploy three separate NAT devices with 1-to-1 NAT translation, increasing maintenance complexity and costs.

## Slide 15: IP Twins Mapping on NAT-108
Reduce Costs and Improve Efficiency.
The Solution with IP Twins Mapping:
In factory automation scenarios, NAT-108 enables multiple PLC devices to connect to SCADA. Even if all devices share the same default LAN IP, IP Twins Mapping allows seamless communication between SCADA and PLCs while handling NAT translation.

## Slide 16: Limitations on IP Twins Mapping
IP Twin Mapping feature for NAT-108
  Not supported on NAT-102
No data transmissions between duplicate IP devices
  e.g., Production Line 2 & Production Line 3 device
Limited support of duplicate IP
  up to 3 devices with an identical LAN IP supported
Note:
  The maximum NAT rule limit remains at 128.

## Slide 17: How to choose NAT Series?

## Slide 18: Typical Application
NAT-Series
NAT-Series
Simplify the IP configuration of machines in existing network infrastructure in factory automation environments

## Slide 19: How to choose NAT Series?
 | NAT-102 | NAT-108 | NAT-108
Target Industry | Discrete Automation / Factory Automation |  | 
Field Scope | Ideal for small sites, single-station or existing network structure with switches. Cost-sensitive and simple network environments, offering basic NAT functionality for single-site conversion. |  | Suitable for multi-line factories and more complex network environments. Emphasizes flexibility to meet multi-device network architecture needs with support for IP Twins Mapping.
Application | Single Connection SCADA to PLC |  | Multiple Connections SCADA to Multi-PLCs, PLCs to PLCs

## Slide 20: NAT-108 Take-Away & Reason to choose
Next-level Network Address Translation
NAT-108 provides seamless network address translation, effectively managing OT networks by resolving complex connection challenges, such as IP conflicts, through its IP Twins Mapping feature.
Solidify OT Network Security
The NAT-108 helps protect critical infrastructure, enhances network reliability, and ensures secure and stable operations with the L3 firewall and Device Lockdown feature.
Empowers OT stability
The NAT-108 maximizes cabinet space, and reduces downtime and maintenance costs, ensuring consistent performance in harsh industrial conditions.
Key Benefits For users
Market-Leading Comprehensive NAT Solution
Robust Security Measures
Comprehensive Market-leading NAT Solution | Robust Security Measures | Reliable Compact Design for Harsh Environments

## Slide 21: Hands-on Recap Network Address Translation (NAT)

## Slide 22: NAT N-1
NAT Series
Internal External
192.168.127.154 192.168.128.254
Addresses @ 192.168.127.X are mapped to 192.168.128.254
192.168.127.x 192.168.128.1

## Slide 23: NAT N-1
Original addresses
Translated addresses
NAT N-1 mode
1
2
NAT
Internal External
192.168.127.X
192.168.128.100
1
2

## Slide 24: NAT 1-1
NAT Series
Internal External
Addresses @ 192.168.127.X are mapped to 192.168.128.X individually
192.168.127.1
192.168.127.2
192.168.128.100
192.168.128.200
192.168.128.1

## Slide 25: NAT 1-1
The translated address @ external network
The device address @ internal network
The External interface
NAT 1-1 mode
1
2
3
NAT
Internal External
192.168.127.1
192.168.128.100
1
2
3

## Slide 26: NAT 1-1: Double NAT
NAT Series
Internal External
Addresses @ 192.168.127.X are mapped to 192.168.128.X individually
192.168.127.1
(Default GW not available)
192.168.127.2
(Default GW not available)
192.168.128.100
192.168.128.200
192.168.128.1

## Slide 27: NAT 1-1: Double NAT
With Double NAT: Source will be replaced by NAT-102’s interface address
Without Double NAT: Source address will not be replaced
NAT Series
Internal External
192.168.127.254
192.168.128.1
192.168.127.1
Wireshark captures on Internal network

## Slide 28: NAT 1-1: Double NAT
Enable Double NAT

## Slide 29: NAT-108 Hands-On

## Slide 30: Test Topology
NAT-108
PC-1
Internal External
(LAN Port) (WAN Port)
192.168.127.254 192.168.128.254
PC-2
IP: 192.168.127.1/24
GW:192.168.127.254
IP: 192.168.128.1/24
EDS
IP: 192.168.127.2/24
GW=192.168.127.254
No Gateway on PC-1 allowed

## Slide 31: Task 1 : NAT Rules
Configure NAT-108
  Use Port 7 / 8 as external WAN
  Use 1-1 NAT IP @ External (WAN Port)
    192.168.128.100 to access PC-2
    Use 192.168.128.200 to access EDS
  Web Interface Access
    Ensure both PC can access NAT-108 configuration interface
  Ping NAT-108 WAN Interface (192.168.128.254)
    Ensure PC-1 can ping NAT-108
    No other WAN device shall ping NAT-108
  Configure NAT rules
Verify your configuration -> All tests should work
  NAT-108 Web Access
    PC-1 and PC-2 shall be able accessing NAT-108 web GUI
  Ping NAT-108 WAN Interface
    Can PC-1 ping 192.168.128.254?
  NAT Rules: Check:
    PC-1 can ping PC-2 / PC-1 can ping EDS
    PC-2 can ping PC-1 / PC-2 can ping EDS
    EDS can ping PC-1
Show results to your table coach before continue to Task 2
No Gateway on PC-1 allowed

## Slide 32: Task 2 : IP Twins
Configure NAT-108
  Use IP Twins Mapping to handle IP address duplication
    Ensure PC-1 can ping EDS and PC-2
Note following Steps:
  Important: Delete NAT rules from Task 1
  Use Port 7 / 8 as external WAN
  Check LAN Interface Configuration
    Keep original LAN Interface
    Need different VLAN ID for the different devices
    Both VLAN ID shall come with same Network IP ( create new Network interfaces)
  Check Interface Configuration
    May need to configure “Secondary IP” configuration
    Use following WAN Interface IP to access the LAN devices:
      192.168.128.100 to access PC-2
      Use 192.168.128.200 to access EDS
  Create NAT rules
Show results to your table coach
No Gateway on PC-1 allowed